## Slide 1: Discussion on Frame Structure for Future WLAN Systems with OFDMA
Date: 2014-10-31
Authors:

## Slide 2: Abstract
This contribution discusses on frame structure of OFDMA in HEW to enhance the efficiency of WLAN systems.

## Slide 3: OFDMA in HEW
OFDMA is crucial technology for high efficient WLAN
802.11ax has considered OFDMA for efficient use of spectrum resources and spectral frequency reuse.
In order to serve users having different link quality, the following TXVECTOR parameters should be considered as user-specific values
  MCS: indicates the modulation and coding scheme
  NUM_STS: indicates the number of space-time streams
  STBC: indicates whether STBC is used
  FEC_CODING: indicates which FEC encoding is used
How to determine user-specific values?

## Slide 4: UL MU Transmission in HEW
802.11ax has discussed UL MU transmission and issues to support UL MU transmission.
Issue on synchronization for UL MU transmission
  Time synchronization
  Frequency synchronization
  Power synchronization
Solution(s) for synchronization in UL MU transmission
  Longer CP size
  Adjustment procedure for synchronization
  UL MU only for STAs who are sufficiently synchronized
Another solution with OFDMA?

## Slide 5: Frame Structure Example to Solve Previous Mentioned Problems
Proposed frame structure with OFDMA
  - To assign control channel which is separated from data subchannels
Subcarrier logical number
OFDMA symbol number
Control subchannel
Data subchannel
Data subchannel
Data subchannel

## Slide 6: Conclusion
We discussed frame structure of OFDMA to enhance efficiency in HEW.
In order to serve users having different link quality and support UL MU transmission, we need to discuss frame structure of OFDMA.
We introduced a example of OFDMA frame structure.

## Slide 7: References
[1] IEEE 802.11-13/1382r0 , "Discussion on OFDMA in HEW"
[2] IEEE 802.11-14/1210r1 , "HEW PPDU Format for Supporting MIMO-OFDMA"
[3] IEEE 802.11-13/1388r1, "Uplink Multi-User Transmission“
[4] IEEE 802.11-14/0802r0, "Consideration on UL MU Transmission“