## Slide 1
Multi-Carrier Training Field for OFDM Transmission in 802.11aj (45GHz)
Authors/contributors:
Date: 2014-11-5
Presenter: Haiming Wang

## Slide 2
Introduction
Multi-Carrier Training Fields (MCTF) is applied for channel estimation in IEEE 802.11aj OFDM transmission.
This presentation focuses on the OFDM-MCTF in OFDM transmission.
Notes: 2

## Slide 3
MCTF
Considering the situation of IEEE 802.11aj, there are two objectives for the design of MCTF.
    Low PAPR of the OFDM signals
    Binary sequence for MCTF
Notes: 3

## Slide 4
MCTF
All the points of the MCTF are set to the same amplitude with different phase. The MCTF can be represented by
where is the index of the subcarriers, and indicates the subcarrier’s
value.
As each frequency point obtains the same power, the selection of phase will not affect the performance of channel estimation.
A sequence with low PAPR is proposed to design.
Notes: 4

## Slide 5
PAPR
In the OFDM system with N subcarriers , the PAPR of the transmitted signal is defined as
where denotes the excepted value operation， is the time domain signal of .
The MCTF is designed by using cross entropy algorithm.
The cross entropy method iteratively optimizes the parameters of the probability distribution to produce a random variable solution in the neighborhood of the global optimal solution by minimizing cross entropy between the associated distribution and the optimal importance sampling distribution.
where denotes the excepted value operation， denotes the IFFT transform.
Notes: 5

## Slide 6
MCTF based on cross entropy
The figure shows the lowest PAPR of random sequences for 256 length and training sequences for 256 length in one hundred training iterations. The value of the PAPR for 256-MCTF converged at 70 times.
Notes: 6

## Slide 7
MCTF based on cross entropy
The 256-MCTF including DC carriers & Null carriers

## Slide 8
MCTF based on CE
The figure shows the lowest PAPR of random sequences for 512 length and training sequences for 512 length in one hundred training iterations. The value of the PAPR for 512-MCTF converged at 80 times.
Notes: 8

## Slide 9
MCTF based on CE
The 512-MCTF including DC carriers & Null carriers

## Slide 10
MCTF based on CE
The MCTF of 512 length obtains PAPR for 3.5 dB the same as the VHT-LTF of 64 length.
NOTE: The sequences calculated including DC carriers and null carriers.
Training Field | PAPR |  |  | 
 | Length of 64 | Length of 128 | Length of 256 | Length of 512
11ac VHT-LTF | 3.5 dB | 5.7 dB | 8.6 dB | 11.6 dB
11aj MCTF | - | - | 3.2 dB | 3.6 dB
The comparison of PAPR between 11aj MCTF and 11ac VHT-VTF

## Slide 11
Conclusion
The proposed MCTF achieves a PAPR of 3.2 dB for the DFT length of 256 and 3.5 dB for the DFT length of 512.
The proposed MCTF sequence is a binary sequence.
Notes: 11

## Slide 12: Appendix

## Slide 13
Simulation Setup
Channel model: IEEE 802.11aj(45 GHz), Conference Scenario
Number of distinguishable paths : 18
Packet length: 4096 bytes
LDPC codeword length: 672bits
Number of channel realizations: 2000
Simulation antennas: 4x4 for 1,2,3,4ss, 2x2 for 1,2ss, 1x1 respectively
Modulation and code rate: {QPSK ½}
Channel estimation: LS with DFT correction
Spatial Extension Matrix:
Notes: 13

## Slide 14
PER Performance
Antenna: 4x4; Modulation: QPSK; Stream: 4;
Channel Estimation: LS estimation with correction;
The gap is 1.5 dB.
Notes: 14

## Slide 15
PER Performance
Antenna: 4x4; Modulation: QPSK; Stream: 3;
Channel Estimation: LS estimation with correction
The gap is 1.5 dB.
Notes: 15

## Slide 16
PER Performance
Antenna: 4x4; Modulation: QPSK; Stream: 2;
Channel Estimation: LS estimation with correction.
The gap is 1.5 dB.
Notes: 16

## Slide 17
PER Performance
Antenna: 4x4; Modulation: QPSK; Stream: 1;
Channel Estimation: LS estimation with correction;
The gap is 2 dB.
Notes: 17

## Slide 18
PER Performance
Antenna: 2x2; Modulation: QPSK; Streams 2;
Channel Estimation: LS estimation with correction;
The gap is 1.25 dB.
Notes: 18

## Slide 19
PER Performance
Antenna:1x1; Modulation: QPSK; Stream: 1;
Channel Estimation: LS estimation with correction
The gap is 1.25 dB.
Notes: 19

## Slide 20
MSE Performance of Channel Estimation
Antenna: 1x1;
Stream: 1;
Channel Estimation: LS estimation with correction
Notes: 20

## Slide 21
Q & A
The gap of the PER curve of ideal and estimated channel is actual?
  The gap is similar in some other simulations.
  The next two figure contrast the PER gap of ideal and estimated channel between IEEE 802.11n and IEEE 802.11aj with MCTF.
Notes: 21

## Slide 22
Q & A
  Reference：Hoefel, R. P. F. (2012). IEEE 802.11n: On Performance of Channel Estimation Schemes over OFDM MIMO Spatially-Correlated Frequency Selective Fading TGn Channels. In XXX Brazilian Symposium on Telecommunications.
  This figure indicated that the PER gap of ideal and LS estimated channel is about 3 dB in such simulation setup: Simulation antennas:1x1, Modulation:16QAM.
Notes: 22

## Slide 23
Q & A
  The corresponding simulation results of MCTF in IEEE 802.11aj in such simulation setup: Antenna:1x1, Modulation: 16QAM.
  This figure indicates that the PER gap of ideal and estimated channel is about 1.2dB. The enhancement of the performance is because of the LS estimation with DFT correction.
Notes: 23

## Slide 24
Thanks for Your Attention!
Notes: 24