## Slide 1: HEW PPDU Transmission Discussion
Date: 2014-11-02
Authors:

## Slide 2: Potential Technologies for High Efficiency WLAN
MU-MIMO and OFDMA are the promising technologies for enhancing an user experience and improving a system performance by serving the heterogeneous users simultaneously
But, in order to sustain a gain of MU-MIMO and OFDMA, the efficient PHY and MAC protocol design [1][2] is very important
This document discusses the protocol design issues for supporting MU-MIMO and OFDMA in IEEE 802.11ax

## Slide 3: Legacy (802.11n/ac) PPDU Transmission
Single-User (SU) PPDU transmission
  A STA shall not transmit to a second STA using a bandwidth (TXVECTOR parameter CH_BANDWIDTH) that is not indicated as supported in the Supported Channel Width Set subfield in the HT/VHT Capabilities element from the second STA
Multi-User (MU) MIMO PPDU transmission
  Additionally, a bandwidth of all MPDUs contained in a MU-MIMO PPDU transmitted from an AP is same

## Slide 4: HEW PPDU Transmission for SU PPDU
Single-User HEW PPDU: A HEW STA should follow the same rule defined in legacy BSS Operation rule
  Single-User PPDU transmission: A HEW STA shall not transmit to a second STA using a bandwidth (TXVECTOR parameter CH_BANDWIDTH) that is not indicated as supported in the Supported Channel Width Set subfield in the HT/VHT/HEW Capabilities element from the second STA

## Slide 5: HEW PPDU Transmission for MU-MIMO (Option1)
MU-MIMO HEW PPDU: A bandwidth of all MPDUs contained in a Downlink/Uplink MU-MIMO PPDU is same
  Pros: Simply follow the design philosophy of 802.11ac Downlink MU-MIMO. Low implementation complexity
  Cons: Inflexible multi-user grouping
Uplink MU-MIMO Poll
(AP to STA1, STA2)
Uplink MU-MIMO Block ACK
(AP to STA1, STA2)
HE Preamble
Uplink MU-MIMO DATA
(STA1 to AP)
40MHz
40MHz
40MHz
Time
AP
STA1, STA2
HE Preamble
HE Preamble
Uplink MU-MIMO DATA
(STA2 to AP)
40MHz
HE Preamble
SIFS
SIFS

## Slide 6: HEW PPDU Transmission for MU-MIMO (Option2)
MU-MIMO HEW PPDU: A bandwidth of MPDUs contained in a Downlink/Uplink MU-MIMO PPDU can be different each other
  Pros: Flexible multi-user grouping with various operating bandwidth users
  Cons: More implementation and protocol design complexity. For example, the pilot tone location of MU-MIMO PPDUs should be the same
Time
Uplink MU-MIMO Poll
(AP to STA1, STA2)
Uplink MU-MIMO Block ACK
(AP to STA1, STA2)
HE Preamble
Uplink MU-MIMO DATA
(STA1 to AP)
40MHz
40MHz
AP
STA1, STA2
HE Preamble
HE Preamble
Uplink MU-MIMO DATA
(STA2 to AP)
40MHz
HE Preamble
SIFS
SIFS
20MHz

## Slide 7: HEW PPDU Transmission for OFDMA
OFDMA HEW PPDU: The principle of OFDMA is that an occupied bandwidth for a single user is a partial bandwidth of a full bandwidth for an OFDMA HEW PPDU
While STAs might be mandated to have 80MHz capability (as in IEEE 802.11ac), for sake of power saving, the STAs could switch to narrower bandwidth (e.g., using Operating Mode Notification element)
  HEW PPDU format should consider the issue for supporting OFDMA with various operating bandwidth users

## Slide 8: HEW PPDU Transmission for OFDMA (Option1)
MPDUs contained in OFDMA HEW PPDU shall not be addressed to users operated in a narrower bandwidth than a bandwidth of OFDMA HEW PPDU
  Pros: Flexible protocol design but it is not a significant gain
  Cons: In order to sustain a gain of OFDMA, STAs should not switch narrower bandwidth. It is not helpful to reduce the energy consumption.

## Slide 9: HEW PPDU Transmission for OFDMA (Option1)
For the below OFDMA HEW PPDU transmission, STA1, STA2, STA3, STA4 and STA5 shall operate in greater than or equal to 40 MHz operating bandwidth
AP to STA1 (5MHz)
AP to STA2 (5MHz)
AP to STA3 (5MHz)
AP to STA4 (5MHz)
AP to STA5 (20MHz)
OFDMA HEW PPDU
AIFA
PIFS
Primary 20MHz Channel
Secondary 20MHz Channel
with TXVECTOR parameter CH_BANDWIDTH equal to CBW40
Receive Bandwidth for
STA1, 2, 3, 4, 5

## Slide 10: HEW PPDU Transmission for OFDMA (Option2)
MPDUs contained in OFDMA HEW PPDU can be addressed to users operated in a narrower bandwidth than a bandwidth of OFDMA HEW PPDU, wherein each sub-channels of OFDMA HEW PPDU have to be assigned within the operating bandwidth of each users
  Pros: OFDMA HEW PPDU can be destined to any STA regardless of its operating bandwidth. It is helpful to sustain a gain of OFDMA and improve an energy consumption
  Cons: Little complexity of user scheduling on AP side

## Slide 11: HEW PPDU Transmission for OFDMA (Option2)
For the below OFDMA HEW PPDU transmission, STA1, STA2, STA3, STA4 can operate in 20MHz operating bandwidth
AP to STA1 (5MHz)
AP to STA2 (5MHz)
AP to STA3 (5MHz)
AP to STA4 (5MHz)
AP to STA5 (20MHz)
AIFS
PIFS
Primary 20MHz Channel
Secondary 20MHz Channel
OFDMA HEW PPDU
with TXVECTOR parameter CH_BANDWIDTH equal to CBW40
Receive Bandwidth for
STA5
Receive Bandwidth for
STA1, 2, 3, 4

## Slide 12: Conclusion
It seems that previous discussions in IEEE 802.11ax are favoring on the enhanced MU-MIMO and OFDMA technologies
But, in order to fully utilize the MU-MIMO and OFDMA technical advantage, the HEW PPDU protocol design should consider heterogeneous users operated in the different operating mode

## Slide 13: References
[1] https://mentor.ieee.org/802.11/dcn/14/11-14-1210-01-00ax-hew-ppdu-format-for-supporting-mimo-ofdma.pptx
[2] https://mentor.ieee.org/802.11/dcn/14/11-14-1211-00-00ax-ack-procedure-for-ofdma.pptx