## Slide 1
Efficient Wider Bandwidth Operation in IEEE 802.11ax
Date: 2014-11-04
Authors:

## Slide 2: Background
802.11 ac Wideband Operation
  802.11 ac based wideband operation supports 20MHz, 40MHz, 80MHz, 160MHz transmission for single user
  AP expands its channel from primary channel, but it is only allowed to expand to predetermined adjacent channel
  If one of the 20MHz channel in secondary channel is busy, AP cannot use other idle channels in secondary channel
802.11 ax PAR document
  Make more efficient use of spectrum resources in scenarios with a high density of STAs per BSS[1]
More Efficient use pattern of spectrum resources should be discussed

## Slide 3: Prior Works on Wider Bandwidth Operation
Legacy channel access can not utilize resource fully

## Slide 4: Prior Works on Wider Bandwidth Operation
Allowing to use all available Channel with PIFS sensing could enhance channel utilization[2]

## Slide 5: Prior Works on Wider Bandwidth Operation
Examples for 80MHz (4 Channels)[2]
  CH1 is primary Channel
 | Channel (Colored means busy) |  |  |  | Resource utilization |  |  |  |  |  |  | 
 | CH1 | CH2 | CH3 | CH4 | Legacy Operation |  |  |  | Using All Available CH |  |  | 
Case1 |  |  |  | busy |  |  |  |  |  |  |  | 
Case2 |  |  | busy |  |  |  |  |  |  |  |  | 
Case3 |  | busy |  |  |  |  |  |  |  |  |  | 
Case4 |  | busy |  | busy |  |  |  |  |  |  |  | 
Case5 |  |  | busy | busy |  |  |  |  |  |  |  | 
Case6 | busy |  |  |  |  |  |  |  |  |  |  | 

## Slide 6: Prior Works on Wider Bandwidth Operation
Previous contributions using new patterns of wider bandwidth provides the enhanced efficiency of wireless LAN system
But there were not enough discussions about HOW to expand and adopt new patterns of channel use
Using all available CHs with PIFS sensing on secondary channels could make more contentions and interferences in dense OBSS scenario[3]
  Fairness need to be considered

## Slide 7: Alternative Primary Channel based Access Method
Adding to Primary Channel based wideband expansion, adopting other secondary channel based wideband expansion could enhance efficient use of spectrum resources
Alternative Primary Channel(APCH) is the basis channel of new wideband expansion
Channel expansion rule on each primary channel can be the same as conventional 802.11ac rule
It allows non-contiguous channel use and new channel use patterns
  eg. Contiguous 60MHz channel, non-contiguous 80MHz channel, etc.

## Slide 8: Alternative Primary Channel based Access Method
Legacy Pattern Case
Alternative Primary Channel Case

## Slide 9: Alternative Primary Channel based Access Method
Alternative Primary Channel Expansion Rule
  Only with Primary Channel
    Sustain primary channel based transmission
    Alternative primary channel as a new start point of channel expansion is only applicable with primary channel-based access
  Allowing transmission without Primary Channel
    Although primary channel is busy, alternative primary channel could replace primary channel
    New back-off rule need to be considered for alternative primary channel

## Slide 10: Alternative Primary Channel based Access Method
Only with Primary Channel
Allowing transmission without Primary Channel

## Slide 11: Alternative Primary Channel based Access Method
Resource utilization of APCH
  CH1 is primary Channel
  CH3 is APCH
 | Channel (Colored means busy) |  |  |  | Resource utilization |  |  |  |  |  |  |  |  |  |  | 
 | CH1 | CH2 | CH3 | CH4 | Legacy |  |  |  | APCH w/ Primary |  |  |  | APCH w/o Primary |  |  | 
Case1 |  |  |  | Busy |  |  |  |  |  |  |  |  |  |  |  | 
Case2 |  |  | Busy |  |  |  |  |  |  |  |  |  |  |  |  | 
Case3 |  | Busy |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Case4 |  | Busy |  | Busy |  |  |  |  |  |  |  |  |  |  |  | 
Case5 |  |  | Busy | Busy |  |  |  |  |  |  |  |  |  |  |  | 
Case6 | Busy |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 12: Analysis (Assumptions)
Calculate average bandwidth of APCH case
    Contention on Primary channel and APCH access is modeled as a Access probability
    Each secondary channel has busy probability of for PIFS duration
    Sub-band(<20MHz) contention and access is not considered
    Maximum Channel bandwidth is 160MHz
      Based on 802.11ac
    Assume APCH is located on secondary 80MHz
    Channel expansion rule is identical for each Primary channel and APCH
      20MHz->40MHz->80MHz->160MHz
    Primary channel based bandwidth expansion has a priority
    New patterns of using channel for same bandwidth

## Slide 13: Analysis (Example: Legacy vs. APCH)
Legacy Pattern of using 80MHz
APCH Pattern of using 80MHz

## Slide 14: Analysis (Parameters)
is bandwidth of downlink transmission
is number of channels AP use
is number of secondary channels AP use
is busy probability of each secondary channel with PIFS duration
AP can access primary channel or APCH with probability
  Back-off method and channel condition have influence on

## Slide 15: Analysis
Equation for Legacy
Using all available channel case
  All the available 20MHz channel could be used
  PIFS sensing for other 7 channels which has of busy probability

## Slide 16: Analysis
Equation for using APCH case
  Different pattern of Channel use
APCH only with Primary Channel case
APCH without Primary Channel case

## Slide 17: Analysis
Channel usage vs busy channel prob. (=0.7)
54%
39%
90%
52%
99%
39%

## Slide 18: Conclusion
Alternative Primary Channel would increase Channel Usage
Alternative Primary Channel would sustain legacy channel expansion rule, and APCH would contend with other Primary Channel also
APCH based transmission without Primary Channel has much more gain
APCH based wider bandwidth operation might control OBSS fairness on wider bandwidth operation
We need to discuss about specific wider bandwidth channel expansion method on 802.11ax

## Slide 19: Reference
[1] IEEE 802.11-14/0165r1 “802.11 HEW SG Proposed PAR”
[2] IEEE 802.11-13/1058r0 “Efficient Wider Bandwidth Operation”
[3] IEEE 802.11-13/0839r1 “Discussion on OFDMA in IEEE 802.11ax”