## Slide 1: MAC Calibration Results
Date: 2014-11-04
Authors:
Name | Affiliations | Address | Phone | email
Vida Ferdowsi Reza Hedayat Young Hoon Kwon Yongho Seok Hyongjin Kwon | NEWRACOM | 9008 Research Drive, Irvine, CA 92618 |  | vida.ferdowsi at newracom.com reza.hedayat at newracom.com younghoon.kwon at newracom.com yongho.seok at newracom.com hj.kwon at newracom.com
Vida Ferdowsi, NEWRACOM

## Slide 2: Summary
This document reports calibration results for MAC SLS [1]
We report results for the calibrations tests:
  MAC overhead: tests 1a/1b (without/with RTS/CTS)
  Deferral: tests 2a/2b (without/with hidden nodes)
  NAV deferral: test 3
We confirm the reported results match other reported results, and for ease of following we report along the comparison tables of [2]
[1] 11-14-980-04-00ax-simulation-scenarios
[2] 11-14-1192-03-00ax-comparing-mac-calibration-results

## Slide 3: Test 1a: MAC overhead without RTS/CTS
Simulation parameters: long GI, 20MHz, AMPDU of 2 MPDUs, MCS0 & MCS8, CWmin=15, PER=0, MSDU length=500/100/1500/2000B, RTS/CTS off.
Configurations | MCS0 (6.5Mbps) |  |  |  | MCS8 (78Mbps) |  |  | 
 | 500 | 1000 | 1500 | 2000 | 500 | 1000 | 1500 | 2000
Huawei | 4.79 | 5.55 | 5.84 | 6.00 | 21.98 | 34.91 | 43.24 | 48.67
LGE | 4.81 | 5.55 | 5.84 | 5.99 | 22.4 | 35.2 | 43.25 | 48.9
Qualcomm | 4.76 | 5.53 | 5.82 | 5.98 | 23.92 | 37.25 | 45.55 | 50.81
MediaTek | 4.76 | 5.53 | 5.82 | 5.98 | 21.71 | 34.65 | 42.71 | 48.15
Intel | 4.76 | 5.53 | 5.82 | 5.98 | 21.53 | 34.46 | 42.58 | 48.14
Ericsson | 4.75 | 5.52 | 5.82 | 5.97 | 21.53 | 34.47 | 42.57 | 48.09
Nokia | 4.76 | 5.52 | 5.83 | 5.97 | 21.19 | 34.22 | 41.93 | 47.74
NTT | 4.79 | 5.54 | 5.84 | 6.00 | 22.00 | 35.00 | 43.20 | 48.40
Newracom | 4.85 | 5.55 | 5.84 | 5.99 | 23.8 | 36.64 | 43.87 | 49.73

## Slide 4: Test 1b: Test 1a: MAC overhead with RTS/CTS
Simulation parameters: long GI, 20MHz, AMPDU of 2 MPDUs, MCS0 & MCS8, CWmin=15, PER=0, MSDU length=500/100/1500/2000B, RTS/CTS on.
Configurations | MCS0 (6.5Mbps) |  |  |  | MCS8 (78Mbps) |  |  | 
 | 500 | 1000 | 1500 | 2000 | 500 | 1000 | 1500 | 2000
Huawei | 4.42 | 5.31 | 5.66 | 5.85 | 15.94 | 27.07 | 34.97 | 40.61
LGE | 4.45 | 5.31 | 5.66 | 5.86 | 16.2 | 27.3 | 35 | 40.8
Qualcomm | 4.4 | 5.29 | 5.64 | 5.84 | 18.64 | 30.75 | 38.94 | 44.51
MediaTek | 4.40 | 5.29 | 5.64 | 5.84 | 15.79 | 26.90 | 34.62 | 40.24
Intel | 4.4 | 5.29 | 5.64 | 5.84 | 15.7 | 26.8 | 34.55 | 40.26
Nokia | 4.40 | 5.28 | 5.64 | 5.83 | 15.52 | 26.66 | 34.12 | 39.96
NTT | 4.42 | 5.30 | 5.67 | 5.85 | 16.00 | 27.10 | 34.97 | 40.40
Newracom | 4.43 | 5.27 | 5.62 | 5.82 | 16.29 | 27.06 | 34.50 | 39.99

## Slide 5: Test 2a: Deferral test without hidden node
Simulation parameters: long GI, 20MHz, AMPDU of 2 MPDUs, MCS0, CWmin=15, PER=0, MSDU length=500/100/1500/2000B, RTS/CTS on/off.
Configurations | Without RTS/CTS |  |  |  | With RTS/CTS |  |  | 
 | 500 | 1000 | 1500 | 2000 | 500 | 1000 | 1500 | 2000
Huawei | 4.56 | 5.25 | 5.51 | 5.66 | 4.46 | 5.33 | 5.68 | 5.87
LGE | 4.62 | 5.28 | 5.54 | 5.66 | 4.5 | 5.34 | 5.68 | 5.88
Qualcomm | 4.57 | 5.26 | 5.53 | 5.67 | 4.45 | 5.32 | 5.67 | 5.86
MediaTek | 4.71 | 5.48 | 5.78 | 5.94 | 4.35 | 5.24 | 5.62 | 5.81
Intel | 4.52 | 5.22 | 5.48 | 5.62 | 4.44 | 5.31 | 5.67 | 5.86
Ericsson | 4.53 | 5.21 | 5.48 | 5.63 |  |  |  | 
Nokia | 4.58 | 5.29 | 5.56 | 5.71 | 4.48 | 5.32 | 5.67 | 5.85
NTT | 4.58 | 5.25 | 5.45 | 5.66 | 4.49 | 5.35 | 5.70 | 5.88
Newracom | 4.80 | 5.49 | 5.77 | 5.93 | 4.39 | 5.22 | 5.57 | 5.77

## Slide 6: Test 2b: Deferral test with hidden node
Simulation parameters: long GI, 20MHz, AMPDU of 2 MPDUs, MCS0, CWmin=15, PER=0, MSDU length=1500B, RTS/CTS off.
Scenarios | Huawei | LGE | Qualcomm | MediaTek | Intel | Nokia | NTT | Newracom
test2b-noRTS-noFA-MCS0 | 1.62 | 1.7 |  |  |  |  |  | 
test2b-noRTS-FA-MCS0 | 1.01 | 1.02 | 0.98 | 0.03631 | 1.008 | 1.20 | 1.06 | 1.03
test2b-noRTS-noFA-MCS8 | 26.54 | 26.8 |  |  |  |  |  | 
test2b-noRTS-FA-MCS8 | 34.75 | 35.0 |  |  |  | 35.66 |  | 34.21

## Slide 7: Test 3: NAV deferral
Simulation parameters: long GI, 20MHz, AMPDU of 2 MPDUs, MCS0 & MCS8, CWmin=15, PER=0, MSDU length=1500B, RTS/CTS on.
Scenarios | Huawei | LGE | Qualcomm | MediaTek | Intel | Nokia | NTT | Newracom
test3-RTS-noFA-MCS0 | 5.15 | 5.14 |  |  |  |  |  | 
test3-RTS-FA-MCS0 | 5.58 | 5.58 | 5.55 | 5.63933 | 5.66 | 5.59 | 5.40 | 5.78
test3-RTS-noFA-MCS8 | 22.04 | 22.4 |  |  |  |  |  | 
test3-RTS-FA-MCS8 | 34.05 | 34.2 |  |  |  | 31.35 |  | 34.24