## Slide 1: Next Generation Positioning Overview and Challenges
Authors:
Name | Affiliation | Address | Phone | Email
Jonathan Segev | Intel |  | +972-54-2403587 | jonathan.segev@intel.com
Brian Hart | Cisco |  |  | brianh@cisco.com
Naveen Kakani | CSR |  |  | naveen.kakani@csr.com

## Slide 2: Motivation and purpose
In previous contributions several useful usage models that are of commercial use for positioning have been presented.
This contribution presents some of the challenges in enabling this set of usages for 802.11 based positioning and an overview of positioning techniques.

## Slide 3: Why 802.11 Based Positioning?
Positioning has symbiotic relation with data connectivity:
  Positioning means nothing without contextual information.
  Data connectivity improves with the addition of positioning.
802.11 based WLAN is almost ubiquitous in many indoor environments (malls, retail chains).
Building on existing technology enables reuse:
  Many of the use cases revolve around the smartphone (already packed with radios, reuse keeps complexity of actual device in check).
  Reuse of connectivity technology shortens and simplifies technology development.
Symbiotic relationship between data and
positioning services
Notes:   Less is more => unite 2 slides.
  Making development effort easier.
  time to market shorter which provide an opportunity for cost efficient strong penetration real world products.
  Using existing connectivity technology also promotes interoperability as it uses existing SDOs and ITOs.
  the Swiss army knife of modern days – the smartphone,
  Vendor reluctant to add radios.

## Slide 4: What is 802.11 Based Positioning?
Indoor positioning major approaches:
  Fingerprinting – a unique characteristic of the radio signal(s). Example: identify a position based on a set of RSSIs associated with APs.
  Geometrical – a mathematical model of the signal propagation properties is created. A device uses this model to trilaterate/multilaterate/triangulate its position using measurements to derive its position.
Notes:   Making development effort easier.
  time to market shorter which provide an opportunity for cost efficient strong penetration real world products.
  Using existing connectivity technology also promotes interoperability as it uses existing SDOs and ITOs.
  the Swiss army knife of modern days – the smartphone,
  Vendor reluctant to add radios.

## Slide 5: Positioning approaches - Fingerprinting
  A survey of the site is performed and “fingerprint” of the signals properties are taken; alternatively crowd sourcing might be used.
  Example: A device takes measurements and sends it to server. The server performs pattern matching trying to find the best matched position.

## Slide 6: Positioning approaches – Fingerprinting
  Essentially any positioning technique can be used with fingerprinting, however RSSI fingerprinting variant is most suited (Rx only, AP scan already part of API).
  Accuracy improves as range to AP reduces.
RSSI example: | 
Pro’s | Con’s
Simple to implement. | Sensitive to noise and channel variations.
Easy to crowd source. | Less dynamic.
No need for a known AP location | Not well suited for proximity usages.
Minimal/no impact on medium usage. | Changes in the environment requires many DB updates.
Geopriv is easy to achieve with downlink RSSI fingerprinting. | Dependent on constant device Tx PWR.
 | Exposed to replay attack.

## Slide 7: Positioning approaches - Geometrical
  A mathematical model of the signal propagation properties is created.
  A device uses this model to trilaterate (for example) its position based on measurements to derive its current position.
  Some examples: FTM (trilateration), RSSI (trilateration or multilateration), AoA/AoD (triangulation).

## Slide 8: Positioning approaches – Geometrical
FTM example: | 
Pro’s | Con’s
Overcomes the need for a site survey. | AP location has to be known.
Fewer updates to AP DB needed | The mathematical model of the signal propagation is not always accurate/optimized.
Suited to proximity usages | Hindered by NLOS (Non Line Of Sight) or NNLOS (Near NLOS) channel conditions giving a wrong sense of range.
Measurements have low variance (less susceptible to noise). | An accurate measurement is essential, 1nsec inaccuracy translates to 0.3m.

## Slide 9: Evolution of 802.11 Based Positioning
RSSI
~5-10m
Time Of Departure ~3-5m
Fine timing measurement 1-2m
Next Generation …
Notes:   Making development effort easier.
  time to market shorter which provide an opportunity for cost efficient strong penetration real world products.
  Using existing connectivity technology also promotes interoperability as it uses existing SDOs and ITOs.
  the Swiss army knife of modern days – the smartphone,
  Vendor reluctant to add radios.

## Slide 10: REVmc Positioning Support – Fine Timing Measurement
  An accurate measurement is essential as measurement error of 1nsec translates to 0.3m range error.
  Highly hindered by NLOS (Non Line Of Sight) or NNLOS (Near NLOS) channel conditions giving a wrong sense of range.
  The NLOS negative effect can be subsided using a Multiple Signal Classification algorithm (MUSIC).

## Slide 11: REVmc Location Support
Main items addressed by FTM introduction to REVmc:
  1:N operation - AP STA: non AP STA is the lead usage model.
  Multi channel operation: AP STAs have a fixed operating channel while non AP STA moves between AP STA’s channels.
  unassociated operation mode, as multiple ranges are required to obtain a single fix.
  Support for AP Location DB protocol.
Notes: 1:N operation - AP STA: non AP STA lead usage model.
AP STA has limited resources which it requires to manage and control.
Non AP STA has limited computation resources.
    Multi channel operation: Non AP STA has other outstanding PHY and MAC level activities of possibly higher priority.
  Non associated operation mode:

## Slide 12: What’s next then?
  In previous* contributions we’ve seen a set of new usage models of commercial value:
    Micro geo-fencing moving from <1m to <0.1m.
    Direction finding.
    Improving scalability and reducing overhead.
  * 11-14-1193/01 – Beyond Indoor Navigation by Jonathan Segev, Carlos Aldana et-al
  11-14-1235/r0 – Scalable Location by Brian Hart, Peter Thornycroft and Mark Rison.
  11-14-1263/r0 – Direction Finding Positioning by James Wang, Gabor Bajko et-al
    High Accuracy Positioning
    Enable the use of FTM <1 GHz frequency bands

## Slide 13: Improved accuracy – moving from <1m to <0.1m
  Problem definition:
  1st generation products are focused on indoor navigation but as technology adoption increases so does the demand for performance.
  Micro location becomes of interest, ~0.1m accuracy opens up a new set of usage models:
    Micro geo-fencing at store entrance.
    Guide me to product on the exact shelf.
    Identify user preference and offer useful valuable service.

## Slide 14: Direction finding
Problem definition:
  People visiting a museum/store would like to:
    Get guidance on exhibits in an exhibition, to articles on a high shelf.
    Articles may not be accessible but there’s a LoS between user and article.
  A manager in a store would like to:
    Provided additional information to clients as they enter the store.

## Slide 15
Improving scalability and reducing overhead
Problem definition:
  People would like to get directions to their seat in the stadium, or their gate at an airport.
  Current protocol requires ~6 frames per fix, per STA, possibly using basic rate (limited link adaptation, trilateration).
  Some work have to assess* medium usage using FTM has been done.
  Heavily crowded scenarios show substantial** impact on medium usage with FTM.
  * 11-12-1249-04-000m-802-11-2012-cid-46-47-48 by Carlos Aldana et-al.
  ** 11-13-0072-01-000m-client-positioning-using-timing-measurements-between-access-points by Erik Lindskog, Naveen Kakani et-al.

## Slide 16: High Accuracy Positioning
Problem definition:
  I’d like to play augmented reality on my gaming machine possibly connected to my WLAN.
  Possibly wearing special glass with sensors on my wearable devices.
  Centimeter accuracy required for new age user experience.
  LOS environment usage scenario is possible.

## Slide 17: Enable the use of FTM <1 GHz frequency bands
Example of usage and benefits of FTM in Sub 1 GHz WLAN:
  Reduce cost of operation when logging Sub 1 GHz enabled smart meter installation locations*
  Smart meters can do trilateration/triangulation with Access Points to have automated location logging and avoid human errors.
  Use of Sub 1 GHz enabled tags can be used both for indoor and outdoor locationing
    Track family members.
*15-14-0391-00-004r-technical-guidance-document-input-for-ami.pptx

## Slide 18: Challenges of using 802.11 Based Positioning - moving from <1m to <0.1m
Calculate range
The local timing function in 802.11 is accurate to within ±20ppm (phy dependent).
How does this effect the RTD measurement?
  Measurement frame of ~100usec
  SIFS ~16usec
  ACK frame ~70usec
AP
STA
FTM measurement frame
M1
ACK
M2 (t4, t1)
t4 = TOA (ACK)
t3 = TOD(ACK)
t1 = TOD(M1)
t2 = TOA(M1)
ACK

## Slide 19: Challenges of using 802.11 Based Positioning - moving from <1m to <0.1m
  Measurement frame of ~100usec
  SIFS ~16usec
  ACK frame ~70usec
  Diagram below describes events at the antenna ports.
T
FTM Meas. Frame M1
FTM Meas. Frame M1
ACK frame
ACK frame
t1-t2
t4-t3
SIFS
RTD = (t4-t1)-(t3-t2)
Both AP & STA local CLKS are used in the RTD meas.
t1
t2
t3
t4
Initiating STA
Responding STA

## Slide 20: Challenges of using 802.11 Based Positioning - moving from <1m to <0.1m
t1 and t4 are measured by STA 1 using CLK1 w/ accuracy PPM1 marked t1’, t4’ respectively.
t3 and t2 are measured by STA 2 using CLK2 w/ accuracy PPM2, marked t3’, t2’ respectively.
RTD = (t4’-t1’+Δ1) – (t3’-t2’+ Δ2)
the measurement can be up to Δ1+ Δ2 off from the actual value.
Δ1 is measured over M1 + SIFS + RTD @ PPM1
Δ2 is measured over M1 + SIFS @ PPM2
M1 = 100usec
SIFS = 16usec
RTD << M1, SIFS
Worst case scenario: PPM1 = -PPM2 = 20ppm
Δ1 + Δ2 = ~(M1+SIFS) * (2*PPM1) * C ~1.4m

## Slide 21: Challenges of using 802.11 Based Positioning - moving from <1m to <0.1m
1st generation mitigation:
  Estimate time difference using a single clock rather than two non dependent ones.
  20ppm is the upper bound, better clock yields better accuracy.
  Doppler is of lower importance.
RTD = (t4’-t1’+Δ1) – (t3’-t2’+ Δ2)
=> Δ1 + Δ2 = ~(M1+SIFS) * (PPM1) * C ~0.7m
Going from <1m to <0.1m is a challenge

## Slide 22: Challenges of using 802.11 Based Positioning - moving from <1m to <0.1m
2nd generation improvement possible solutions:
  Using of 802.11ad (shorter packets yields smaller drift), but set additional challenges.
  Usage of mid-amble or post amble greatly reducing t4-t1 interval which is the main cause for the drift.
Nov. 2014

## Slide 23: Challenges of using 802.11 Based Positioning - moving from <1m to <0.1m
NLOS and NNLOS channel conditions increases the likelihood of having a wrong sense of range due to undetected first path.
These play a role when moving to the higher accuracy resolution and for proximity usages:
  Outliers harder to detect.
  Usage of MIMO techniques may help.
  Signals’ properties in the 60GHz band presents both
  an opportunity and a challenge.
Nov. 2014

## Slide 24: Challenges of using 802.11 Based Positioning - Scalable Positioning
FTM has a high overhead:
  Minimum of 6 messages required per single fix per AP.
  Minimum of 4 APs required per single fix.
  The medium usage is linearly dependent by the number of positioning STAs.
  We’ve seen* before that in dense environments this becomes unfeasible and that an infrastructure broadcast protocol might be better suited.
  * 11-14-1235/r0 – Scalable Location by Brian Hart, Peter Thornycroft and Mark Rison.
Nov. 2014

## Slide 25: Challenges of using 802.11 Based Positioning -Scalable Positioning
AP STA will need to communicate its intent and preference to its peers and indicate it to the positioning STAs in a form which is independent of number of positioning STAs.
Positioning STA may or may not be associated (use case dependent).
Larger BWs provides better channel resolution, at the expanse of co-channel interference.
Acceptable deployment uses multi channel deployments to reduce interference, which means inter AP communication will be needed to indicate their absence to associated STAs in a transparent/backwards compatible way.
  * 11-14-1235/r0 – Scalable Location by Brian Hart, Peter Thornycroft and Mark Rison.
Nov. 2014

## Slide 26: Summary
We described a new set of useful usage models that are of commercial use and interest.
We’ve described the challenges and area of technical development that are extension of existing technology either in 802.11 or other similar std.
REVmc has completed support for the basic indoor positioning which will lead to implementations and market adoption in the near future.
The group should now take the next step to extend the positioning support, and this should be done in a dedicated SG.

## Slide 27: Straw poll - 1
Do you think this would be a useful project for 802.11 to investigate?
Y:
N:
A:

## Slide 28
Backup

## Slide 29: Improved accuracy moving from <1m to <0.1m
  Current std. overview
  Current technology has a theoretical limitation of 0.7m with real world scenarios bringing it to 2-4m depending on environment.
Shown:
  Current technology.
  Ray trace simulation.
  40Mhz BW.
  5 APs
  Mix of dry walls, wood and metal frames.
  No MIMO (1x1 antenna scheme).
  Basic trilateration – no outlier handling.
  Simulated thermal and receive noise
Notes: -91dbm thermal and -20db receiver.