## Slide 1: NG60 Channel model challenges
Date: 2014-11-04
Authors:

## Slide 2: NG60 features required by the channel model
Channel bonding
Multiple streams MIMO
Multi-users channel (MU-MIMO): focus on DL-MU-MIMO
Interference and dense deployment
Outdoor channel

## Slide 3: Channel Bonding
Non-ideal antenna frequency responses
Reflection, penetration and diffraction coefficients @ mmWave are often frequency dependent due to the small wavelength
RF circuitry, including the shifters and combiners, have some frequency response
Extremely high BW in channel model distinguishes different paths (>4cm apart) More time-domain coefficients are deterministic
Outdoor frequency response depends on medium absorption
Outdoor channel with Doppler spreads/fast fading

## Slide 4
MIMO/MU-MIMO in the channel model
SISO model focuses on the largest singular value
MIMO model should predict several singular values and provide correlation between streams, thus model should be extended with
  Reflections with higher order (3rd were noticed in indoor measurements)
  Diffraction, especially for NLOS, provides higher rank to the channel matrix
Polarity characterization of reflections is required if polarity is to be used for spatial multiplication
Antenna array intimately connected to the model:
  Coupling between subassemblies (S21), and between chains
Subassembly patterns:
  Antenna elements pattern: patch, dipole, Yagi-Uda, combinations
RF control circuits: phase resolution, gain resolution
Array configuration algorithms included in model
  SVD which is approximated by the RF circuitry
  Max SNR approximated by the RF circuitry
  Max SINR approximated by the RF circuitry
Polarity separation of the array
Outdoor vs. indoor antennas
  Outdoor arrays are more directional

## Slide 5: Summary
NG60 channel model is required for evaluations of specifications
Channel model should be verified with measurements corresponding to the different scenarios
Channel model should account for the unique challenges posed by the NG60, presented in this presentation