## Slide 1: EPD for IEEE 802.11 5.9GHz Operations
Date: 2015-1-14
Authors:
Nov 2014

## Slide 2: Abstract
Background
Rationale for switching from LLC Protocol Discrimination (LPD) to EtherType Protocol Discrimination (EPD) in the IEEE 802.11 5.9 GHz bands
Current status of implementations and support
Nov 2014

## Slide 3: Background
From their inception, 802.2 (LLC) and 802.3 (L/T aka Ethernet) have been and continue to be incompatible layer-2 (LLC-sublayer) protocols.
Somewhere between 1999 and 2007, IEEE 802.11 specifically designated LLC (as defined in 802.2) as the Logical Link Control sublayer protocol to be used in all 802.11 STAs.
Ethernet now dominates the LAN market (FDDI and Token Ring are disappearing)
Slide 3
Nov 2014
Notes: doc.: IEEE 802.11-yy/0339r0
Month Year
John Doe, Some Company
Page 3

## Slide 4: Background (continued)
IEEE 802.2 was withdrawn in 2011 and is no longer supported by IEEE (ISO maintains a “stabilized” version in ISO/IEC 8802-2:1998)
IEEE 802-2014 Overview and Architecture explicitly discourages the use of 802.2 LLC in the future.
  “New IEEE 802 standards shall support protocol discrimination in the LLC sublayer using EPD.”
Slide 4
Nov 2014
Notes: doc.: IEEE 802.11-yy/0339r0
Month Year
John Doe, Some Company
Page 4

## Slide 5: Background (continued)
The use of EtherTypes instead of DSAP/SSAP addresses as network layer protocol identifiers means LLC SNAP/RFC1042 has to be used (cf. IEEE 802.11)
As a consequence, six (6) octets of fixed content (and therefore useless) are transmitted in every over-the-air stream.
Slide 5
Nov 2014
Notes: doc.: IEEE 802.11-yy/0339r0
Month Year
John Doe, Some Company
Page 5

## Slide 6: Background (continued)
Slide 6
LLC-sublayer 802.2 (LPD) header format (LLC SNAP RFC1042)
Length/Type encoding (EPD) header format
Length < 1503 (0x05DF)
Ethertype > 1535 (0x05FF)
Nov 2014
Notes: doc.: IEEE 802.11-yy/0339r0
Month Year
John Doe, Some Company
Page 6

## Slide 7: Background (continued)
IEEE 802.11 TGp created the amendment to IEEE 802.11 for operations in the 5.850-5.925 GHz frequency bands currently allocated by the FCC to Intelligent Transport Systems (ITS) operations
Operations in these bands are “outside the context of a BSS” (dot11OCBActivated is true in 5.9 GHz bands in the US and Europe (see IEEE Std 802.11 Annex E))
Slide 7
Nov 2014
Notes: doc.: IEEE 802.11-yy/0339r0
Month Year
John Doe, Some Company
Page 7

## Slide 8: Rationale
There are currently no commercial deployments of IEEE 802.11 5.9 GHz units/systems (only prototype units in trials); hence the 5.9 GHz MAC/PHY can be considered to be “new”.
Therefore, EPD should be used because it is:
  more efficient (6 bytes saved in every data frame)
  “compatible” with 802.3 ethernet LANs and 802.1Q bridges
  compatible with GLK (EPD) operation (when standardization is complete)
  IEEE 802-2014 mandates it!
Slide 8
Nov 2014
Notes: doc.: IEEE 802.11-yy/0339r0
Month Year
John Doe, Some Company
Page 8

## Slide 9: Rationale (continued)
There are ongoing discussions on and investigations into possible sharing of some part of the ITS 5.9 GHz frequency bands (cf. UNII-4 in FCC NPRM 13-22)
Changing from LPD to EPD for ITS communications in the ITS bands would neither impact nor be impacted by possible sharing with other IEEE 802.11 devices should such sharing eventually be allowed
The ONLY change is to the contents of the LLC sublayer Protocol Data Unit (LPDU … aka MSDU)
Slide 9
Nov 2014
Notes: doc.: IEEE 802.11-yy/0339r0
Month Year
John Doe, Some Company
Page 9

## Slide 10: Current Implementations
Vendors of 5.9 GHz (11p) radio units have made and successfully tested the change including:
  Q-Free
  Commsignia
  Savari Networks
  Arada Systems
  Denso
  ITRI
Slide 10
Nov 2014
Notes: doc.: IEEE 802.11-yy/0339r0
Month Year
John Doe, Some Company
Page 10

## Slide 11: Current Implementations - LPD (before)
Slide 11
Nov 2014
Notes: doc.: IEEE 802.11-yy/0339r0
Month Year
John Doe, Some Company
Page 11

## Slide 12: Current Implementations - EPD (after)
Slide 12
Nov 2014
Notes: doc.: IEEE 802.11-yy/0339r0
Month Year
John Doe, Some Company
Page 12

## Slide 13: Current Support
A large number of vendors have indicated support for the change
In October 2014, TC 204 passed the following resolution:
“Resolution 1072:
ISO/TC 204 resolves to support a change from LPD
to EPD in the 802.11 specifications for 5.9 GHz frequency bands.
APPROVED”
Slide 13
Nov 2014
Notes: doc.: IEEE 802.11-yy/0339r0
Month Year
John Doe, Some Company
Page 13

## Slide 14: 802.11 WG Straw Poll Results November 2014 (San Antonio)
Do you support a change from LPD to EPD for ITS communications in the IEEE 802.11 5.9GHz (“11p”) frequency bands?
  YES: 20
  NO: 0
  NEED MORE INFORMATION/TIME: 37
  ABSTAIN: 1
Slide 14
Nov 2014
Notes: doc.: IEEE 802.11-yy/0339r0
Month Year
John Doe, Some Company
Page 14

## Slide 15: MOTION
Move to instruct the TGm editor to make the changes specified in 11-14-1522-02-000m-lpd-to-epd-in-5-9ghz.docx to the latest version of the 802.11 draft.
  YES:
  NO:
  ABSTAIN:
Slide 15
Nov 2014
Notes: doc.: IEEE 802.11-yy/0339r0
Month Year
John Doe, Some Company
Page 15