## Slide 1: Offline Discussion Minutes of SLS Calibration
Date: 2015-01-12
Authors:

## Slide 3: Motivation & Objective
Though basic SLS evaluation methodology has been formally described [1], there are still many issues not clearly defined.
Companies may have different implementations of those unclear MAC/PHY features, which has exhausted so much time and effort.
To speed up the joint SLS calibration, we definitely require a common implementation (simple and reasonable) for each divergent feature.
This contribution further clarifies several unclear points in its last version [2].

## Slide 4: Potential Differences
  Differences depend on how accurate we’d like the SLS is
    Preamble model
    Preamble detection metric
    RBIR PHY abstraction
    Receiving procedure and CCA status
    Control frame detection
    Box5 calibration scenario
  Discussion results for each item are highlighted in red color
  Special setting for calibration is marked in green color

## Slide 5: Preamble Model
Which model do you prefer?
  Opt 1: Take the whole preamble as a standalone sub-frame
  Opt 2: Deal with SFT, LTF, SIG individually
Companies prefer Opt 1.
  Note that for calibration the preamble here indicates the entire preamble for each PHY frame
    For control frame, the preamble only includes the legacy part
    For data frame, both legacy part and VHT part are included.

## Slide 6: Preamble Detection
Which method do you prefer?
  Take the whole preamble as a standalone sub-frame
    Opt 1: Preamble decoding error modeled based on SINR threshold
      Set a preamble error SINR threshold T
      If SINR < T, preamble decoding fails, otherwise, it passes;
    Opt 2: Preamble decoding modeled as a sub-frame decoding
      Take the whole preamble as a standalone sub-frame
      The PHY abstraction can be used for preamble PER prediction
        For calibration, the packet length in bytes used in PER computation is calculated based on the assumption of 3-byte/4us (MCS0)
        For calibration, the duplicated parts in preamble among multiple 20MHz channels are not combined.
      The impairments such as channel estimation error may be captured
        The CE model based on LTF is TBD
        For calibration, link adaptation and CE model are ignored unless otherwise stated
Companies prefer Opt 2.

## Slide 7: RBIR PHY Abstraction
Which RBIR-based PHY abstraction solution do you prefer for PER prediction under asynchronous and time-varying interference?
  For AMPDU, each MPDU is decoded individually
    Opt 1: Whole packet average
    Opt 2: Weakest link
    Opt 3: Block-wise PHY abstraction
    Opt 4: Simplified block-wise (aka the weakest link with the length scaled) [3]
Companies prefer Opt 4.

## Slide 8: Receiving Procedure (1)
Do you agree the following basic reception principle?
  Receiver starts a scanning window if a packet arrives, and switches the window to another packet if this packet arrives within the window and has rx power xdB higher than the current packet.
    The xdB threshold is TBD and the window size is TBD in [0, PPDU duration].
    If window size = 0, that is, receiver will be locked by the first-arrived packet, and later-arrived packets are considered as interference.
      For calibration, set window size = 0
  Any packet with rx power lower than rx sensitivity is dropped, which does not impact current receiver status;
  Any packet with rx power higher than rx sensitivity will be dealt with, i.e., its preamble will be detected, when the receiving device is able to receive packets.
Accepted by companies.

## Slide 9: Receiving Procedure (2)
Do you agree the following description?
  If preamble passes (i.e., successfully detected), the receiver continues to receive the rest part of the packet, i.e., to decode each MPDU;
    If successfully decoding of a MAC frame, defer for NAV;
      Apply NAV cancellation for RTS according to current std spec
    Otherwise, set CCA to busy for the entire PPDU duration if rx power higher than TBD [rx sensitivity or CCA-SD].
      For calibration, set rx sensitivity = CCA-SD
  If preamble fails, the receiver terminates current reception
    The entire PPDU fails
    The receiver is unlocked again and then CCA-ED threshold is used to determine if the medium is busy.
Accepted by companies.
  The above procedure could be modified correspondingly if BSS color or/and PAID is introduced later.

## Slide 10: Control Frame Detection
How to decide RTS/CTS/ACK reception is pass or fail after successful preamble detection?
  Opt 1: decoding error modeled based on SINR threshold
    Set a error SINR threshold T
    If SINR < T, decoding fails, otherwise, it passes;
  Opt 2: decoding error modeled as a sub-frame decoding
    Take the whole control frame as a standalone sub-frame
    The PHY abstraction can be used for the PER prediction
      For calibration, MCS0 is used for control frames
Companies prefer Opt 2.

## Slide 11: Box5 Calibration Scenario
Which scenario do you prefer to use for Box5 calibration?
  Opt 1: Firstly using 11ac SS6 as an easy-to-start reference scenario to solve differences among individual implementations, and then after successfully calibration, turn to calibrate more complicated 11ax scenarios;
  Opt 2: Directly calibrating more complicated and time-comsuming 11ax scenarios;
  Opt 3: Slim down one of the 4 11ax scenarios into a simplified scenario, and redefine the number and locations of the used APs/STAs; after successfully calibrating the clipped scenario, go to calibrate the full 11ax scenarios.
No consensus but at least 4 companies have already got initial results based on Opt1.

## Slide 12: Summary
A big progress was made towards SLS calibration.
Open issues will be further discussed among companies.
The agreements in this contribution are suggested to be reflected in the EMD [1].

## Slide 13: Reference
[1] 11-14/0571r6 Evaluation Methodology
[2] 11-14/1523r4 Offline Discussion Minutes of SLS Calibration
[3] 11-15/0093r1 Text Update on PHY Abstraction and SP

## Slide 14: Straw Poll
Do you agree to add to the EMD 11-14/0571r6?
Yes/No/Abs: