## Slide 1: FILS element assignment
Date: 2014-11-06
Authors:

## Slide 2: Abstract
IEEE 802.11 standard is running out of Element IDs. This document discusses possible steps TGai could take in this process.

## Slide 3: Element extension (TGmc and WG)
Discussion showed clear support for Option 1 (single octet Element ID extension) (see 14/1353r3)
  expected to pass motion Thursday PM2
WG discussion on Friday on policy for remaining Element IDs
  may affect how ANA handles pending TGai request
Only a very small number of IDs remain available
Would be helpful for 802.11 in general to use the shortest Element option in Beacon (and Beacon-like) frames (and use extended version for frames that are not as critical as far as length is concerned)

## Slide 4: FILS elements
Beacon frame
  CAG Number element
  FILS Indication element
  AP-CSN element
  Differentiated Initial Link Setup element
  FILS Public Key Indicator element
    note: missing from Table 8-85
FILS Discovery frame
  FILS Indication element

## Slide 5: FILS elements
Only in other frames
  FILS Request Parameters element
  FILS Key Confirmation element
  FILS Session element
  FILS Public Key element
  FILS HLP Container element
  FILS IP Address Assignment element
  Key Delivery element
  FILS Wrapped Data element
  Fragment element

## Slide 6: TGai request to ANA
Could provide more information to ANA on the specific need (elements included in Beacon-like frames) to help allocation process
  Need for this depends on the WG discussion on Friday
Should be fine for elements that are not included in Beacon or FILS Discovery frames to use the new extension format (one extra octet per element)

## Slide 7: Motion
Move to provide following additional information to the ANA on TGai Element ID assignment request:
  TGai preference is to get “legacy elements” (no extension octet) for following new elements:
    CAG Number element
    FILS Indication element
    AP-CSN element
    Differentiated Initial Link Setup element
    FILS Public Key Indicator element
  Extended Element (one octet extension) is acceptable for the other requested Element IDs