## Slide 1: MAC Calibration Results
Date: 2015-01-012
Authors:

## Slide 2: Abstract
In [1] and [2] MAC calibration tests and evaluation methods for MAC simulator are described
Other MAC simulator calibration results were presented in [3] – [11]
This document provides MAC calibration results for:
  MAC overhead (Test 1a (without RTS/CTS), and 1b (with RTS/CTS)
  Deferral tests (Test 2a (without hidden nodes), and 2b (with hidden nodes)
  NAV deferral (Test 3)
Comparison of [3] – [11] MAC calibration results

## Slide 3: Common Assumptions and Parameters
PHY
  Long Guard Interval: 800 ns
  Data Preamble: 802.11ac
  Bandwidth: 20 MHz
MAC
  A-MPDU aggregation: up to 2 MPDU
  No A-MSDU aggregation: 1 MSDU
  Maximum number of retransmissions: 10
  No rate adaptation: Fixed at MCS 0 or MCS 8
  EDCA Best Effort: CWmin = 15, AIFS = DIFS = 34 us
  Transport Protocol: UDP
  Traffic model: Full buffer

## Slide 4: Test 1a: MAC Overhead without RTS/CTS
Goal
  Verification of basic frame exchange, including AIFS+backoff and A-MPDU+SIFS+BA, and their overheads
Assumptions
  PER = 0 %
  MSDU lengths: 500, 1000, 1500, 2000 bytes
  Two MPDUs per A-MPDU
  Data MCS = 0 and 8
  ACK MCS = 0
Test Metrics
  Application and MAC layer throughputs
  Check points and time traces
STA 1
AP1

## Slide 5: Test 1a: Check Points
Test Items | Standard definition | Check points (MCS 0) |  |  |  | Matching?
MSDU Length (B) |  | 500 | 1000 | 1500 | 2000 | 
A-MPDU duration (us) | ceil((FrameLength*8)/rate/OFDMsymbolduration) * OFDMsymbolduration + PHY Header | Tcp2 - Tcp1 = 1364 | Tcp2 - Tcp1 = 2592 | Tcp2 - Tcp1 = 3824 | Tcp2 - Tcp1 = 5056 | √
SIFS (us) | 16 | Tcp3 - Tcp2 = 16 | Tcp3 - Tcp2 = 16 | Tcp3 - Tcp2 = 16 | Tcp3 - Tcp2 = 16 | √
ACK duration (us) | ceil((ACKFrameLength*8)/rate/OFDMsymbolduration) * OFDMsymbolduration + PHY Header | Tcp4 - Tcp3 = 68 | Tcp4 - Tcp3 = 68 | Tcp4 - Tcp3 = 68 | Tcp4 - Tcp3 = 68 | √
Avg. Defer & backoff duration (us) | DIFS(34 us)+backoff (CWmin) =34+n*9/2 | Tcp5 - Tcp4 = 101.5 | Tcp5 - Tcp4 = 101.5 | Tcp5 - Tcp4 = 101.5 | Tcp5 - Tcp4 = 101.5 | √

## Slide 6: Test 1a: Time Traces
MSDU Length (B) | 500 | 1000 | 1500 | 2000 | 500 | 1000 | 1500 | 2000
MCS | 0 | 0 | 0 | 0 | 8 | 8 | 8 | 8
CP1: start of A-MPDU (s) | 40.000664020 | 40.000664020 | 40.000664020 | 40.000664020 | 40.000588456 | 40.000588456 | 40.000588456 | 40.000588456
CP2: end of A-MPDU (s) CP2-CP1 (us) | 40.002028020 1364 | 40.003256020 2592 | 40.004488020 3824 | 40.005720020 5056 | 40.000740456 152 | 40.000844456 256 | 40.000944456 356 | 40.001048456 460
CP3: start of BA (s) CP3-CP2 (us) | 40.002044020 16 | 40.003272020 16 | 40.004504020 16 | 40.005736020 16 | 40.000756456 16 | 40.000860456 16 | 40.000960456 16 | 40.001064456 16
CP4: end of BA (s) CP4-CP3 (us) | 40.002112020 68 | 40.003340020 68 | 40.004572020 68 | 40.005804020 68 | 40.000824456 68 | 40.000928456 68 | 40.001028456 68 | 40.001132456 68
CP5: start of new A-MPDU (s) CP5-CP4 (us) | 40.002227020 115 | 40.003455020 115 | 40.004687020 115 | 40.005928020 124 | 40.000939456 115 | 40.001043456 115 | 40.001143456 115 | 40.001301456 169

## Slide 7: Test 1a: Throughput Results
MCS | Application Length (B) | MSDU Length (B) | Numerical Application Layer Throughput (Mbps) | Simulated Application Layer Throughput (Mbps) | Numerical MAC Layer Throughput (Mbps) | Simulated MAC Layer Throughput (Mbps)
0 | 464 | 500 | 4.79112 | 4.790378 | 5.16296 | 5.162045
0 | 964 | 1000 | 5.55320 | 5.553432 | 5.76058 | 5.760822
0 | 1464 | 1500 | 5.84212 | 5.843068 | 5.98578 | 5.986750
0 | 1964 | 2000 | 5.99523 | 5.995335 | 6.10512 | 6.105229
8 | 464 | 500 | 21.99704 | 21.940582 | 23.70370 | 23.642869
8 | 964 | 1000 | 34.93545 | 34.868915 | 36.24009 | 36.171073
8 | 1464 | 1500 | 43.25762 | 43.192417 | 44.32133 | 44.254526
8 | 1964 | 2000 | 48.68164 | 48.656924 | 49.57397 | 49.548803

## Slide 8: Test 1a: Application Throughput Comparison (Mbps)
Contribution # | MCS 0 |  |  |  | MCS 8 |  |  | 
 | 500 | 1000 | 1500 | 2000 | 500 | 1000 | 1500 | 2000
11-14/0600r0 | 4.76 | 5.53 | 5.82 | 5.98 | 23.92 | 37.25 | 45.55 | 50.81
11-14/1147r0 | 4.79 | 5.54 | 5.84 | 6.00 | 22.00 | 35.00 | 43.20 | 48.40
11-14/1175r1 | 4.81 | 5.55 | 5.84 | 5.99 | 22.4 | 35.2 | 43.25 | 48.9
11-14/1191r0 | 4.79 | 5.55 | 5.84 | 6.00 | 21.98 | 34.91 | 43.24 | 48.67
11-14/1217r0 | 4.76 | 5.52 | 5.83 | 5.97 | 21.19 | 34.22 | 41.93 | 47.74
11-14/1230r2 | 4.76 | 5.53 | 5.82 | 5.98 | 21.71 | 34.65 | 42.71 | 48.15
11-14/1342r1 | 4.79 | 5.55 | 5.84 | 5.99 | 21.99 | 34.94 | 43.27 | 48.68
11-14/1449r0 | 4.85 | 5.55 | 5.84 | 5.99 | - | - | - | -
11-15/0022r1 | 4.79 | 5.55 | 5.84 | 6.00 | 21.94 | 34.87 | 43.19 | 48.66

## Slide 9: Test 1b: MAC Overhead with RTS/CTS
Goal
  Verification of basic frame exchange, including AIFS+backoff and A-MPDU+SIFS+BA, and their overheads.
Assumptions
  PER = 0 %
  MSDU lengths: 500, 1000, 1500, 2000 bytes
  Two MPDUs per A-MPDU
  Data MCS = 0 and 8
  ACK MCS = 0
Test Metrics
  Application and MAC layer throughputs
  Check points and time traces
STA 1
AP1

## Slide 10: Test 1b: Check Points
Test Items | Standard definition | Check points (MCS 0) |  |  |  | Matching?
MSDU Length (B) |  | 500 | 1000 | 1500 | 2000 | 
RTS duration (us) | ceil((RTSFrameLength*8)/rate/OFDMsymbolduration) * OFDMsymbolduration + PHY Header | Tcp2 - Tcp1 = 52 | Tcp2 - Tcp1 = 52 | Tcp2 - Tcp1 = 52 | Tcp2 - Tcp1 = 52 | √
CTS duration (us) | ceil((CTSFrameLength*8)/rate/OFDMsymbolduration) * OFDMsymbolduration + PHY Header | Tcp4 – Tcp3 = 44 | Tcp4 – Tcp3 = 44 | Tcp4 – Tcp3 = 44 | Tcp4 – Tcp3 = 44 | √
Frame Duration (us) | ceil((FrameLength*8)/rate/OFDMsymbolduration) * OFDMsymbolduration + PHY Header | Tcp6 – Tcp5 = 1364 | Tcp6 – Tcp5 = 2592 | Tcp6 – Tcp5 = 3824 | Tcp6 – Tcp5 = 5056 | √

## Slide 11: Test 1b: Time Traces
MSDU Length (B) | 500 | 1000 | 1500 | 2000 | 500 | 1000 | 1500 | 2000
MCS | 0 | 0 | 0 | 0 | 8 | 8 | 8 | 8
CP1: start of RTS (s) | 40.000664020 | 40.000664020 | 40.000664020 | 40.000664020 | 40.000588456 | 40.000588456 | 40.000588456 | 40.000588456
CP2: end of RTS (s) CP2-CP1 (us) | 40.000716020 52 | 40.000716020 52 | 40.000716020 52 | 40.000716020 52 | 40.000640456 52 | 40.000640456 52 | 40.000640456 52 | 40.000640456 52
CP3: start of CTS (s) | 40.000732020 | 40.000732020 | 40.000732020 | 40.000732020 | 40.000656456 | 40.000656456 | 40.000656456 | 40.000656456
CP4: end of CTS (s) CP4-CP3 (us) | 40.000776020 44 | 40.000776020 44 | 40.000776020 44 | 40.000776020 44 | 40.000700456 44 | 40.000700456 44 | 40.000700456 44 | 40.000700456 44
CP5: start of A-MPDU (s) | 40.000792020 | 40.000792020 | 40.000792020 | 40.000792020 | 40.000716456 | 40.000716456 | 40.000716456 | 40.000716456
CP6: end of A-MPDU (s) CP6-CP5 (us) | 40.002156020 1364 | 40.003384020 2592 | 40.004616020 3824 | 40.005848020 5056 | 40.000868456 152 | 40.000972456 256 | 40.001072456 356 | 40.001176456 460

## Slide 12: Test 1b: Throughput Results
MCS | Application Length (B) | MSDU Length (B) | Numerical Application Layer Throughput (Mbps) | Simulated Application Layer Throughput (Mbps) | Numerical MAC Layer Throughput (Mbps) | Simulated MAC Layer Throughput (Mbps)
0 | 464 | 500 | 4.42563 | 4.426146 | 4.76900 | 4.769554
0 | 964 | 1000 | 5.30855 | 5.310115 | 5.50680 | 5.508418
0 | 1464 | 1500 | 5.66139 | 5.663762 | 5.80060 | 5.803035
0 | 1964 | 2000 | 5.85231 | 5.853787 | 5.95959 | 5.961087
8 | 464 | 500 | 15.94844 | 15.953555 | 17.18582 | 17.191331
8 | 964 | 1000 | 27.08341 | 27.091740 | 28.09482 | 28.103464
8 | 1464 | 1500 | 34.98730 | 34.997768 | 35.84765 | 35.858369
8 | 1964 | 2000 | 41.37039 | 40.565609 | 41.37039 | 41.309174

## Slide 13: Test 1b: Application Throughput Comparison (Mbps)
Contribution # | MCS 0 |  |  |  | MCS 8 |  |  | 
 | 500 | 1000 | 1500 | 2000 | 500 | 1000 | 1500 | 2000
11-14/0600r0 | 4.40 | 5.29 | 5.64 | 5.84 | 18.64 | 30.75 | 38.94 | 44.51
11-14/1147r0 | 4.42 | 5.30 | 5.67 | 5.85 | 16.00 | 27.10 | 34.97 | 40.40
11-14/1175r1 | 4.45 | 5.31 | 5.66 | 5.86 | 16.20 | 27.30 | 35.00 | 40.80
11-14/1191r0 | 4.42 | 5.31 | 5.66 | 5.85 | 15.94 | 27.07 | 34.97 | 40.61
11-14/1217r0 | 4.40 | 5.28 | 5.64 | 5.83 | 15.52 | 26.66 | 34.12 | 39.96
11-14/1230r2 | 4.40 | 5.29 | 5.64 | 5.84 | 15.79 | 26.90 | 34.62 | 40.24
11-14/1342r1 | 4.42 | 5.31 | 5.66 | 5.85 | 15.94 | 26.97 | 34.99 | 40.63
11-14/1449r0 | 4.43 | 5.27 | 5.62 | 5.82 | - | - | - | -
11-15/0022r1 | 4.43 | 5.31 | 5.66 | 5.85 | 15.95 | 27.09 | 35.00 | 40.57

## Slide 14: Test 2a: Deferral Test 1
Goal
  Verification of deferral procedure due to collisions without hidden nodes, and due to energy levels.
Assumptions
  All devices within energy detect range of each other. APs should defer to each other.
  When AP1 and AP2 transmit on the same slot, both packets are lost (PER = 100 %), otherwise both packets get through (PER = 0 %)
  MSDU lengths: 500, 1000, 1500, 2000 bytes
  Two MPDUs per A-MPDU
  RTS/CTS on and off
  Data, ACK, and RTS/CTS MCS = 0
Test Metrics
  Application layer throughput
STA 1
AP 2
AP1
STA 2
(AP1 and STA2 are essentially co-located)

## Slide 15: Test 2a: Throughput Results
RTS/CTS | Application Length (B) | MSDU Length (B) | Simulated Application Layer Throughput (Mbps) | Simulated MAC Layer Throughput (Mbps)
Off | 464 | 500 | 4.640073 | 5.000079
Off | 964 | 1000 | 5.293784 | 5.491477
Off | 1464 | 1500 | 5.545018 | 5.681371
Off | 1964 | 2000 | 5.701751 | 5.806265
On | 464 | 500 | 4.47186 | 4.818812
On | 964 | 1000 | 5.35922 | 5.559355
On | 1464 | 1500 | 5.711964 | 5.85242
On | 1964 | 2000 | 5.873815 | 5.981482

## Slide 16: Test 2a: Application Throughput Comparison (Mbps)
Contribution # | RTS/CTS Off |  |  |  | RTS/CTS On |  |  | 
 | 500 | 1000 | 1500 | 2000 | 500 | 1000 | 1500 | 2000
11-14/0600r0 | 4.57 | 5.26 | 5.53 | 5.67 | 4.45 | 5.32 | 5.67 | 5.86
11-14/1147r0 | 4.58 | 5.25 | 5.45 | 5.66 | 4.49 | 5.35 | 5.70 | 5.88
11-14/1175r1 | 4.62 | 5.28 | 5.54 | 5.66 | 4.50 | 5.34 | 5.68 | 5.88
11-14/1191r0 | 4.56 | 5.25 | 5.51 | 5.66 | 4.46 | 5.33 | 5.68 | 5.87
11-14/1217r0 | 4.58 | 5.29 | 5.56 | 5.71 | 4.48 | 5.32 | 5.67 | 5.85
11-14/1230r2 | 4.71 | 5.48 | 5.78 | 5.94 | 4.35 | 5.24 | 5.62 | 5.81
11-14/1342r1 | 4.59 | 5.28 | 5.55 | 5.68 | 4.47 | 5.31 | 5.65 | 5.87
11-14/1449r0 | 4.80 | 5.49 | 5.77 | 5.93 | 4.39 | 5.22 | 5.57 | 5.77
11-15/0022r1 | 4.64 | 5.29 | 5.55 | 5.70 | 4.47 | 5.36 | 5.71 | 5.87

## Slide 17: Test 2b: Deferral Test 2
Goal
  Verification of deferral procedure due to collisions with hidden nodes.
Assumptions
  APs can not hear each other.
  Interference assumptions:
    If preamble sees interference, all MPDUs fail. If an MPDU sees interference, it fails. Otherwise, all MPDUs pass. All ACK PER = 0 %.
  Backoff assumptions:
    If no ACK is received, transmitter doubles it’s CW.
    If an ACK is received, transmitter resets it’s CW.
    If MPDU is not decoded, no ACK is sent.
    After 10 missing ACKs, transmitter resets it’s CW.
  MSDU length: 1500 bytes

## Slide 18: Test 2b: Deferral Test 2
Assumptions – cont’d
  Two MPDUs per A-MPDU
  RTS/CTS off
  Data MCS = 0 and 8
  ACK MCS = 0
Test Metrics
  Throughput calculated from successfully ACKed MPDUs and the total time
    With frame aggregation
    Without frame aggregation
  PER = 1 – ACKed data MPDUs / Total data MPDUs sent
STA 1
AP 2
AP1
STA 2

## Slide 19: Test 2b: Throughput Results
Frame Aggregation | MCS | Application Length (B) | MSDU Length (B) | Simulated Application Layer Throughput (Mbps) | Simulated MAC Layer Throughput (Mbps)
No | 0 | 1464 | 1500 | - | -
No | 8 | 1464 | 1500 | - | -
Yes | 0 | 1464 | 1500 | 1.378822 | 1.412728
Yes | 8 | 1464 | 1500 | 23.609922 | 24.190494

## Slide 20: Test 2b: Application Throughput Comparison (Mbps)
Contribution # | MCS 0 |  | MCS 8 | 
 | No Frame Aggregation | Frame Aggregation | No Frame Aggregation | Frame Aggregation
11-14/0600r0 | - | 0.98 | - | -
11-14/1147r0 | - | 1.06 | - | -
11-14/1175r1 | 1.70 | 1.02 | 26.80 | 35.00
11-14/1191r0 | 1.62 | 1.01 | 26.54 | 34.75
11-14/1217r0 | - | 1.20 | - | 35.66
11-14/1230r2 | - | 0.04 | - | -
11-14/1342r1 | 1.62 | 0.95 | 28.85 | 33.96
11-14/1449r0 | - | 1.03 | - | -
11-15/0022r1 | - | 1.38 | - | 23.61

## Slide 21: Test 3: NAV Deferral
Goal
  Verification of deferral procedure due to collisions with hidden nodes and with RTS/CTS.
Assumptions
  APs can not hear each other.
  Interference assumptions:
    If preamble sees interference, all MPDUs fail. If an MPDU sees interference, it fails. Otherwise, all MPDUs pass. All ACK PER = 0 %.
  Backoff assumptions:
    If no ACK is received, transmitter doubles it’s CW.
    If an ACK is received, transmitter resets it’s CW.
    If MPDU is not decoded, no ACK is sent.
    After 10 missing ACKs, transmitter resets it’s CW.
  MSDU length: 1500 bytes

## Slide 22: Test 3: NAV Deferral
Assumptions – cont’d
  Two MPDUs per A-MPDU
  Data MCS = 0 and 8
  ACK and RTS/CTS MCS = 0
Test Metrics
  Throughput calculated from successfully ACKed MPDUs and the total time
    With frame aggregation
    Without frame aggregation
  PER = 1 – ACKed data MPDUs / Total data MPDUs sent
STA 1
AP 2
AP1
STA 2

## Slide 23: Test 3: Throughput Results
Frame Aggregation | MCS | Application Length (B) | MSDU Length (B) | Simulated Application Layer Throughput (Mbps) | Simulated MAC Layer Throughput (Mbps)
No | 0 | 1464 | 1500 | - | -
No | 8 | 1464 | 1500 | - | -
Yes | 0 | 1464 | 1500 | 5.798560 | 5.941148
Yes | 8 | 1464 | 1500 | 22.924866 | 22.101817

## Slide 24: Test 3: Application Throughput Comparison (Mbps)
Contribution # | MCS 0 |  | MCS 8 | 
 | No Frame Aggregation | Frame Aggregation | No Frame Aggregation | Frame Aggregation
11-14/0600r0 | - | 5.55 | - | -
11-14/1147r0 | - | 5.40 | - | -
11-14/1175r1 | 5.14 | 5.58 | 22.40 | 34.20
11-14/1191r0 | 5.15 | 5.58 | 22.04 | 34.05
11-14/1217r0 | - | 5.59 | - | 31.35
11-14/1230r2 | - | 5.64 | - | -
11-14/1342r1 | 5.19 | 5.61 | 21.64 | 33.82
11-14/1449r0 | - | 5.78 | - | -
11-15/0022r1 | - | 5.80 | - | 22.92

## Slide 25: Conclusion
  MAC calibration simulation results for Tests 1a, 1b, 2a, 2b, and 3 were mostly similar to other contribution results.

## Slide 26: References
[1] IEEE 802.11-14/0980r5, Simulation Scenarios, Simone Merlin et. al., November 2014.
[2] IEEE 802.11-14/0571r6, Evaluation Methodology, Ron Porat et. al., November 2014.
[3] IEEE 802.11-14/0600r0, MAC Simulator Calibration, Gwen Barriac et. al., May 2014.
[4] IEEE 802.11-14/1147r0, MAC Simulator Calibration Results, Shoko Shinohara, et. al. September 2014.
[5] IEEE 802.11-14/1175r1, MAC Calibration Results, Suhwook Kim, et. al., September 2014.
[6] IEEE 802.11-14/1191r0, MAC Calibration Huawei Results, Yanchun Li, et. al., September 2014.
[7] IEEE 802.11-14/1192r3, Comparing MAC Calibration Results, Yanchun Li, et. al., October 2014.
[8] IEEE 802.11-14/1217r0, MAC Calibration Results for Tests 1 and 2, Esa Tuomaala, et.al., September 2014.
[9] IEEE 802.11-14/1230r2, MAC Calibration Result, Chinghwa Yu, et. al., September 2014.
[10] IEEE 802.11-14/1342r1, MAC Calibration Results, Igor Kim, et. al., November 2014.
[11] IEEE 802.11-14/1449r0, MAC Calibration Results, Vida Ferdowsi, et.al., November 2014.