## Slide 1: Simulation-based evaluation of DSC in residential scenario
Date: 2015-Jan
Authors:

## Slide 2: Outline
Context
Simulation Environment: NS-3
DSC algorithm
Simulation scenarios and assumptions
Metrics used for evaluation
Selection of suitable parameters for DSC
Combining DSC with channel selection and rate control
Hybrid case A: Impact of DSC cells over legacy cells
Hybrid case B: Impact of DSC nodes over legacy nodes within cells
Worst case scenario (MCS0 & packet size of 1500 bytes)
Conclusions/next steps
References
Appendix

## Slide 3: 1. Context
One of the main objectives of IEEE 802.11ax standards is to improve efficiency in scenarios with high density of AP and non-AP stations by,
  increasing spectral frequency reuse.
  managing interference in OBSS.
It has been shown in previous presentations[1-11] that the use of DSC can increase the per-user throughput in dense scenarios.
In this submission we,
  investigate the performance of DSC,
    NS-3 simulator is used to measure the performance of DSC in dense WLAN network that contains multiple OBSS.
  recommend parameters to be employed for DSC algorithm.
  study the impact of DSC cells over legacy cells.

## Slide 4: 2. Simulation Environment: NS-3
NS-3 is a simulator for Internet systems,
  It allows the study of protocols and network performance of large-scale systems in a controlled and scalable environment.
Main characteristics,
  Discrete event simulator
  Packet level simulator (layer 2 and above)
  Layered architecture
  Free and open source
  Frequent updates ( latest version ns 3.21- release date 17-09-2014)
Large number of protocol implementations and models available,
  TCP, UDP
  IPV4, IPV6, static routing
  IEEE 802.11 and variants, WiMAX, LTE
  IEEE 802 physical layer
  Mobility models and routing protocols
  Ability to design indoor, outdoor or hybrid networks
  etc.

## Slide 5: 2. Simulation Environment: NS-3
Challenges
  dense WLAN scenario with multiple OBSS generated in NS-3 where the simulation package is modified to,
    allow STAs to measure the energy level of received beacon frames.
    improve hybrid building pathloss model to accommodate floor penetration losses.
  modifications /new additions made to accommodate real time operation of DSC algorithm.
Limitations
  MPDU aggregation is not yet implemented and thus not used within these simulations.
  IEEE 802.11ac model has not yet been developed and current results focus on IEEE 802.11g/n.

## Slide 6: 3. DSC algorithm
DSC varies CST levels at each station in a distributed manner,
  stations near their respective AP can have higher CST because interference from concurrent transmissions would have limited implications.
  stations further away can have lower CST because the probability of correct transmissions can be increased by reducing the presence of hidden nodes.
Flow chart highlights the basic operation of DSC algorithm over non-AP stations in an infrastructure-based WLAN.

## Slide 7: 4. Simulation scenarios and assumptions
Topology
  multi-floor residential building,
    5 stories
    2×10 apartments per story.
    Apartment size: 10m×10m×3m.
  1 AP placed randomly in each apartment at 1.5m height.
  channel selected randomly for each cell.
    Three channel scheme (1, 6, 11) 1/3 of the cells share the same channel
  5 STAs placed randomly around their respective AP.

## Slide 8: 4. Simulation scenarios and assumptions
  Frequency band: focused on 2.4GHz ,
  Intended to investigate the impact of DSC in a band that is more restricted in dense environments.
  Traffic: UDP CBR uplink transmission in saturation conditions is considered,
  Worst case in terms of contention.
Pathloss model: Hybrid Building Propagation loss model [12],
  obtained through a combination of several well known pathloss including indoor (through walls, floors) and outdoor (urban, suburban, open).
We simulated specific scenarios (with same STA and AP positions) with and without utilizing the DSC.
Additional simulation details are provided in the appendix.

## Slide 9: 5. Metrics used for evaluation
Aggregate throughput and STA’s individual throughput
Frame Error Rate (FER)
  ratio of data frames received with errors to total data frames received.
Fairness
  calculated according to Jain’s fairness index [13].
Number of hidden nodes
  Hidden node: detected when a node that is located outside the sensing range of the transmitter is able to interfere in the ongoing transmission from the transmitter to the receiver.
  a pair of hidden nodes is considered a single entry.
Number of exposed nodes
  Exposed node: detected when a node is needlessly silenced to concurrently transmit, even though the node is not able to generate ample interference that could cause collisions at the receiver.
  a pair of exposed nodes is considered a single entry.

## Slide 10: 6. Selection of suitable parameters for DSC
Observations:
  throughput results indicate around 10 % improvement for all the cases over the conventional IEEE 802.11 protocol.
  maximum fairness benefits were achieved when lower values of Margin are used.
Conclusions:
  the proposed algorithm increases the aggregate throughput along with fairness.
Chart: Margin
| 5 | 10 | 15 | 20 | 25
RSSIDEC=4 | 12.0763 | 10.2153 | 9.7463 | 11.6145 | 10.6053
RSSIDEC=5 | 12.5336 | 11.9562 | 10.4349 | 9.6179 | 10.7888
RSSIDEC=6 | 9.5064 | 13.0846 | 9.8743 | 11.5034 | 10.2063
Chart: Margin
| 5 | 10 | 15 | 20 | 25
RSSIDEC=4 | 14.9402 | 15.7796 | 15.5221 | 8.6768 | 8.3059
RSSIDEC=5 | 15.9083 | 10.1938 | 12.9291 | 11.0586 | 6.9486
RSSIDEC=6 | 16.318 | 12.3559 | 11.2021 | 10.8206 | 10.3309

## Slide 11: 6. Selection of suitable parameters for DSC
Observations:
  higher values of Margin and RSSIDec result in smaller FER degradation.
  at higher Margin values, the increase in hidden nodes is smaller.
  the presence of exposed nodes is driven to 0 by the DSC algorithm.
Conclusions:
  a consequence of the increased number of hidden nodes, the overall FER in network is increased  larger access delay.
Chart: Margin
| 5 | 10 | 15 | 20 | 25
RSSIDEC=4 | 23.8868 | 20.8743 | 16.7762 | 14.4307 | 10.0107
RSSIDEC=5 | 24.5317 | 24.1258 | 16.843 | 13.5253 | 9.3021
RSSIDEC=6 | 24.8713 | 20.9429 | 15.3192 | 13.1938 | 11.9587
Chart: Margin
| 5 | 10 | 15 | 20 | 25
RSSIDEC=4 | 436.5992 | 306.7323 | 196.1538 | 110.7414 | 69.4962
RSSIDEC=5 | 327.3374 | 269.9911 | 227.171 | 120.5066 | 62.6582
RSSIDEC=6 | 360.6557 | 276.6887 | 241.6451 | 116.3646 | 72.1348

## Slide 12: 7. Combining DSC with channel selection and rate control (1/2)
Observations:
  scenarios where DSC is combined with optimal channel selection provide maximum throughput gains of more than 20%.
  DSC has more room for improvement when MCS is set randomly.
  Fairness and throughput increased in all the scenarios when DSC is used.
Conclusions:
  Optimal channel selection has slightly larger impact on performance than DSC
  DSC increases the aggregate throughput by fairly increasing throughput over all the nodes.
Chart: Fairness
| RCHS+FMCS | OPCHS+FMCS | RCHS+RMCS | OPCHS+RMCS
Without DSC | 0.66126 | 0.74786 | 0.62734 | 0.68932
With DSC | 0.71364 | 0.80628 | 0.69073 | 0.77287
Chart: % Increase in throughput
RCHS+FMCS | 6.2422
OPCHS+FMCS | 20.9756
RCHS+RMCS | 8.5526
OPCHS+RMCS | 21.6212

## Slide 13: 7. Combining DSC with channel selection and rate control (2/2)
Observations:
  FER is slightly improved when optimal channel selection is used along with DSC.
  % increase in hidden nodes is smaller while utilizing optimal channel selection.
  with random channel selection, the increase in hidden nodes is around 150%.
  100% decrease in the number of exposed nodes is witnessed for all the cases.
Conclusions:
  the effect of increase in FER and the number of hidden nodes due to the DSC algorithm can be reduced while utilizing optimal channel selection along with DSC.
Chart: FER
| RCHS+FMCS | OPCHS+FMCS | RCHS+RMCS | OPCHS+RMCS
Without DSC | 0.28937 | 0.25746 | 0.27501 | 0.25385
With DSC | 0.34671 | 0.32042 | 0.33955 | 0.32606
Chart: % Increase in hidden nodes
RCHS+FMCS | 142.266
OPCHS+FMCS | 60.9325
RCHS+RMCS | 171.2202
OPCHS+RMCS | 66.2673

## Slide 14: 8. Hybrid case A: Impact of DSC cells over legacy cells (1/3)
Observations:
  average throughput of DSC cells increases over the cost of decrease in average throughput of non-DSC cells.
  throughput gains for DSC cells are more evident in hybrid scenarios (i.e. DSC + non-DSC cells) .
  average fairness in the network increases with the inclusion of DSC enabled cells.
Conclusions:
  overall average throughput and fairness are increased within the hybrid network due to DSC,
    Legacy cells/devices become less competitive.
Chart: % of DSC cells
| 0 | 20 | 40 | 60 | 80 | 100
All cells | 2.6708 | 2.7204 | 2.7737 | 2.905 | 2.8323
DSC cells | 0 | 3.3567 | 3.2318 | 3.2833 | 3.0036 | 2.8719
non-DSC cells | 2.6708 | 2.5614 | 2.4684 | 2.3374 | 2.1471 | 0
Chart: % of DSC cells
| 0 | 20 | 40 | 60 | 80 | 100
 | 0.67127 | 0.67003 | 0.6826 | 0.70015 | 0.70811 | 0.71672

## Slide 15: 8. Hybrid case A: Impact of DSC cells over legacy cells (2/3)
Chart: % of DSC cells
| 0 | 20 | 40 | 60 | 80 | 100
All cells | 0.28928 | 0.30159 | 0.31044 | 0.31604 | 0.33278 | 0.34842
DSC cells | 0 | 0.32424 | 0.33293 | 0.32892 | 0.34048 | 0.34842
non-DSC cells | 0.28928 | 0.29592 | 0.29545 | 0.29671 | 0.30198 | 0
Observation:
  average FER of DSC cells increases whereas the FER of non-DSC cells remains approximately consistent.
Conclusion:
  overall FER in the network increases with the increase in DSC cells.

## Slide 16: 8. Hybrid case A: Impact of DSC cells over legacy cells (3/3)
Observations:
  % increase in hidden nodes is greater for more number of DSC cells.
  maximum % decrease in exposed nodes is witnessed when all cells are DSC enabled.
Conclusions:
  the FER in the network is increased due to increased number of hidden nodes.
  DSC increases fairness in the network by reducing the number of exposed nodes.
Chart: % of DSC cells
| 20 | 40 | 60 | 80 | 100
 | 4.4899 | 21.037 | 61.2356 | 89.6701 | 158.2947
Chart: % of DSC cells
| 20 | 40 | 60 | 80 | 100
 | 33.3819 | 65.3169 | 85.1399 | 96.3993 | 99.8282

## Slide 17: 9. Hybrid case B: Impact of DSC nodes over legacy nodes within cells (1/3)
Chart: % of nodes using DSC per cell
| 0 | 20 | 40 | 60 | 80 | 100
 | 0.67127 | 0.56702 | 0.59982 | 0.65742 | 0.69077 | 0.71672
Chart: % of nodes using DSC per cell
| 0 | 20 | 40 | 60 | 80 | 100
All nodes | 2.6708 | 2.8454 | 2.8531 | 3.0035 | 3.0472 | 2.8719
DSC nodes | 0 | 5.1198 | 4.2245 | 3.7178 | 3.3532 | 2.8719
Non-DSC nodes | 2.6708 | 2.2768 | 1.9389 | 1.9312 | 1.8233 | 0
Observations:
  average throughput of DSC nodes increases over the cost of decrease in throughput of non-DSC nodes.
  throughput gains for DSC nodes are more evident than performance losses for non-DSC nodes.
  average fairness in the network was reduced for some hybrid scenarios (20% to 60% DSC nodes).
Conclusions:
  overall average throughput of the network is increased due to DSC, at the cost of noticeable performance degradation for legacy devices.

## Slide 18: 9. Hybrid case B: Impact of DSC nodes over legacy nodes within cells (2/3)
Chart: % of nodes using DSC per cell
| 0 | 20 | 40 | 60 | 80 | 100
All nodes | 0.28928 | 0.30159 | 0.31044 | 0.31604 | 0.33278 | 0.34842
DSC nodes | 0 | 0.32424 | 0.33293 | 0.32892 | 0.34048 | 0.34842
non-DSC nodes | 0.28928 | 0.29592 | 0.29545 | 0.29671 | 0.30198 | 0
Observation:
  average FER of DSC and non-DSC nodes increase with an increase in % nodes using DSC in a cell.
Conclusion:
  overall FER in the network (for all nodes) increases with the increase in DSC enabled nodes.

## Slide 19: 9. Hybrid case B: Impact of DSC nodes over legacy nodes within cells (3/3)
Chart: % of nodes using DSC per cell
| 20 | 40 | 60 | 80 | 100
 | 14.2322 | 24.1036 | 53.6492 | 99.8341 | 158.2947
Chart: % of nodes using DSC per cell
| 20 | 40 | 60 | 80 | 100
 | 41.6118 | 58.4013 | 85.2388 | 95.8213 | 99.8282
Observations:
  % increase in hidden nodes is greater for more number of DSC nodes.
  for the hybrid scenario, the % increase in hidden nodes is less than the case where all nodes are DSC enabled within a cell.
  maximum % decrease in exposed nodes is witnessed when all cells utilize DSC.
Conclusions:
  due to increased number of hidden nodes, the FER in the network is increased.
  DSC increases fairness in the network by reducing the number of exposed nodes.

## Slide 20: 10. Worst case scenario (MCS0 & packet size of 1500 bytes) (1/2)
Observations:
  scenario where DSC is combined with optimal channel selection provides maximum throughput gains of around 35%.
  fairness is increased in all the scenarios when DSC is used.
Conclusions:
  DSC increases the aggregate throughput by fairly increasing throughput over all the nodes.
  % increase in throughput for DSC plus optimal channel selection cells is considerable even under difficult network conditions.
Chart: % increase in throughput
MCS0+ps1500+RCHS | 14.3326
MCS0+ps1500+OPCHS | 35.0979
Chart: Fairness
| MCS0+ps1500+RCHS | MCS0+ps1500+OPCHS
Without DSC | 0.61052 | 0.69833
With DSC | 0.67569 | 0.78585

## Slide 21: 10. Worst case scenario (MCS0 & packet size of 1500 bytes) (2/2)
Observations:
  difference of average FER per node between DSC enabled and legacy nodes is notable when optimal channel selection is utilized.
  % increase in hidden nodes is less while utilizing optimal channel selection.
  almost 100% decrease in the number of exposed nodes is witnessed for all the cases.
Conclusions:
  relatively small difference in FER is observed between the network consisting of optimal channel selection and random channel selection.
  optimal channel selection helps to reduce the number of hidden nodes.
Chart: FER
| MCS0+ps1500+RCHS | MCS0+ps1500+OPCHS
Without DSC | 0.25762 | 0.24207
With DSC | 0.2803 | 0.28179
Chart: % increase in hidden nodes
MCS0+ps1500 | 85.4031
MCS0+ps1500+OPCHS | 47.1676

## Slide 22: 11. Conclusions/next steps
  DSC scheme provides improvements in throughput and fairness in all cases
    Based on the reduction of exposed nodes
  DSC also increases number of hidden nodes and FER.
  DSC makes more sense (i.e. provides larger improvements) in worse conditions
    Higher contention
    Slower STAs
  Margin of 20 and RSSIDec of 6 are observed to create a balance between the negative and positive aspects of DSC.
  Channel selection and rate control can improve the positive effects of DSC scheme.
  For Hybrid case A (DSC cells vs non-DSC cells): notable throughput gains for DSC cells at the cost of slight degradation for non-DSC cells.
  For Hybrid case B (DSC STAs vs. non-DSC STAs in the same cell): fairness results indicate the coexistence problem between DSC and legacy IEEE 802.11 nodes within the cells.
  Next steps,
    Repeat study in different scenarios.
    Analyze the impact of DSC in uplink plus downlink traffic.
    Study the effects of DSC algorithm over a network operating in 5GHz.

## Slide 23: 12. References
Graham Smith, DSP Group, 11-13-1290-01 Dynamic Sensitivity Control for HEW
Graham Smith, DSP Group, 11-13-1487-02 Dense Apartment Complex Capacity Improvements with Channel selection and Dynamic Sensitivity Control
Graham Smith, DSP Group, 11-13-1489-05 Airport Capacity Analysis
Graham Smith, DSP Group, 11-14-0045-02 E-Education Analysis
Graham Smith, DSP Group, 11-14-0058-01 Pico Cell Use Case Analysis
Graham Smith, DSP Group, 11-14-0294-02 Dynamic Sensitivity Control Channel Selection and Legacy Sharing
Graham Smith, DSP Group, 11-14-0365-01 Dynamic Sensitivity Control Implementation
Graham Smith, DSP Group, 11-14-0328-02 Dense Apartment Complex Throughput Calculations
Graham Smith, DSP Group, 11-14-0779-00 Dynamic Sensitivity Control Practical Usage
Imad Jamil, Orange, 11-14-0523-00 Mac Simulation Results for DSC and TPC
William Carney, Sony, 11-14-0854-00 DSC and Legacy Coexistence
Hybrid buildings propagation loss model: ns3-design document. [Online]. Available: http://www.nsnam.org/docs/models/html/buildingsdesign.html
J. R., “Fairness: How to measure quantitatively?” ATM Forum/94-0881, Sept. 1994.

## Slide 24: 13. Appendix

## Slide 25: Simulation assumptions
PHY parameters
Parameters4 | Values | Parameters | Values
Wireless Standard | IEEE 802.11g and IEEE 802.11n | Packet size | 1000bytes
Frequency band | 2.4 GHz | STA TX power | 16dBm
Physical transmission rate for IEEE 802.11g | 24Mbps | Transmission gain | 1dB
Physical transmission rate for IEEE 802.11n | 7.2Mbps 28.9Mbps 72.2Mbps | Reception gain | 1dB
Channel width | 20MHz | Noise figure | 7dB
Propagation delay model | Constant speed propagation delay | Energy detection threshold | -78dBm
Propagation loss model | Hybrid buildings propagation loss | Initial CCA threshold | -80dBm
Wall penetration loss | 12dB | Guard interval | Short
Floor penetration loss | 17dB | Data preamble | Short

## Slide 26
MAC parameters
Parameters | Values | Parameters | Values
Access protocol | EDCA | Retransmission attempts | 16
RTS/CTS | Disabled | Maximum missed beacons for re-association | 10000
Association | 100% STAs associated to AP in an Apartment | Active probing | Disabled
QOS | Enabled | Traffic model | Best effort
Aggregation | Disabled |  | 
Simulation parameters
Parameters | Values | Parameters | Values
Simulation time | 25 seconds | Simulations for each hybrid case | 24
Confidence interval | 95% | Simulations for non-DSC network | 24