## Slide 1: DL-OFDMA Map Frame
Date: 2015-01-09
Authors:

## Slide 2: Abstract
This submission proposes “DL-OFDMA Map frame” to indicate a specific sub-channel (20MHz) for receiving destined data to each STA in OFDMA PPDU.
This scheme will enable narrower band reception of DL-OFDMA PPDU. It also may realize operation with lower energy consumption on a STA side.

## Slide 3
Narrower bandwidth reception in the same OFDMA HEW PPDU was proposed as possible operating option.  Lower energy consumption
Figure in doc. 14/1417r0 (Nov. 2014)
AP to STA1 (5MHz)
AP to STA2 (5MHz)
AP to STA3 (5MHz)
AP to STA4 (5MHz)
AP to STA5 (20MHz)
AIFS
PIFS
Primary 20MHz Channel
Secondary 20MHz Channel
OFDMA HEW PPDU
with TXVECTOR parameter CH_BANDWIDTH equal to CBW40
Receive Bandwidth for
STA5
Indication is required in advance to select a specific sub-channel to receive data destined to each STA.  Proposal of Map frame in the next slide.
Receive Bandwidth for
STA1, 2, 3, 4
Receiving this bandwidth may be possible for STA5.

## Slide 4: DL-OFDMA Map frame (Concept)
Indicates pairs of a sub-channel and destined STAs (DL-OFDMA Mapping IE?) before sending OFDMA PPDU.
Is sent in 20MHz bandwidth as broadcast frame primarily on the primary 20MHz channel.
Is copied to other 20MHz channels to block media accesses by surrounding devices.
Helps to let a STA sleep (micro sleep) during OFDMA PPDU when no data exists for that STA.
May include indication of ACK procedure. (channel based sequentially, sub-channel based in parallel or …)
Example of Map frame is shown in Slide 12.

## Slide 5: Operation concept (1)
time
time
time
time
Map
Primary
20MHz
Secondary
20MHz
3rd 20MHz
4th 20MHz
Copy
Copy
Copy
DIFS or
AIFS
SIFS
Data
Data
Data
Data
RX
(20M)
Power state on a STA
LI
RX
(20M)
SIFS
ACK
*
ACK
*
ACK
*
ACK
*
LI
TX
RX
(20M)
Sleep
LI
LI
With data
No data
A STA receives DL-OFDMA Map frame on the primary 20MHz and designates which 20MHz channel has data destined to that STA in the following 80MHz OFDMA PPDU.
Frame flow
TX: Transmit
RX: Receive
LI: Listen
* It should be considered how to respond ACK in other contributions.
So normal ACK was considered here.
Colors indicate power state on a STA.

## Slide 6: Operation concept (2)
Busy
Busy
time
time
time
time
Map
Primary
20MHz
Secondary
20MHz
Secondary
40MHz-1/2
Secondary
40MHz-2/2
SIFS
Data
Data
RX
(80M)
Power state on a STA
LI
RX
(20M)
ACK
*
ACK
*
LI
TX
RX
(80M)
Sleep
LI
(80M)
LI
(80M)
With data
No data
When a STA receives DL-OFDMA Map frame across all operating channels (e.g. 80MHz), flexible channel usage may be possible. AP can transmit data even when the primary 20MHz is occupied.
Frame flow
SIFS
Map
DIFS or
AIFS
TX: Transmit
RX: Receive
LI: Listen
* It should be considered how to respond ACK in other contributions.

## Slide 7: Throughput Comparison
TP by DL-OFDMA
16 STAs in 80MHzBW
* Detailed assumptions are in Slide 12 and 13.
Chart: MCS 0
| 100.0 | 200.0 | 300.0 | 400.0 | 500.0 | 600.0 | 700.0 | 800.0 | 900.0 | 1000.0
OFDMA with MAP | 1.2349 | 1.536 | 1.6718 | 1.7492 | 1.7992 | 1.8341 | 1.8599 | 1.8797 | 1.8954 | 1.9082
OFDMA without MAP | 1.563 | 1.7666 | 1.8468 | 1.8897 | 1.9164 | 1.9346 | 1.9479 | 1.9579 | 1.9658 | 1.9722
11ac | 0.35059 | 0.59798 | 0.78188 | 0.92395 | 1.037 | 1.1291 | 1.2056 | 1.2702 | 1.3253 | 1.373
Throughput per STA (Mbps)
Data size per PPDU per STA (Byte)
Chart: MCS 8
| 100.0 | 200.0 | 300.0 | 400.0 | 500.0 | 600.0 | 700.0 | 800.0 | 900.0 | 1000.0
OFDMA with MAP | 2.7892 | 5.0056 | 6.8093 | 8.3056 | 9.567 | 10.6448 | 11.5764 | 12.3896 | 13.1056 | 13.7409
OFDMA without MAP | 5.3043 | 8.7127 | 11.0874 | 12.8369 | 14.1792 | 15.2418 | 16.1038 | 16.8171 | 17.4172 | 17.929
11ac | 0.41649 | 0.81898 | 1.2082 | 1.5847 | 1.9492 | 2.3022 | 2.6443 | 2.976 | 3.2976 | 3.6098
Data size per PPDU per STA (Byte)
Performance degradations were observed because of the Map overhead.  Optimization is required.
degradation
degradation
It’s just mathematical comparison. So media accesses by other BSSs wasn’t considered here.

## Slide 8: Energy Consumption on STA (for one round)
With Map frame (50% data existence)
Map
Map
Map
Map
Data
Data
Data
Data
ACK
Map
Map
Map
Map
Data
Data
Data
Data
ACK
ACK
ACK
ACK
ACK
ACK
ACK
Without Map frame (50% data existence)
Data
Data
Data
Data
ACK
Data
Data
Data
Data
ACK
ACK
ACK
ACK
ACK
ACK
ACK
LI
Power state
RX
LI
RX
LI
TX
LI
RX
Sleep
LI
RX
LI
TX
LI
RX
Sleep
Power state
<Assumption> ref : 14/1496r5
Power state | 20MHzBW | 80MHzBW
TX | 280mA | - - -
RX | 100mA | 400mA
LI | 50mA | 200mA
Sleep | 0.003mA | - - -
Data size | 100B |  | 1000B | 
MCS | MCS0 | MCS8 | MCS0 | MCS8
With Map (pri20M only) | 91 | 52 | 481 | 84
With Map (Across 80MHz) | 179 | 140 | 569 | 172
Without Map | 487 | 170 | 3606 | 429
Table: Power Model
Unit: micro J
Energy Consumption
We may have big gain by using Map frame!
time
time
Less chance to sleep and wider RX bandwidth in case of without Map.

## Slide 9: Summary
DL-OFDMA Map frame is proposed for efficient reception of DL-OFDMA PPDU. It will realize:
  Narrower bandwidth reception,
  Lower energy consumption and
  Flexible channel utilization without the primary 20MHz (maybe)
Related discussions are required for:
  Data mapping to realize partial reception of OFDMA PPDU
  Map frame contents for better efficiency,
  Media access method (Carrier sense),
  And so on.

## Slide 10: References
14/1417r0, “hew-ppdu-transmission-discussion”
14/1496r5, “power-save-calibration-scenario”
14/1210r1, “hew-ppdu-format-for-supporting-mimo-ofdma”

## Slide 11: Backup

## Slide 12: Assumption-1 DL-OFDMA Map IE
Element ID
Length
Map Info #1
Map Info #2
Map Info #N
….
Octets:
1
1
variable
variable
variable
Map
Control
Channel Identifier
AID #1
AID #2
AID #3
AID #4
….
AID #n
Octets:
1
1
2
2
2
2
2
Sub-IE
IE
N=4 and n=4 were used for comparison.
 Sub-IE length = 10 octets. IE length = 42 octets.
Control flags: 4bits
No. of AID: 4bits (up to 16)
Note: This figure is just for assumption for performance comparisons. It’s not for frame format proposal.

## Slide 13: Assumption-2 DL-OFDMA PPDU
L-STF
L-LTF
L-SIG
HEW
SIG-A
HEW-
STF
HEW-
STF
HEW-
STF
HEW-
STF
HEW-
LTF
HEW-
LTF
HEW-
LTF
HEW-
LTF
HEW
SIG-B
HEW
SIG-B
HEW
SIG-B
HEW
SIG-B
PSDU (AP to STA1, 2, 3 & 4)
PSDU (AP to STA5, 6, 7 & 8)
PSDU (AP to STA9, 10, 11 & 12)
PSDU (AP to STA13, 14, 15 & 16)
8us
8us
4us
8us
4us
4us
4us
Note: This figure is just for assumption for performance comparisons. It’s not for frame format proposal.
variable
+
+
+
+
+
+
= 40us
PPDU length [us] = 40 + Data size (per a STA) / Data rate (per 80MHzBW) / 16
MIMO isn’t considered in this assumption.