## Slide 1: Box5 Results of 11ac SS6
Date: 2015-01-12
Authors:

## Slide 2: Abstract
The simplified 1-BSS case of 11ac SS6 has been well calibrated by four companies [1].
This presentation further shows our complete 3-BSS case of 11ac SS6.

## Slide 3: Calibration Scenario - 11ac Scenario 6 [2]
AP A | (0,0)
AP B | (40,20)
AP C | (-40,-20)
STA3 | (7.5+xb, ‑9.5+yb)
STA9 | (7+xb, -7.5+yb)
STA15 | (3+xb, -0.5+yb)
STA21 | (-6.5+xb, -3+yb)
STA27 | (‑6+xb, 2.5+yb)
STA6 | (-5.5+xc,4.5+yc)
STA12 | (7+xc,7+yc)
STA18 | (10+xc,0.5+yc)
STA24 | (3+xc,2.5+yc)
STA30 | (9.5+xc,3.5+yc)
STA1 | (5,-9.5)
STA2 | (3.5,7.5)
STA4 | (-4.5,0.5)
STA5 | (-1.5,6)
STA7 | (-9,-5)
STA8 | (-8.5,8.5)
STA10 | (-3,0.5)
STA11 | (-0.5,8)
STA13 | (-4,-4)
STA14 | (7.5,-1)
STA16 | (8,-6)
STA17 | (0,-7.5)
STA19 | (-2.5,-4.5)
STA20 | (0.5,-2)
STA22 | (0,-4.5)
STA23 | (-1.5,7)
STA25 | (3.5,-5)
STA26 | (9,9.5)
STA28 | (-8,-5.5)
STA29 | (1.5,3.5)
Fixed Location and Association

## Slide 4: PHY Parameters
PHY parameters | 
BW | All BSSs at 5GHz [80 MHz, no dynamic bandwidth]
Channel model | TGac D NLOS per link
Shadow fading | iid log-normal shadowing (5 dB standard deviation) per link
Data Preamble Type | [5GHz, 11ac], duration is considered.
STA TX Power | 15 dBm per antenna
AP TX Power | 20 dBm per antenna
AP number of TX/RX antennas | 1/1
STA number of TX /RX antennas | 1/1
AP antenna gain | 0 dBi
STA antenna gain | -2 dBi
Noise Figure | 7dB
CCA threshold | -70dBm/80MHz (measured after large-scale fading)
Rx sensitivity | -82dBm/80MHz (a packet with lower rx power is dropped)
Link Adaption | Fixed MCS =7
Channel estimation | ideal
PHY abstraction | RBIR, BCC [3, 4]
Channel correlation | Same as defined in the used channel model

## Slide 5: MAC Parameters
[
MAC parameters | 
Access protocol | [EDCA, AC_BE with default parameters] [CWmin = 15, CWmax = 1023, AIFSn=3 ]
Queue length | A single queue for each traffic link is set inside AP/STA sized of 2000 packets
Traffic type | UDP CBR with rate 10^8bps
MPDU size | 1540 Bytes (1472 Data + 28 IP header + 40 MAC header)
Aggregation | [A-MPDU / max aggregation size / BA window size, No A-MSDU, with immediate BA], Max aggregation: 64 MPDUs with 4-byte MPDU delimiter
Max number of retries | 10
Beacon | Disabled
RTS/CTS | OFF
Traffic direction | DL Only, UL only and mixed DL&UL
Throughput metric | Histogram of per non-AP STA throughput (received bits/overall simulation time)
*Please refer to [5] for more info about how to model these parameters.

## Slide 6: Traffic Flow Model
STA | DL | UL | STA | DL | UL
STA1 | y | y | STA23 | n | y
STA2 | y | y | STA25 | y | y
STA4 | y | y | STA26 | y | y
STA5 | y | y | STA28 | y | y
STA7 | y | y | STA29 | y | y
STA8 | y | y | STA3 | y | y
STA10 | y | n | STA9 | y | n
STA11 | y | n | STA15 | y | n
STA13 | y | n | STA21 | n | y
STA14 | y | n | STA27 | y | y
STA16 | y | n | STA6 | y | y
STA17 | y | n | STA12 | y | n
STA19 | y | n | STA18 | y | n
STA20 | y | n | STA24 | n | y
STA22 | n | y | STA30 | y | y
“y” means having DL/UL traffic flow; “no” means not having DL/UL traffic flow
DL/UL traffic assigned for each STA [2]

## Slide 7: One BSS Test (1/2)
Upright corner BSS B (STAs 3, 9 ,15, 21, 27)
  DL only, UL only and mixed DL&UL (STA rate in Mbps)
  The same traffic is attached to each STA
DL thrpt = 256.48 Mbps
UL thrpt = 222.01 Mbps

## Slide 8: One BSS Test (2/2)
DL thrpt = 49.37 Mbps
UL thrpt = 168.99 Mbps
Total thrpt = 218.36 Mbps
DL still has uniform rate distribution among STAs
UL still has similar trend as that in UL-only case
Similar observation was made in [6]

## Slide 9: 3-BSS Test (1/2)
BSSA thrpt = 70.60 Mbps
BSSB thrpt = 107.10 Mbps
BSSC thrpt = 118.40 Mbps
TOTAL = 296.10 Mbps
Each BSS has uniform STA rate
BSS B and BSS C have similar throughput higher than BSS A has
  AP A can hear both AP B and AP C in the most of time
  AP B and AP C cannot always hear each other
  If 3 APs could always hear each other, each AP should have equal access probability and each BSS should have similar DL throughput

## Slide 10: 3-BSS Test (2/2)
BSSA thrpt = 80.45 Mbps
BSSB thrpt = 81.96 Mbps
BSSC thrpt = 123.21 Mbps
TOTAL = 285.62 Mbps
DL：
BSSA thrpt = 7.19 Mbps
BSSB thrpt = 42.96 Mbps
BSSC thrpt = 29.91 Mbps
DL TOTAL = 80.06 Mbps
UL：
BSSA thrpt = 43.48 Mbps
BSSB thrpt = 57.57 Mbps
BSSC thrpt = 87.50 Mbps
UL TOTAL = 188.55 Mbps
DL & UL thrpt = 268.61 Mbps
Previous observations of uniform DL rate and distance-related UL rate still hold true.
But it is hard to justify whether the throughput ratio among BSSs is correct or not.
More analysis and comparison are required by companies.

## Slide 11: Summary
Four companies have been already able to provide aligned Box5 results of the simplified 1-BSS case of 11ac SS6.
However, for the 3-BSS case different results were observed by those companies.
We showed our 3-BSS results for comparison and we hope more companies could prepare their results so that we can have more sources for calibration.

## Slide 12: Reference
[1] 11-15/0051r0 Box5 Calibration Results
[2] 11-09/0451r16 TGac Functional Requirements and Evaluation Methodology
[3] 11-14/0571r6 Evaluation Methodology
[4] 11-14/1176r0 PHY Abstraction Tables for 11ax System Level Simulation
[5] 11-14/1523r4 Offline Discussion Minutes of SLS Calibration
[6] 11-14/1392r2 Simulation Results for Box5 Calibration