## Slide 1: Uplink RTS/CTS Control
Date: 2015-01-05
Authors:

## Slide 2: Introduction
RTS/CTS is an optional mechanism in 802.11 to mitigate collisions from hidden nodes
It is also used as a protection mechanism and to distribute the NAV
The use of RTS/CTS is controlled by the MIB parameter dot11RTSThreshold
  Always use RTS/CTS
  Never use RTS/CTS
  Use RTS/CTS, conditional on length of PSDU

## Slide 3: Autonomous use
APs and STAs could also decide to use RTS/CTS as a function of observed channel conditions
  If interference from hidden nodes is suspected, use RTS/CTS
  Otherwise, transmission overhead can be reduced by not using it
Autonomous use is very useful in OBSS environments
  Part of effective rate control/medium access
  Adapt to presence of interference

## Slide 4: What’s missing?
Current use of RTS/CTS is either configured through the MIB or is done autonomously
In dense environments, configuration control by the AP can help the overall interference situation
  AP may have better view of the network situation
  AP could control the use of RTS/CTS for STAs associated with the AP in a way that optimizes network resources
Add a mechanism to the 802.11 standard to enable configuration by the AP of use of RTS/CTS by the STA, on a per-STA basis

## Slide 5: Possible implementation
Define new information element
  “Uplink RTS/CTS Control element”
In its simplest form, such an element could look like:
  With “RTSThreshold” having a similar interpretation to the MIB variable “dot11RTSThreshold”.
This IE can be used for individual configuration of a STA or included in e.g. Beacon
Element ID
Length
RTSThreshold
Octets:
1
1
2

## Slide 6: Possible implementation (2)
The previous slide shows only the simplest possible IE, reusing the format used in current MIB control
Other formats are possible, e.g.:
  Use TXTIME rather than PSDU size
  Add extra information, e.g.: different TXTIME for 1st transmission and subsequent retransmissions
  ….
Element ID
Length
TXTIME
Octets:
1
1
TBD
Element ID
Length
TXTIME 1st transmission
Octets:
1
1
TBD
TXTIME retransmissions
…

## Slide 7: Individual configuration of STA
802.11 defines Action frame formats for wireless network management (WNM)
  See 8.5.14 in 802.11-2012 or 8.6.14 in P802.11REVmc_D3.3
  WNM Action frame serves a variety of Wireless Network Management purposes
  WNM Action field values 29-255 currently unused
Details:
  Category = WNM
  WNM Action = newly defined WNM Action field value
  Uplink RTS/CTS Control Element = newly defined information element
Category
Uplink RTS/CTS Control Element
WNM Action

## Slide 8: In Summary
We propose to provide a mechanism to allow the AP to control the RTS/CTS policy for associated STAs
A possible implementation involves:
  Definition of dedicated information element
    Examples given, but details to be determined
  New Action frame type of Category WNM
  IE could also be included in Beacon

## Slide 9: Straw Poll
Do you support adding a mechanism that allows the AP to individually configure the use of RTS/CTS by its associated STAs?