## Slide 1: FPS Network Traffic Model
Date: 2014-11-02
Authors:

## Slide 2: Abstract
The purpose of this presentation is to provide network traffic details of multiplayer First Person Shooter (FPS) online games. Modern popular FPS games present unique challenges when it comes to network traffic. From this profile we can cooperatively develop a simulation that can be incorporated into (Simone’s Simulation document).

## Slide 3
Characteristics of most FPS games
  Low bit-rate
  Sensitive to the impacts of delay(latency) and Jitter [3] [6] [7]
  High frequency of small packets (UDP)
  Short Duration (matches lasting around 10 min.)
  Client-Server Architecture
  Sensitive to QoS requirements[3][5]

## Slide 4
Architecture – Dedicated Server
The dedicated server model provides geographically dispersed servers to host the game matches with optimal network paths. Some implementations[1] use virtual servers to provide the necessary matchmaking and virtual world state services while others use a combination of physical dedicated servers and console servers.

## Slide 5
Typical modern console game 18 player match (Dedicated Server)

## Slide 6
Architecture – Console Server
The console server model elects one of the consoles to host the game and synchronize the other consoles throughout the match. This console also plays the game as well. Statistics are still managed by centralized servers, but the majority of the network traffic is handled by the consoles. This model has key economic advantages as there does not need to be as many dedicated servers in order to host all the games and utilizes the consoles network bandwidth which lowers bandwidth costs as well.

## Slide 7
Typical modern console game 18 player match (Console Server)

## Slide 8
Client / Server Communications
The client to server communications averages will vary for any specific FPS game as will the server to client communication.
FPS games all have delay sensitivity (latency and jitter) that creates severe consequences to the quality of gameplay. (e.g. the player can lose the game due to delays in communications).
Network requirements for FPS games will increase by the time 802.11ax is deployed. Earlier IEEE and other supporting studies show a 50ms round trip tolerance. (e.g. 50ms bursts from the server) [2][4] We can anticipate the 50ms threshold to be around 25-30ms as 802.11ax is released.

## Slide 9
Chart: FPS Client Packets/sec

## Slide 10
Chart: FPS Client Bits/Sec

## Slide 11
Chart: FPS Server Packets/sec

## Slide 12
Chart: FPS Server bits/sec.

## Slide 13
Client/Server Packet and bandwidth profile
The client to server communications and server to client averages are presented in the table below.
Description | FPS 1 | FPS 2 | FPS 3
Average Client Packets/sec | 29 | 34 | 41
Average Client bits/sec | 37018 | 23118 | 54039
Average Server Packets/sec/client | 10 | 26 | 77
Average Server bits/sec/client | 20489 | 51464 | 269326
Average Server Aggregate Packets/sec | 177 | 248 | 861
Average Server Aggregate bits/sec | 372519 | 625974 | 2396306

## Slide 14
Chart: Comparison of FPS Client Packet Sizes
| 0-19 | 20-39 | 40-79 | 80-159 | 160-319 | 320-639 | 640-1279 | 1280-2559 | 2560-5119 | 5120-4294967295
FPS 1 | 0 | 0 | 15 | 5592 | 5940 | 1 | 20 | 7 | 0 | 0
FPS 2 | 0 | 0 | 16428 | 2608 | 895 | 264 | 100 | 205 | 0 | 0
FPS 3 | 0 | 0 | 859 | 5201 | 229 | 423 | 32 | 96 | 0 | 0

## Slide 15
Chart: Comparison of FPS Server Packet Sizes
| 0-19 | 20-39 | 40-79 | 80-159 | 160-319 | 320-639 | 640-1279 | 1280-2559 | 2560-5119 | 5120-4294967295
FPS 1 | 0 | 0 | 10 | 460 | 3274 | 338 | 27 | 47 | 0 | 0
FPS 2 | 0 | 0 | 4928 | 2121 | 4128 | 5823 | 548 | 1044 | 0 | 0
FPS 3 | 0 | 0 | 1173 | 98 | 5607 | 5814 | 572 | 230 | 0 | 0

## Slide 16: References
[1] Saroj Kar, “Windows Azure: The power behind upcoming game Titanfall for the Xbox One”, Silicon Angle – February 25th, 2014 ; http://siliconangle.com/blog/2014/02/25/windows-azure-the-power-behind-blockbuster-game-titanfall-for-the-xbox-one/
[2] Mark Claypool, David LaPoint, and Josh Winslow. “Network Analysis of Counter-strike and Starcraft”, In Proceedings of the 22nd IEEE International Performance, Computing, and Communications Conference (IPCCC), Phoenix, Arizona, USA, April 2003
[3] Amit Sinha, Kenneth Mitchell, Deep Medhi “Network Game Traffic: A Broadband Access Perspective”, Computer Networks, vol. 49, no. 1, pp. 71-83, 2005
[4] L. Pantel, L. Wolf, “On the impact of delay on real-time multiplayer games”, Proc. International Workshop on Network and Operating System Support for Digital Audio and Video (NOSSDAV) (2002) 23-29
[5] Tristan Henderson, Saleem Bhatti “Networked games — A QoS sensitive application for QoS insensitive users?”, ACM SIGCOMM 2003 Workshops August 25 & 27, 2003, Karlsruhe, Germany
[6] Rahul Amin, France Jackson, Juan Gilbert, Jim Martin “Assessing the Impact of Latency and Jitter on the Perceived Quality of Call of Duty Modern Warfare 2”,
[7] Kjetil Raaen, “Latency Thresholds for Usability in Games”
[8] Mark Claypool, Kajal Claypool, “Latency Can Kill: Precision and Deadline in Online Games” , February 22–23, 2010, Phoenix, Arizona, USA.