## Slide 1: Consideration on UL-MU overheads
Date: 2015-01-12
Authors:

## Slide 2: Abstract
This presentation considers impact of UL-MU overheads.

## Slide 3: UL-MU
UL-MU is more difficult than DL-MU because STAs have to synchronize their transmissions.
The easiest way to achieve synchronization is by an AP’s support.
But the AP doesn’t really know which STA has data to transmit.
To find out STAs’ transmission demands, asking one by one is the steadiest way, but that will be a large overhead.
On the other hand, if we can do UL MU transmission for data, then response frames can also be in MU transmission.

## Slide 4: UL-MU
Assume to divide into 3 phases for UL-MU transmission.
Initial phase
UL data transmission phase
DL response phase

## Slide 5: Initial phase
Assume two approaches
AP
STA 1
STA 2
STA N_m
…
Poll
N_m: number of STAs multiplexed (4)
Inquiry
Resp.
Poll
…
≒RTS
≒CTS
Note: above conventional frames were used as substitutes for throughput calculation (may be too convenient)
ref. doc.11-14/0598
Inquiry
Resp.
Inquiry
Resp.
≒QoS CF-Poll
AP asks STAs one by one if they have Tx demands
method 1
method 2
TxReq
to N_m
STAs
…
≒RTS
≒CTS
Both exchanges in legacy rate (24 Mbps)

## Slide 6: DL response phase
Assume two approaches
AP
STA 1
STA 2
STA N_m
…
BA
BA to all N_m STAs by DL-MU
N_m: number of STAs multiplexed (4)
BAR
BA
BAR
BA
BAR
BA
…
method A
method B
…
All exchange in legacy rate (24 Mbps)

## Slide 7: Comparison cases
Initial phase
UL data transmission phase
DL response phase
method 1
method 2
method A
method B
Throughput comparison on DL response phase methods (method 1-A and 1-B)
Throughput comparison on initial phase methods (method 1-B and method 2-B)

## Slide 8: Throughput calculation
N_m: number of STAs multiplexed (and also inquired for method 1) (4)
assumed OFDMA using short GI for MU transmission
TXOP limit = 0
20 MHz bandwidth, 1SS, MCS 8
  assumed 24 us for HE preamble part (+4 us to VHT preamble)
full buffer, error free

## Slide 9: Throughput comparison on DL response phase methods
Initial phase: method 1
DL response phase: method A vs. method B

## Slide 10: Throughput comparison on initial phase methods
Initial phase: method 1 vs. method 2
DL response phase: method B

## Slide 11: From the results…
DL BA responses after UL-MU transmission should be multiplexed (in some way, such as transmit in DL MU or extend BA frame format to carry multiple STAs’ responses).
Initial phase prior to UL-MU transmission should be simple. Need to find a more rough way to grasp or estimate TX demands.

## Slide 12: Straw Poll
Do you agree to include in the specification framework a mechanism by which DL BA/ACKs, in responses to UL MU transmission, are multiplexed
  eg. DL MU-MIMO, DL-OFDMA, single PSDU
  Yes: 60
  No: 1
  Abstain: 51