## Slide 1: Simulation Results of Box5
Date: 2015-01-12
Authors:
Name | Affiliation | Address | Email
Ke Yao | ZTE |  | yao.ke5@zte.com.cn
Ruimei Li | ZTE |  | li.ruimei@zte.com.cn
Zhiqiang Han | ZTE |  | han.zhiqiang1@zte.com.cn
Bo Sun | ZTE |  | sun.bo1@zte.com.cn
Kaiying Lv | ZTE |  | lv.kaiying@zte.com.cn
Yonggang Fang | ZTE |  | yfang@ztetx.com
Yakun Sun | Marvell |  | yakunsun@marvell.com
Meng Yang | CATR |  | yangmeng1@catr.cn

## Slide 2: Abstract
  This submission provides simulation results for Box-5 calibration.
  We agree to use the assumptions about preamble detection and other issues like receiving procedure in [2].
  Some further details in our simulation are listed in the following slides.
  We also compare our results with some other companies.

## Slide 3: Simulation settings
The texts marked in green are our settings
  Box5 calibration scenario
    Use 11ac simulation scenario 6 (Enterprise OBSS networks) as an easy-to-start point as suggested in [1].
  Preamble model
    Take the whole preamble as a standalone sub-frame
    Use PHY abstraction for preamble PER prediction
    not combine the duplicated parts in preamble among multiple 20MHz
    For calibration, the packet length in bytes used in PER computation is calculated based on the assumption of 3-byte/4us (MCS0). For example, the duration of preamble in 11ac is 40us, then the length is (40/4*3)=30 bytes.
  PHY abstraction
    Block-wise RBIR based PHY abstraction as suggested in [6]

## Slide 4: Simulation settings (continued)
  Control frame detection
    Take the whole control frame as a standalone sub-frame
    Use PHY abstraction for the PER prediction
    MCS0 is used
  Traffic Initialization
    To avoid collision storm at the beginning of the simulation, the start time of each traffic is randomized. It means that the start time of every traffic link is equal to a constant time plus a random time, and the random time is a (0, 2s) uniformly distributed random variable.
  Receiving procedure and CCA status
    see next

## Slide 5: Receiving Procedure
Receiver will be locked by the first-arrived packet, and later-arrived packets are considered as interference.
  Any packet with rx power lower than rx sensitivity is dropped, which does not impact current receiver status;
  Any packet with rx power higher than rx sensitivity will be dealt with that its preamble will be detected;
CCA-SD = -82dBm, CCA-ED= -62dBm
  If preamble passes (successfully detected and rx power is higher than -82 dBm), the receiver continues to receive the rest of the packet, that is to decode each MPDU;
    If a MAC frame is successfully decoded, defer for NAV;
      Apply NAV cancellation for RTS according to the current spec
    Otherwise, set CCA to busy for the entire PPDU duration if rx power is higher than TBD [rx sensitivity or CCA-SD].
      For calibration, set rx sensitivity = CCA-SD
  If preamble fails, the receiver use CCA-ED(-62dBm) to decide whether the channel is idle or not.

## Slide 6: Box5 Calibration Scenario
11ac SS6 – OBSS Enterprise [1]
AP C | (-40,-20)
STA6 | (-5.5+xc,4.5+yc)
STA12 | (7+xc,7+yc)
STA18 | (10+xc,0.5+yc)
STA24 | (3+xc,2.5+yc)
STA30 | (9.5+xc,3.5+yc)
AP A | (0,0)
STA1 | (5,-9.5)
STA2 | (3.5,7.5)
STA4 | (-4.5,0.5)
STA5 | (-1.5,6)
STA7 | (-9,-5)
STA8 | (-8.5,8.5)
STA10 | (-3,0.5)
STA11 | (-0.5,8)
STA13 | (-4,-4)
STA14 | (7.5,-1)
STA16 | (8,-6)
STA17 | (0,-7.5)
STA19 | (-2.5,-4.5)
STA20 | (0.5,-2)
STA22 | (0,-4.5)
STA23 | (-1.5,7)
STA25 | (3.5,-5)
STA26 | (9,9.5)
STA28 | (-8,-5.5)
STA29 | (1.5,3.5)
Fixed Location and Association
AP A | (0,0)
AP B | (40,20)
AP C | (-40,-20)
AP B | (40,20)
STA3 | (7.5+xb, ‑9.5+yb)
STA9 | (7+xb, -7.5+yb)
STA15 | (3+xb, -0.5+yb)
STA21 | (-6.5+xb, -3+yb)
STA27 | (‑6+xb, 2.5+yb)

## Slide 7: 11ac SS6 Traffic Flow Model
DL/UL traffic assigned for each STA
STA | DL | UL | STA | DL | UL
STA1 | y | y | STA23 | n | y
STA2 | y | y | STA25 | y | y
STA4 | y | y | STA26 | y | y
STA5 | y | y | STA28 | y | y
STA7 | y | y | STA29 | y | y
STA8 | y | y | STA3 | y | y
STA10 | y | n | STA9 | y | n
STA11 | y | n | STA15 | y | n
STA13 | y | n | STA21 | n | y
STA14 | y | n | STA27 | y | y
STA16 | y | n | STA6 | y | y
STA17 | y | n | STA12 | y | n
STA19 | y | n | STA18 | y | n
STA20 | y | n | STA24 | n | y
STA22 | n | y | STA30 | y | y
“y” means having DL/UL traffic flow; “no” means not having DL/UL traffic flow

## Slide 8: Box-5 PHY Details
PHY parameters | 
BW | All BSSs at 5GHz [80 MHz, no dynamic bandwidth]
Channel model | TGac D NLOS per link
Shadow fading | iid log-normal shadowing (5 dB standard deviation) per link
Data Preamble Type | [5GHz, 11ac], always decoded correctly after successful reception, duration is considered.
STA TX Power | 15 dBm per antenna
AP TX Power | 20 dBm per antenna
AP number of TX/RX antennas | 1/1
STA number of TX /RX antennas | 1/1
AP antenna gain | 0 dBi
STA antenna gain | -2 dBi
Noise Figure | 7dB
CCA threshold ( CCA-SD) | -82dBm (measured across the entire bandwidth after large-scale fading)
Rx sensitivity | -82dBm (a packet with lower rx power is dropped)
ED threshold (CCA-ED) | -62dBm
Link Adaption | Fixed MCS =7 (292.5Mbps)
Channel estimation | ideal
PHY abstraction | RBIR, BCC [1, 5]
Channel correlation | Independent or time-correlated channel per packet

## Slide 9: MAC Parameters
MAC parameters | 
Access protocol | [EDCA, AC_BE with default parameters] [CWmin = 15, CWmax = 1023, AIFSn=3]
Queue length | 2000 packets length multiplied by the STA number inside AP; 2000 packets length inside STA
Traffic type | UDP CBR with rate 10^8bps. The same traffic is attached to each STA or AP.
MPDU size | 1530 Bytes (1464 MSDU + 36 UDP、IP、LLC header + 30 MAC header)
Aggregation | [A-MPDU / max aggregation size / BA window size, No A-MSDU with immediate BA], Max aggregation: 64 MPDUs with 4-byte MPDU delimiter (with 2 bytes padding)
Max number of retries | 10
Beacon | Disabled
RTS/CTS | OFF
Traffic direction | UL Only, DL only, Mixed DL & UL
Throughput metric | CDF or Histogram of per non-AP STA throughput (received bits/overall simulation time)

## Slide 10: One BSS Test Result
BSS B (STAs 3, 9, 15, 21, 27)
Throughput (Mbps):
  DL：252.74
  UL：222.02
  Comparisons with other companies[1][3][4][5] are in the next 2 slides.
Throughput (Mbps) | ZTE | HUAWEI[1] | LGE[4] | MARVELL[5]
BSS B (DL only) | 252.74 | 256.48 | 254.93 | 234
BSS B (UL only) | 222.02 | 222.01 | 206.66 | 263

## Slide 11: DL only
Chart: 
| 3 | 9 | 15 | 21 | 27
Huawei | 51.09 | 51.55 | 51.05 | 51.42 | 51.37
LG | 51.05 | 50.97 | 51.11 | 50.7 | 51.1
MRVL | 52 | 52.68 | 52.68 | 52.51 | 52.81
NTT | 49.92 | 50.08 | 49.95 | 50.04 | 50.24
ZTE | 50.75 | 49.77 | 49.31 | 50.81 | 48.47
1-BSS DL-only results from five companies show similar trend. We have slightly bigger fluctuant results

## Slide 12: UL only
Chart: 
| 3 | 9 | 15 | 21 | 27
Huawei | 40.83 | 45.4 | 48.49 | 43.29 | 44.06
LG | 36.83 | 39.86 | 48.95 | 42 | 39.01
MRVL | 37.74 | 41.15 | 51.52 | 46.6 | 44.83
NTT | 42.79 | 44.86 | 48.92 | 40.4 | 42.21
ZTE | 40.92 | 39.97 | 51.61 | 44.67 | 44.85
1-BSS UL-only results from five companies show similar trend and aligned within an acceptable range.

## Slide 13: Three BSSs Test Result -- DL only
BSS A (STAs 1, 2, 4, 5, 7, 8, 10, 11, 13, 14, 16, 17, 19, 20, 25, 26, 28, 29)
BSS B (STAs 3, 9 ,15, 27)
BSS C (STAs 6, 12,18, 30)
Throughput (Mbps):
  BSS A: 71.87
  BSS B: 127.96
  BSS C: 111.62
  Total: 311.45

## Slide 14: Three BSSs Test Result -- DL only
Compared with other companies [1][4][5]:
  The results of ZTE are within the others except that LGE whose results is quite different.
  In addition, by comparing histograms from the four companies we find that the distribution tendency of throughput for each BSS are quite similar.
  Each BSS has nearly a uniform STA rate
Throughput (Mbps) | ZTE | HUAWEI | LGE[4] | MARVELL
BSS A | 71.87 | 70.6 | 15.87 | 74.70
BSS B | 127.96 | 107.1 | 178.01 | 128.71
BSS C | 111.62 | 118.4 | 172.28 | 101.34
Total | 311.45 | 296.1 | 366.16 | 313.56

## Slide 15: Three BSSs Test Result -- DL only
Observations:
  BSS A shows the lowest performance.
    It’s because that BSS A is in the middle of the square thus it’s interfered by both BSS B and BSS C. Moreover, there are 20 STAs in BSS A while each other BSS has only 5 STAs.
  DL performance of each BSS has uniform distribution.
  The area throughput of 3 OBSSs is improved by about 23% compared to that of 1 BSS case.
  Note that the ARP process may be an issue which affects alignment of throughputs from different companies.
    In our simulation, the time of ARP process is included in the time of statistics.

## Slide 16: Three BSSs Test Result -- UL only
BSS A (STAs 1, 2, 4, 5, 7, 8, 22, 23, 25, 26, 28, 29)
BSS B (STAs 3, 21, 27)
BSS C (STAs 6, 24, 30)
Throughput (Mbps):
  BSS A: 65.02
  BSS B: 105.21
  BSS C: 138.01
  Total: 308.24

## Slide 17: Three BSSs Test Result -- UL only
Compared with other companies [1][4][5]:
  Our results are within the others except the BSS A.
  By comparing histograms from the four companies we find that the distribution tendency of throughput for each BSS are quite similar.
  However, there are still large gaps among different companies.
Throughput (Mbps) | ZTE | HUAWEI | LGE[4] | MARVELL
BSS A | 65.02 | 80.45 | 83.84 | 149.94
BSS B | 105.21 | 81.96 | 112.87 | 121.44
BSS C | 138.01 | 123.21 | 148.61 | 139.27
Total | 308.24 | 285.62 | 345.32 | 410.65

## Slide 18: Three BSSs Test Result -- UL only
Observations:
  BSS A shows the lowest performance.
    Same reason as DL-only case.
  The distribution of UL performance of each BSS is not uniform distribution any more.
  The area throughput of 3 OBSSs is improved by about 38% compared to that of 1 BSS case.

## Slide 19: Three BSSs Test Result -- DL&UL
Throughput (Mbps):
  BSS A: 60.92 (DL:14.19, UL:46.73)
  BSS B：129.74 (DL:81.64, UL:48.10)
  BSS C：130.30 (DL:36.22, UL:94.08)
  Total：320.96 (DL:132.05, UL:188.91)

## Slide 20: Three BSSs Test Result -- DL&UL
Compared with other companies [1][7]:
  BSS A: the results of ZTE is highest.
  BSS B and BSS C: the results of ZTE are in the middle.
  By comparing histograms we find that the distribution tendency of area throughput of 3 OBSSs are quite similar.
Throughput (Mbps) | ZTE | HUAWEI | LGE[7]
BSS A | 60.89 | 50.67 | 49.18
BSS B | 129.75 | 100.53 | 152.38
BSS C | 130.31 | 117.41 | 148.39
Total | 320.95 | 268.61 | 349.95

## Slide 21: Three BSSs Test Result -- DL&UL
Observations:
  BSS A shows the lowest performance
    Same reason as DL only and UL only cases.
  The distribution of DL&UL performance of each BSS is not uniform distribution any more.

## Slide 22: Summary
Provide our Box 5 simulation results and compare with some other companies.
1-BSS case and 3-OBSS DL-only case seem to be aligned.
For 3-OBSS UL-only and DL&UL mixed cases, results from different companies have not converged to a stable state, our results are within them.
The distribution tendency of area throughput of 3-OBSS are similar among some companies.
More efforts are needed for calibration of box 5, especially for multi-OBSS cases.

## Slide 23: References
[1] 11-15-0053-00-00ax-box5-results-of-11ac-ss6.
[2] 11-14-1523-03-00ax-offline-discussion-minutes-of-sls-calibration
[3] 11-15-0051-00-00ax-box5-calibration-results
[4] 11-14-1392-04-00ax-simulation-results-for-box-5-calibration
[5] 11-14-1419-00-00ax-sls-box5-calibration-results-and-discussions
[6] 11-14-1388-01-00ax-consideration-on-per-prediction-for-phy-abstruction
[7] 11-14-1392-01-00ax-simulation-results-for-box-5-calibration