## Slide 1: Power Saving Proposal
Date: 2015-01-11
Authors:

## Slide 2: Abstract
This document contains a proposal for TGak for handling power saving state STAs

## Slide 3: The Problem
GLK intends to (optionally) use multicast frame delivery, for bandwidth efficiency
GLK has been modified to support “mixed mode” BSSs, with simultaneously both GLK and non-GLK STA links to the AP
Under current 802.11 wording, if any non-AP STA enters power save state, the AP _must_ buffer group addressed traffic, and only deliver at DTIMs
Thus, any non-AP STA (including a legacy, non-GLK STA) entering power save state will introduce delay/jitter in downlink traffic for _all_ non-AP STAs, which is much larger than generally acceptable on a bridge link

## Slide 4: The Proposal
Within a GLK-capable AP, divide the downlink, group addressed Data traffic into two categories: the traffic destined for non-GLK STAs (that is, using a non-GLK link), and traffic destined for GLK STAs (that is using GLK links)
These traffic classes are easily separable, as the only group addressed traffic that can use a GLK link are SYNRA MPDUs, and no non-GLK link can carry SYNRA addressed frames.
Treat all non-GLK (non-SYNRA) group addressed traffic using existing power save rules (buffer until a DTIM)
Do not buffer any GLK (SYNRA) group addressed traffic, rather buffer for delivery as normal
All non-Data traffic is delivered using existing power save methods, independent of STA/link types

## Slide 5: Power Save for GLK STAs
Handling GLK non-AP STAs in power save:
  To allow GLK non-AP STAs to use power save, when that is appropriate, continue to support the power save signaling from GLK STAs as per existing rules
  However, when a GLK STA enters power saving state, the effect at the AP is to stop delivering any traffic to that STA using SYNRA (or any other group addressing, for that matter)
  All traffic to a power save state GLK non-AP STA will be delivered with the individually addressed method
  All SYNRA traffic transmitted in the BSS (for any set of STAs) must exclude all power save GLK STAs, using the SYNRA subsetting methods.

## Slide 6: Text changes
Subclause 10.2 has most of the text for power saving operation
10.2.2 covers non-DMG, non-IBSS, non-MBSS power saving
Later subclauses (10.2.3, 102.4 and 10.2.6) cover IBSS, MBSS and DMG
GLK can apply to all these cases
Therefore, suggest a new subclause, 10.2.7, for power save operation by a GLK-capable AP. The new subclause can reference the existing subclauses for the “legacy” operation, and describe in detail only the GLK cases, as outlined above

## Slide 7: Straw Poll
Are you in support of this power save proposal?
  Yes
  No
  Abstain