## Slide 1: Uplink MU Transmission and Coexistence
Date: 2015-01-12
Authors:
Name | Affiliations | Address | Phone | email
Reza Hedayat Young Hoon Kwon Yongho Seok Vida Ferdowsi | NEWRACOM | 9008 Research Drive, Irvine, CA 92618 |  | reza.hedayat at newracom.com younghoon.kwon at newracom.com yongho.seok at newracom.com vida.ferdowsi at newracom.com
Reza Hedayat, NEWRACOM

## Slide 2: Summary
TGax SFD considers UL MU transmissions such as UL OFDMA and UL MU MIMO, which is expected to offer good medium utilization
Compared to existing SU and DL MU, UL MU transmission is unique due to multiple STAs participating in forming a single PPDU
This contribution focuses on the issues that should be considered for UL MU in order to obtain best coexistence in BSS/OBSS scenarios. Particularly, the focus is on channel sensing in presence of UL MU frames

## Slide 3: SU vs UL MU Transmission
TGax is considering UL MU transmissions such as UL OFDMA and UL MU MIMO
While UL MU transmissions are expected to increase medium utilization, they also bring many challenges since multiple STAs participate in forming a single PPDU
Things become more complicated since some of the PPDU attributes may not a priori known to all of the STAs participating in forming UL MU PPDU

## Slide 4: SU vs UL MU Transmission
An important aspect in 802.11 operation is CSMA/CA where all nodes sense the medium and verify whether the medium is busy or idle based on which they decide whether to prepare to access the medium or not
In SU transmission and DL MU transmission, since the frame is sent by a single node, it is straightforward how the neighboring nodes interpret the state of the medium
However, in UL MU transmission, multiple nodes participate in forming the UL MU frame, hence the assessment of the status of the medium could become tricky. Thus an important aspect in UL MU transmissions is to make sure that unintended STAs have accurate channel sensing regarding the ongoing UL MU frame on the entire BW

## Slide 5: Channel sensing in presence of UL MU frames
Regarding UL MU PPDUs, we assume that TGax might adopt mechanisms that specify the length of the PPDU in either L-SIG or any of 11ax-SIG symbols.
Moreover, in an UL MU exchange, AP of the STAs might engage in classic RTS/CTS exchange or any new form of it suited for MU exchange
However in addition to above mechanisms, operation of UL MU MIMO and UL OFDMA might get affected by unintended STAs that might start assessing the medium somewhere after the PLCP part of the UL MU PPDU
The situations described in next slides illustrate the situation where artificial hidden nodes are created due to narrow-band transmissions of some or all of the STAs that participate in forming the UL MU PPDU

## Slide 6: Channel sensing in presence of UL MU MIMO frames
In the case of UL MU MIMO if each STA occupies the same bandwidth as others then there would be no channel sensing ambiguity from the neighborhood of each participating STA, even if a STA starts sensing the medium in the middle of the PPDU
However if an UL MU MIMO PPDU is formed in a way that some STAs sends their PSDU in narrower bandwidth, depending on the location of STAs forming the PPDU, there could be ambiguity in channel sensing since some unintended neighboring STAs sense energy on narrower bandwidth than others and might assume the medium is available
For instance, assume that an 80MHz UL MU PPDU is formed by several STAs where one or more of those send their PSDU with 40MHz bandwidth. In this case if there are OBSS STAs whose primary channel is different that the primary of the BSS they could sense the medium is idle and attempt to access the medium

## Slide 7: Channel sensing in presence of UL OFDMA frames
In the case of UL OFDMA, depending on the sub-band assignment of the UL OFDMA PPDU, there could be ambiguity in channel sensing in the neighborhood of each participating STA
Since a participating STA in an UL OFDMA PPDU could transmit less or no energy on some 20MHz sub-bands, the coverage area of the STA differs from one 20MHz sub-channel to another
  A STA within the coverage of a transmitting UL OFDMA STA assesses the 20MHz channel the STA occupies is busy; the rest might be assessed as idle
  If this happens to the primary channels then STAs in the BSS might assess the medium is available even though there is an ongoing UL MU OFDMA frame
  If this happens to the non-primary channels then STAs in OBSSs (whose primary channel is different than primary channel of the BSS) might assess the medium is available even though there is an ongoing UL MU OFDMA frame

## Slide 8: Channel sensing in presence of UL OFDMA frames
For instance in the case of UL SU transmission, all the nodes in the coverage area of the transmitter would have correct assessment of status of the medium even if they start assessing the medium in the middle of the frame
  While it is true that some nodes outside of the coverage area of the transmitter might see the medium is available, this case is considered the classic hidden node problem
However, in the case of UL OFDMA things could be different. For instance, in the case of an 80MHz UL OFDMA PPDU with four participating STAs where each STA is assigned one of the 20MHz sub-channels, only the cross-coverage of the four STAs would sense the medium properly (see next slide)
  In other words, the hidden nodes for each participating STA add to the set of the hidden nodes where some subsets of it appears hidden to some portions of the bandwidth of the UL OFDMA frame

## Slide 9: Channel sensing in presence of UL OFDMA frames
LEG STF
LTF
SIG
11ax
STF
LTF
SIG
20MHz sub-band
20MHz sub-band
20MHz sub-band
20MHz sub-band
AP
LEG STF
LTF
SIG
11ax
STF
LTF
SIG
20MHz sub-band
20MHz sub-band
20MHz sub-band
20MHz sub-band
LEG STF
LTF
SIG
11ax
STF
LTF
SIG
20MHz sub-band
20MHz sub-band
20MHz sub-band
20MHz sub-band
LEG STF
LTF
SIG
11ax
STF
LTF
SIG
20MHz sub-band
20MHz sub-band
20MHz sub-band
20MHz sub-band
Only STAs in the intersection of the coverage area of all STAs have proper CS of the whole bandwidth
Unintended STAs inside the RED area sense the channel busy for the RED 20MHz sub-band. STAs outside of the RED coverage are hidden nodes wrt the RED sub-band

## Slide 10: Channel sensing in presence of UL OFDMA frames
One solution to obtain correct channel sensing is to manage the sub-band allocation such that a minimum TBD bandwidth is assigned to each STA in each of the 20MHz bands
  This allows each unintended STA to sense the medium correctly across all the 20MHz bands that the UL OFDMA frame occupies
  Additionally, each STA may boost power in each assigned sub-band in each 20MHz channel to partially adjust any possible coverage shrinkage
For instance, in the case of an 80MHz UL OFDMA PPDU with four participating STAs where each STA is assigned total of 20MHz bandwidth, the assigned bandwidth to each STA is distributed to all four 20MHz sub-channels. In such case almost the union of the coverage areas of the four STAs would sense the medium properly (compared to single 20MHz band assignment where only the intersection of the coverage areas sense the medium properly)

## Slide 11: Channel sensing in presence of UL OFDMA frames
The method described in previous slide makes sure that the neighborhood of each participating STA in the UL OFDMA frame has correct channel sensing whether they belong to BSS or OBSS
However the minimum bandwidth assignment per STA per each 20MHz sub-channel can be relaxed so that is applied only to the primary 20MHz channel, or to the primary 40 MHz channel
By above relaxation, at least it is made sure that the STAs of the same BSS interrupt the status of the medium correctly in presence of an ongoing UL OFDMA frame
Also, STAs belonging to OBSS that happen to have their primary 20MHz channel on the same primary channel of the BSS would sense the status of the medium correctly

## Slide 12: Conclusion
CSMA/CA is an important aspect of 802.11 operation that needs to be observed in presence of UL MU MIMO and UL OFDMA frames
UL MU transmissions require additional considerations so that the unintended nodes accurately sense the status of the medium across the whole bandwidth (or at least across the primary channel) in presence of UL MU PPDUs