## Slide 1: UL-OFDMA procedure in IEEE 802.11ax
Date: 2015-01-14
Authors:

## Slide 2: Introduction
UL-OFDMA is included in Spec Framework Document for 11ax [1],[2]
  UL-OFDMA is a key enabling technique to meet the requirement of throughput enhancement
  Number of problem statement and solutions have been discussed in TGax [3], [4], [5], [6], [7]
11ax is aiming to enhance the spectral efficiency
  Finer granularity of bandwidth usage (2.5/5 MHz BW)
  Aggressive wideband operation
In this contribution, issues on UL-OFDMA procedure in 802.11ax, as well as possible solutions will be discussed
  With finer sub-channels, wideband operation, dense OBSS environment

## Slide 3: Issues on UL-OFDMA in 802.11
lack of multiple transmission control mechanism
  When and who to initiate UL-OFDMA?
  Which STA to participate or to be selected?
    Scheduling
  How to protect data transmission(NAV) from multiple groups of hidden nodes
  How to finish the whole procedure
    ACK procedure
How do we support UL-OFMDA in wideband and dense OBSS environment?

## Slide 4: When and who to initiate UL-OFDMA
Timing/power/frequency Synchronization
  AP can calculate the timing/power/frequency differences among STAs
AP centralized initiation
  AP indicates each STA to adjust time/frequency/power differences[5]
  Trigger frame[3]
Periodic or scheduling
  Following beacon period
  Whenever scheduling status meets UL-OFDMA trigger condition
  Depends on target situation, procedure development

## Slide 5: Which STA to participate
AP doesn’t have any information on STAs’ buffer status
Conventional polling mechanism
  Simple, stable, rich information/Large overhead
  UL-request frame[3]
    Each STA sends UL request frame independently to indicate its buffer status to AP
Buffer status feedback
  Buffer status indication with ongoing tx/rx
    Reusing duplicated or reserved field of preamble/header
      Ex) group ID, NSTS, partial AID of UL transmission
    More data, more fragment bit
    Less overhead / limited information

## Slide 6: NAV Protection
Each STA has different hidden nodes group
In order to set NAV for every hidden nodes group, each UL-tx STA must transmit at least one RTS or CTS
  RTS/CTS with 802.11a format
  Legacy STAs cannot read Data frame

## Slide 7: NAV Protection
Serial RTS transmission
  Large overhead
  CTS time out
    Reset NAV if no PHY-RXSTART.indication with a duration of (2 × aSIFSTime) + (CTS_Time) + aPHY-RX-START-Delay + (2 × aSlotTime)
    The hidden nodes group of STA1 won't receive any RXstart. indication within the time limit

## Slide 8: NAV setting using common CTS
① CTS-to-STA group
  Using CTS to prevent hidden nodes group from resetting NAV
  CTS doesn’t have condition for resetting NAV
  Assign a dedicated multicast address for 11ax UL-OFDMA
② Common CTS[3]
  Every UL-OFDMA participants send CTS with identical waveform
    E.g., DA: AP, SA: multicast address for 11ax UL-OFDMA
  Resource allocation acknowledgement might follow

## Slide 9: ACK procedure
Serial ACK transmission
  Large overhead
Sub-channel based ACK
  Less overhead
  Unfairness between Legacy and ax STAs
    STA that received erroneous frame previously has to defer EIFS
    The STA having the shorter EIFS parameter has the higher channel access probability[8]

## Slide 10: ACK procedure using common ACK
Sub-channel based ACK
  Acknowledgement of received data
Common ACK
  Preventing legacy STAs from waiting for EIFS
  Identical waveform

## Slide 11: UL-OFDMA in wideband operation
In dense OBSS environment
  STAs might belong to different OBSSs
AP initiates UL-OFDMA after CCA
  The snapshot of CCA results could be different from each other
  Channel availability
  Which band should be assigned to which STAs?

## Slide 12: UL-OFDMA in wideband operation
STAs should inform AP of both their buffer status and channel availability
Channel availability feedback might also introduce massive overhead

## Slide 13: Code based access
Pseudo random code
  Enhancing CSMA/CA performance via introducing code based contention mechanism[9], [10]
  PRACH, PUCCH, PUSCH in LTE
  CAZAC sequence (Zadoff-chu)
Code access could play a role both for channel availability feedback and buffer status indication
  Every 11ax STA that has uplink data simultaneously sends a chosen code to clear-assessed channels after CTS-to-STA group
Code assignment
  Randomly chosen from code set
  Unique code for each STA

## Slide 14: Comparison of channel availability feedback

## Slide 15: Expected form of UL-OFDMA procedure

## Slide 16: Conclusion
In this contribution, we discussed issues on UL-OFDMA procedure in 802.11ax, as well as possible solutions
UL-OFDMA might cause massive control overhead, and unstable transmission protection
  Due to lack of multiple transmission control mechanism
  Developments or modifications on Scheduling, NAV setting, ACK procedure, channel availability feedback are necessary
We introduced several possible solutions to the discussed issues
  Common CTS/ACK(identical wave form) transmission
    NAV setting, ACK procedure
  Code based access
    Scheduling, CCA feedback

## Slide 17: Reference
[1][14/1453/r2] Spec Framework Proposal
[2][14/1447/r1] Proposed Spec Framework Document for 11ax considering potential tech features
[3][14/1431/r1] Issues on UL-OFDMA
[4][14/1446/r0] Analysis of frequency and power requirements for UL-OFDMA
[5][14/0802/r0] Consideration on UL MU transmission
[6][14/1190/r2] Frame Exchange Control for Uplink Multi-user transmission
[7][14/1232/r1] On Multi-STA Aggregation Mechanism in 11ax
  [8][14/1211/r0] Ack Procedure for OFDMA
  [9][14/0616/r0] CSMA/CA enhancements
  [10][14/1681/r1] 802.11 Tgax PHY Frame Structure Discussion for Enabling New Contention Mechanism

## Slide 18: Straw Poll 1
Do you agree to add to the TG Specification Framework:
x.y.z AP shall indicate UL OFDMA initiation.
Y
N
ABS

## Slide 19: Straw Poll 2
Do you agree to add to the TG Specification Framework:
x.y.z UL OFDMA uplink channels shall be allocated considering STAs’ channel status.
Y
N
ABS

## Slide 20: Straw Poll 3
Do you agree to add to the TG Specification Framework:
x.y.z UL OFDMA shall provide NAV setting mechanism for allocated channels.
Y
N
ABS