## Slide 1
DL-OFDMA Procedure in IEEE 802.11ax
Date: 2015-01-14
Authors:

## Slide 2: Background
Achieving High Efficient WLAN
  In IEEE 802.11ax PAR [1], IEEE 802.11ax should provide methods for efficient use of spectrum resources in dense STAs per BSS.
    Make more efficient use of spectrum resources in scenarios with a high density of STAs per BSS.
    Significantly increase spectral frequency reuse and manage interference between neighboring overlapping BSS (OBSS) in scenarios with a high density of both STAs and BSSs.
  Efficient use of spectrum resource
    Using Multiuser Diversity – OFDMA, UL-MU-MIMO
  Increasing spectral frequency reuse and manage interference between neighboring overlapping BSS (OBSS)
    New Channel usage pattern under dense OBSS scenario – APCH based channel access[2]

## Slide 3: OFDMA
20MHz band based OFDMA and smaller band based OFDMA could be considered
  New preamble and frame structure for sub-band based OFDMA
OFDMA Procedure
  Without RTS/CTS[3]
    New preamble and header include channel-user assignment information
    Full scanning is needed for different header on wider band operation
    Heavy header for Conventional primary channel based scanning
  With RTS/CTS[4]
    Conventional RTS could not provide channel-user assignment information
    Channel-user assignment frame or New type of RTS should be used
  ACK or CTS[4]
    Multiuser ACK or CTS method need to be provided

## Slide 4: Alternative Primary Channel(APCH) based OFDMA
APCH is a new basis channel of channel expansion[2]
11ax Control frames could be transmitted via APCH
  Reducing 11ax Control Frame overhead
  Control frames for APCH operation are transmitted via Conventional Primary Channel
APCH could be allocated statically or dynamically
  Dynamic allocation could enhance performance but need more complexity
  History based allocation, inter AP management based allocation

## Slide 5: APCH based OFDMA
Resource utilization comparison[2]
  CH1 is Primary Channel
  CH3 is APCH
 | Channel (Colored means busy) |  |  |  | Legacy |  |  |  | All available CH |  |  |  | APCH |  |  | 
 | CH1 | CH2 | CH3 | CH4 | CH1 | CH2 | CH3 | CH4 | CH1 | CH2 | CH3 | CH4 | CH1 | CH2 | CH3 | CH4
Case1 |  |  |  | Busy |  |  |  |  |  |  |  |  |  |  |  | 
Case2 |  |  | Busy |  |  |  |  |  |  |  |  |  |  |  |  | 
Case3 |  | Busy |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Case4 |  | Busy |  | Busy |  |  |  |  |  |  |  |  |  |  |  | 
Case5 |  |  | Busy | Busy |  |  |  |  |  |  |  |  |  |  |  | 
Case6 | Busy |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 6: APCH based OFDMA
Channel usage vs busy channel prob. (=0.7)[2]
69%
39%
108%
52%
119%
39%

## Slide 7: APCH based OFDMA
vs All available channel based OFDMA
  All available channel access allows target AP to utilize full available channel just at that time
  All available channel access sustaining primary channel based back-off might degrade OBSS channel usage and frequency reuse
    Throughput/AREA might be degraded
  # of APCH is a factor of channel access aggressiveness
  all available channel based OFDMA = set all channels as APCH(# of APCH == # of capable channels)

## Slide 8: APCH based OFDMA
RTS/CTS procedure
  RTS/CTS exchange could initiate OFDMA transmission[4]
    Protection will prevent Multiuser TX failure but it is hard to protect transmission duration because of multiple points in OFDMA[4]
  Channel-user assignment information(Resource Allocation, RA) need to be provided during RTS/CTS phase
  RTS – RA – MU-CTS – Data – MU-ACK
Assumption
  Each STA could listen its Primary Channel and APCH
  Multiuser and Wideband TX failure is more costly than protection overhead
  # of users or TXOP length might affect RTS/CTS threshold

## Slide 9: APCH based OFDMA
RTS/CTS procedure concept

## Slide 10: APCH based OFDMA Procedure
RTS-to-Self
  Using Legacy RTS frame format
  Transmitter Address(TA) = Receiver Address(RA)
  Multi-user session initiator frame
  11ax STA is ready to receive resource allocation
  Legacy STAs recognize it as a RTS frame and set NAV
Resource Allocation(RA)
  New control frame to support OFDMA
  STA-Channel information
  Different RA frames are transmitted between Primary channel and APCH (Reducing RA overhead)

## Slide 11: APCH based OFDMA Procedure
Resource Allocation(RA)
  Since RI Frame is transmitted right after RTS, NAV setting will be sustained
    A STA which receive RTS could be reset its NAV if no PHY-RXSTART.indication primitive is detected from the PHY during (2 × aSIFSTime) + (CTS_Time) + aPHY-RX-START-Delay + (2 × aSlotTime)[5]
MU-CTS & MU-ACK
  CTS and ACK for supporting Multiuser session
  Following slides show some possible solutions

## Slide 12: APCH based OFDMA Procedure
Cascade CTS/ACK Method
  CTS and ACK overhead increases as the number of sub-band STAs increases

## Slide 13: APCH based OFDMA Procedure
Cascade CTS/ACK Method with Fast ACK
  CTS and ACK overhead increases as the number of sub-band STAs increases(Relatively lower than without Fast ACK case)
  Last Fast ACK could be replaced by Legacy ACK to announce TXOP termination

## Slide 14: APCH based OFDMA Procedure
Cascade CTS/ACK
  Each STA within the Resource Allocation Frame sends CTS frame sequentially
  Using conventional CTS and ACK
Fast ACK
  Fast ACK may not have legacy preamble, only have HEW preamble
  Shorter air time than Conventional ACK
  Fast ACK may not provide any information to legacy STAs

## Slide 15: APCH based OFDMA Procedure
Sub-band CTS/ACK Method
  CTS overhead have only 2 variations, with Sub-band TX case or not
  Common CTS is transmitted by STAs which have transmitted sub-band CTS

## Slide 16: APCH based OFDMA Procedure
Sub-band CTS and ACK
  STAs transmit its CTS via sub-band indicated from RA
  STAs transmit its ACK via sub-band which they receive DATA from
Common CTS and ACK
  Legacy form of CTS and ACK
  Base rate and identical frames
  Transmitted from STAs that participate in OFDMA sub-band transmission
  Provide legacy protection and Legacy NAV update (Early TXOP termination by ACK)
  Common ACK could be eliminated unless Early TXOP termination might be supported

## Slide 17: Conclusions
APCH based OFDMA was presented
  Protection for Multiuser and Wideband operation
  RTS-to-Self as a OFDMA session initiator
  Resource Allocation frame is needed
  Mechanisms for OFDMA RTS/CTS
    RTS – RA – CTS – DATA – ACK structure in order to maximize commonality with the legacy procedure
    Common CTS, common ACK in order to provide NAV operation
We need to discuss about
  Adopting RA frame for OFDMA

## Slide 18: Straw Poll 1
Do you agree to add to the TG Specification Framework:
4.y.z DL OFDMA shall support both basic transmission (without RTS/CTS) and RTS/CTS based transmission.
Y
N
ABS

## Slide 19: Straw Poll 2
Do you agree to add to the TG Specification Framework:
4.y.z DL OFDMA shall transmit STAs’ resource allocation information through all allocated channels.
Y
N
ABS

## Slide 20: Straw Poll 3
Do you agree to add to the TG Specification Framework:
4.y.z DL OFDMA shall provide NAV setting mechanism for allocated channels.
Y
N
ABS

## Slide 21: Straw Poll 4
Do you agree to add to the TG Specification Framework:
4.y.z DL OFDMA shall utilize idle channels without utilizing primary channel.
Y
N
ABS

## Slide 22: Reference
[1] IEEE 802.11-14/0165r1 “802.11 HEW SG Proposed PAR”
[2] IEEE 802.11-14/1437r1 “Efficient Wider Bandwidth Operation in IEEE 802.11ax”
[3] IEEE 802.11-14/1210r1 “HEW PPDU Format for Supporting MIMO-OFDMA”
[4] IEEE 802.11-14/1431r1 “Issues on UL-OFDMA Transmission”
[5] IEEE802.11-2012 section 9.3.2.4