## Slide 1: SYNRA Extended AID list
Date: 2015-01-13
Authors:

## Slide 2: Abstract
This document contains a proposal for TGak to add missing list size and figure for the AID list of the Extended synra Information

## Slide 3: IEEE P802.11ak™/D0.06 , Clause 9.42 SYNRA address filtering operation
    If the SYNRA type is 2, the Extended SYNRA Information is a sequence of two-octets elements each element containing an AID in the 14 LSBs. In this case, the Extended SYNRA Size subfield is the number of elements and only bit B25 of the Extended SYNRA Second subfield is used; bits B26 through B39 are ignored.
SYNRA Type | Description
0 | AID bit array
1 | Extended AID bit array
2 | Extended AID list
3 | Reserved

## Slide 4: The Problem
The max size of the Extended AID list (i.e. max number of AID elements) is not specified
The Extended SYNRA Information field is missing in Fig 9-90
There is no figure for SYNRA Type 2

## Slide 5: The Proposal
Specify a number of AID elements for the Extended SYNRA Information
Add the Extended SYNRA Information field to Fig 9-90
Add Fig 9-92 for SYNRA Type 2

## Slide 6: Figs 9-90 & 9-92