## Slide 1: Report from ETSI TC BRAN#81
Date: 2015-01-14
Authors:

## Slide 2: Abstract
This document contains a summary of the ETSI TC BRAN#81 meeting that took place in Las Palmas, Gran Canaria December 16-19, 2015, with a focus on EN 301 893 comment resolution and revision.

## Slide 3: BRAN Agenda Items
New Work Items (WI)
  ETSI Technical Report (TR) on Coexistence with EESS in 5 GHz
  ETSI TR on Coexistence with ITS and Road Tolling in 5 GHz
  ETSI TR on Coexistence with radiolocation in 5 GHz
  DA2GC in 5 GHz with beamforming antennas
  DA2GC in 5 GHz with fixed antennas
  Revision of EN 301 893 for compliance with the new Radio Equipment Directive (RED)
EN 301 893 - 5 GHz high performance RLAN – Comment Resolution

## Slide 4: The Radio Equipment Directive
Since the early 1990s, all the EU Harmonised Standards for radio equipment have been created in compliance with the R&TTE Directive, governing placement on the market
With the increasing demand for spectrum sharing, the EC had developed new guidelines aimed at improving spectrum efficiency, and addressing issues with the R&TTE Directive
This is scheduled to go into effect in June of 2016, with mandatory compliance in June of 2017
  https://mentor.ieee.org/802.18/dcn/15/18-15-0009-00-0000-ec-radio-equipment-directive.pdf
I plan to supply a summary of the RED and a list of potential issues for new IEEE 802.11 standards

## Slide 5: Summary
Work Items approved
  ETSI Technical Report (TR) on Coexistence with EESS in 5 GHz
  ETSI TR on Coexistence with ITS and Road Tolling in 5 GHz
  ETSI TR on Coexistence with radiolocation in 5 GHz
  DA2GC in 5 GHz with beamforming antennas
  DA2GC in 5 GHz with fixed antennas
WI for EN 301 893 RED compliance includes final resolution of paragraph 4.8.3.2 LBT for Load Based Devices
EN 301 893 v1.7.3 (to become v1.8.1) was approved
  Paragraph 4.8.3.2 maintains the wording from v1.7.1
  Adds an alternate based on inputs from the Wi-Fi industry

## Slide 6: Revision of EN 301 893
The issue with Paragraph 4.8.3.2
  LBT for Load Based Devices of v1.7.1 provided sufficient “adaptivity” to meet EC requirements while 802.11 was the only technology in the band
  The introduction of other technologies in compliance with 4.8.3.2 could severely disadvantage Wi-Fi
    CableLabs, Broadcom and WFA submitted simulations showing this
    Wi-Fi could virtually be excluded where v1.7.1 compliant devices operated
  Exponential backoff, the primary Wi-Fi to Wi-Fi coexistence mechanism not in the text
New DFS test requirement, test uncertainties made approval of v1.7.x necessary at this time

## Slide 7: The Arguments
Wi-Fi industry proponents
  V1.7.1 leaves Wi-Fi vulnerable to unfair sharing
  Simulations by CableLabs, WFA and Broadcom clearly demonstrate this
  Although proposed changes to Paragraph 4.8.3.2 still need to be improved to ensure fair sharing, this first step is needed so that 3GPP LAA-LTE planning is based on a fair approach, not v1.7.1
Others
  No changes should be made until a final solution is available
  Not yet known what LAA-LTE is until their simulations are done, so how can IEEE 802.11 know they will be disadvantaged
  Keep v1.7.1 Paragraph 4.8.3.2

## Slide 8: The Results
The group approved v1.7.3 (to become v1.8.1) with both the v1.7.1 and Wi-Fi industry proposal as alternatives for Paragraph 4.8.3.2
The first draft of the new version will not be written until June of 2015
The new WI, for RED compliance will resolve the 4.8.3.2 duality well before June 2017, when EN 301 893 is out of force
For the next 18 months v1.7.1 vulnerabilities will remain in the Harmonised Standard

## Slide 9: References
Approved v1.7.3 for National voting:
  http://www.ieee802.org/11/private/ETSI_documents/BRAN/05-CONTRIBUTIONS/2014/BRAN(14)000073r1_EN_301_893_HS_5_GHz_RLANs_for_national_voting.zip
The New Work Item
  http://www.ieee802.org/11/private/ETSI_documents/BRAN/05-CONTRIBUTIONS/2014/BRAN(14)000087r5_Revision_of_EN_301_893_to_become_a_HS_under_the_new_RE-Direc.zip
Minutes of the meeting:
  http://www.ieee802.org/11/private/ETSI_documents/BRAN/05-CONTRIBUTIONS/2014/BRAN(14)000092r1_Minutes_of_the_RCWG_sessions_during_BRAN_81.doc
My full report
  https://mentor.ieee.org/802.18/dcn/15/18-15-0002-02-0000-report-from-etsi-tc-bran-81.pptx