## Slide 1: GCR using SYNRA for GLK
Date: 2015-01-13
Authors:

## Slide 2: Abstract
Described the GCR protocol and proposes changes that makes GCR use SYNRA and hence support GLK.
Note that
DMG STAs do not support GCR (Cl. 4.3.20, Cl. 10.24.16.1)
GCR is only supported if dot11RobustAVStreamingImplemented is true, which is true if and only if dot11DMSImplemented and dot11HighThroughputOptionImplemented are true.

## Slide 3: AP functions – GCR modifications
A SYNRA is constructed every time a GLK STA associates. The SYNRA represents an RA that excludes the STA but includes all other STAs in the BSS
  AP constructs as many SYNRAs as there are GLK STAs associated with the AP
  STA’s Group membership is known to the AP (no need to exchange Group Membership Request/Response frames)
  The AP deletes the SYNRA corresponding to the GLK STA when the GLK STA gets disassociated from the BSS
A GCR Service is setup for every SYNRA
  What is the choice of retransmission policy? Block ACK when SYNRA represents a small (< 10) GLK STAs; unsolitied retries, otherwise.
  AP implicitly does the GCR Service setup which may be modified if the AP decides to move between Block ACKs and Unsolicited Retries
  Since GCR Service setup is implicit (no explicit DMS Request from GLK STAs), unsolicited transmission of DMS Response that includes a GCR Response element is needed (this tells the member STAs what retransmission policy is used for the GCR) – Cl. 10.24.16.3.3
Notes: SYNRA type-2 or type-3; why can’t type-3 use a longer (bits 26 thru 39 are available); If SYNRA is the RA where does the Extended SYNRA Information Vector for Type-1 and the Extended SYNRA Information sequence of two-byte octets go in the frame/frame header?
Block ACK for GCR could be used but it may not be effective is the number of GLK STAs represented by the corresponding SYNRA is large.

## Slide 4: AP Functions – GCR Modifications
Support for GLK should imply support for GCR
  The spec mandates it only for dot11GCRActivated implementations
If one or more GLK STAs go into PS mode, the AP will not buffer packets destined to those GLK STAs
  Should buffering be enabled conditionally based on the knowledge AP has on PS?
    Buffer if the PS Duration is short and skip buffering otherwise?
    AP will advertise what it considers is a short PS Duration
    If buffering is enabled GCR-SP delivery allows for low latency delivery of buffered frames.
Notes: GCR-SP transmits GCR group addressed frames at intervals, where the interval between transmissions might be smaller than the beacon interval. Compared to non-GCR-SP, GCR-SP might provide lower delay and jitter.

## Slide 5: GLK STA functions – GCR Modifications
Support for GLK should imply support for GCR
  The spec mandates it only for dot11GCRActivated implementations
Receive and process autonomous DMS Response frames that include a GCR Response element
  Handle corresponding GCR frames received appropriately
    Drop duplicates, respond to BARs, etc
No need for a GCR Concealment Address
  The non-AP STA need not pay attention to the GCR Concealed Address field in the GCR Response from the AP

## Slide 6: GATS
DMS – directed multicast
GCR – unsolicited retries
GCR Advanced – block ACK and GCR-SP
GCR for Mesh
GCR phases -- announcement, setup, modification, and teardown
GCR group addressed MSDUs shall be sent in an A-MSDU when
  Retransmitted via the GCR unsolicited retry or GCR block ack retransmission policies or
  Transmitted via the GCR-SP delivery method.

## Slide 7: Overview of the GCR Protocol
STA
AP/MAP
DMS Request with GCR Request Element
DMS Response with GCR Response Element
DMS Request with GCR Request Element
DMS Response with GCR Response Element
Announce
Teardown
DMS Request with GCR Request Element
DMS Response with GCR Response Element
Setup
.
.
.
GCR transmission of MSDU/A-MSDU

## Slide 8: Overview of the frames
DMS Request – a set of DMS Request elements
DMS Response – a set of DMS Response elements
DMS Request element – a DMS Descriptor List (8.4.2.87)
DMS Response element – a DMS Status List (8.4.2.88)

## Slide 9: DMS Descriptor
DMS Descriptor |  |  |  | Zero or moe |  |  | 
 | DMSID | DMS Length | Request Type | TCLAS elements | TCLAS processing element (optional) | TSPEC element (optional) | Optional subelements
octets | 1 | 1 | 1 | variable | 0 or 3 | 0 or 57 | variable
DMSID – 0 when Request Type is ‘add’; otherwise an AP assigned DMSID is used
Request Type – add/remove/change
TCLAS elements – one or more if the Request Type is ‘add’
Optional subelements – GCR Request
GATS Retransmission Policy – DMS/GCR Unsolicited Retries/GCR Block ACK
GCR Delivery Method – no preference/non-GCR-SP/GCR-SP
GCR Request |  |  |  | 
 | Subelement ID | Length | GATS Retransmission Policy | GCR Delivery Method
octets | 8 | 8 | 4 | 4

## Slide 10: DMS Status
DMSID – An AP assigned DMSID is used
Response Type – Accpt/Denied/Terminate/GCR Advertise
TCLAS elements – one or more if the Request Type is ‘add’
Optional subelements – GCR Response
GATS Retransmission Policy – DMS/GCR Unsolicited Retries/GCR Block ACK
GCR Delivery Method – no preference/non-GCR-SP/GCR-SP
DMS Status |  |  |  |  | Zero or moe |  |  | 
 | DMSID | DMS Length | Request Type | Last Sequence Control | TCLAS elements | TCLAS processing element (optional) | TSPEC element (optional) | Optional subelements
octets | 1 | 1 | 1 | 2 | variable | 0 or 3 | 0 or 57 | variable
GCR Response |  |  |  |  |  | 
 | Subelement ID | Length | GATS Retransmission Policy | GCR Delivery Method | GCR Concealed Address | Schedule Element
Octets | 1 | 1 | 0 or 1 | 0 or 1 | 0 or 6 | 0 or 14