## Slide 1: GCR using SYNRA for GLK
Date: 2015-01-13
Authors:

## Slide 2: Abstract
Describes a GLK-GCR which is a simplified GCR service for GLK.

## Slide 3: AP functions
A GLK-GCR Service is setup for every SYNRA
  What is the choice of retransmission policy?
    Block ACK when SYNRA represents a small (< 10) GLK STAs; unsolicited retries, otherwise.
  AP implicitly does the GLK-GCR Service setup for each SYNRA which may be modified if the AP decides to move between Block ACKs and Unsolicited Retries
    [Re]Association response include the GLK-GCR Response element
      may also include a BA Agreement element if the GLK-GCR retransmission policy is BlockACK
    Notifications can be groupcast to all affected GLK STAs using current GLK-GCR retransmission policy
      Useful when GLK-GCR retransmission policy changes

## Slide 4: AP Functions
If one or more GLK STAs go into PS mode, the AP will not buffer GLK-GCR frames destined to those GLK STAs
  But send the corresponding frames as unicasts to the GLK STA.
Notes: GCR-SP transmits GCR group addressed frames at intervals, where the interval between transmissions might be smaller than the beacon interval. Compared to non-GCR-SP, GCR-SP might provide lower delay and jitter.

## Slide 5: GLK STA functions
Set internal state based on the contents of the GLK-GCR Response element in [Re]Association Response frames and in that include a GLK-GCR Response element
  Handle corresponding GLK-GCR frames received appropriately
    Drop duplicates, respond to BARs, etc

## Slide 6: Overview of the GLK-GCR Protocol
STA
AP/MAP
Association Request with GLK Cap element
Association Response with GLK-GCR Response Element
GLK Link Setup
GLK-GCR Teardown when the STA disassociates from the AP
.
.
.
GLK-GCR transmission of MSDU/A-MSDU
(with BlockACK)
GLK-GCR retransmission policy change
.
.
.
GLK-GCR transmission of MSDU/A-MSDU
(with Unsolicited Retransmissions)

## Slide 7: Overview of the frames/elements
GLK-GCR Response element
Retransmission Policy Change Notification frame

## Slide 8: GLK-GCR Response element
GLK-GCR Response |  |  |  | optional |  |  |  | 
 | Element ID | Length | GLK-GCR Retransmission Policy | A-MSDU Supported | Reserved | Reorder Buffer Size | Block Ack Timeout | Starting Sequence Control
Octets bits | 1 | 1 | 2 |  |  |  | 2 | 2
 |  |  | 1 | 1 | 4 | 10 |  | 

## Slide 9: Retransmission Policy Change Notification frame (GLK Action Frame)
 | Category | Public Action | GLK-GCR element
octets | 1 | 1 | 4 or 8