## Slide 1: GCR using SYNRA for GLK
Date: 2015-03-09
Authors:

## Slide 2: Abstract
Describes a GLK-GCR which is a simplified GCR service for GLK.

## Slide 3: Overview of the GLK-GCR Protocol
STA
AP/MAP
Association Request with GLK Cap element
Association Response with GLK-GCR Response Element
GLK Link Setup
GLK-GCR Teardown when the STA disassociates from the AP
.
.
.
GLK-GCR transmission of MSDU/A-MSDU
(with BlockACK)
GLK-GCR retransmission policy change
.
.
.
GLK-GCR transmission of MSDU/A-MSDU
(with Unsolicited Retransmissions)

## Slide 4: AP functions
A GLK-GCR Service is setup implicitly by the AP for all SYNRA
  What is the choice of retransmission policy?
    Depends on the traffic load for GLK links at the AP
    E.g. Block ACK when SYNRA represents a small (< 10) GLK STAs; unsolicited retries, otherwise.
  AP implicitly does the GLK-GCR Service setup for all SYNRA
    The retransmission policy may be modified if the AP decides to move between Block ACKs and Unsolicited Retries
    [Re]Association response include the GLK-GCR Response element
      may also include a BA Agreement element if the GLK-GCR retransmission policy is Block ACK
    The GCR Delivery Method is non-GCR-SP (See Cl. 10.24.16.3.1)
    Notifications can be groupcast to all affected GLK STAs using current GLK-GCR retransmission policy
      Useful when GLK-GCR retransmission policy changes

## Slide 5: AP Functions
If one or more GLK STAs go into PS mode, the AP will not buffer GLK-GCR frames destined to those GLK STAs
  But send the corresponding frames as unicasts to the GLK STA.
AP needs to advertize (via the GLK Capabilities element) if GLK-GCR is active or otherwise
  Helps a STA to decide if it should associate with the AP or look for a different AP.
  GLK-GCR bits in the GLK Capabilities element
Notes: GCR-SP transmits GCR group addressed frames at intervals, where the interval between transmissions might be smaller than the beacon interval. Compared to non-GCR-SP, GCR-SP might provide lower delay and jitter.

## Slide 6: GLK STA functions
Set internal state based on the contents of the GLK-GCR Response element in [Re]Association Response frames and in that include a GLK-GCR Response element
  Handle corresponding GLK-GCR frames received appropriately
    Drop duplicates, respond to BARs, etc

## Slide 7: Overview of the frames/elements
GLK Capabilities Element
GLK-GCR Response element
Retransmission Policy Change Notification frame

## Slide 8: GLK Capabilities Element
GLK-Capabilities |  |  | GLK Capability field |  |  |  |  | 
 | Element ID | Length | DNSB | DNSU | DNSM | GLK-GCR Supported | GLK-GCR | Reserved
Octets bits | 1 | 1 | 1 |  |  |  |  | 
 |  |  | b0:1 | b1:1 | b2:1 | B3:1 | b4,5:2 | b,6,7:2
b3 | b4 | 
0 | 0 | GLK-GCR not supported/implemented/activated
0 | 1 | GLK-GCR not operational (reserved in STA)
1 | 0 | Operating in GLK-GCR unsolicited retransmission mode (reserved in STA)
1 | 1 | Operating in GLK-GCR Block ACK mode (reserved in STA)

## Slide 9: GLK-GCR element
GLK-GCR Response |  |  |  | optional |  |  | 
 | Element ID | Length | GLK-GCR Retransmission Policy | A-MSDU Supported | Reserved | Reorder Buffer Size | Block Ack Timeout Value
Octets bits | 1 | 1 | 2 |  |  |  | 2
 |  |  | 2 | 1 | 3 | 10 | 
b0 | b1 | Description
0 | 0 | Reserved
0 | 1 | GLK-GCR not operational
1 | 0 | Operating in GLK-GCR unsolicited retransmission mode (reserved in STA)
1 | 1 | Operating in GLK-GCR Block ACK mode (reserved in STA)

## Slide 10: Retransmission Policy Change Notification frame (GLK Action Frame)
 | Category | Public Action | GLK-GCR element
octets | 1 | 1 | 4 or 8

## Slide 11: Questions from the discussion
GLK-GCR may not be good for some applications
  Like video where unsolicited retransmissions will be wasteful of the bandwidth and Block ACK based retransmissions may be too late. So we need a mode for STAs to choose not to do GLK-GCR
  Might need a hybrid model where legacy multicast is used with GLK STAs that choose not to do GLK-GCR; SYNRA may not be useful with these GLK STAs
What if a device desires GCR for some applications and non-GCR for others?
  Use different Groupcast Addresses
What if a GLK device desires GLK-GCR for some applications and non-GLK-GCR for others?
  Do not use GLK-GCR
What happens when a GLK STA that does not support GLK-GCR joins the BSS?
  The AP terminates GLK-GCR by sending a Retransmission Policy Change Notification where the GLK-GCR Retransmission Policy is set to GLK-GCR Not Operational