## Slide 1: GCR using SYNRA for GLK
Date: 2015-06-29
Authors:

## Slide 2: Abstract
Describes a GLK-GCR which is a simplified GCR service for GLK.

## Slide 3: Overview of the GLK-GCR Protocol
STA
AP/MAP
Association Request with GLK Cap element
Association Response with GLK-GCR Response Element
GLK Link Setup
GLK-GCR Teardown when the STA disassociates from the AP
.
.
.
GLK-GCR transmission of MSDU/A-MSDU
(with BlockACK)
GLK-GCR retransmission policy change
.
.
.
GLK-GCR transmission of MSDU/A-MSDU
(with Unsolicited Retransmissions)
Messages shown in black are unicast. Messages in red and blue are multicast

## Slide 4: AP functions
A GLK-GCR Service is setup implicitly by the AP for all SYNRA
  What is the choice of retransmission policy?
    Depends on the traffic load for GLK links at the AP
    E.g. Block ACK when SYNRA represents a small (< 10) GLK STAs; unsolicited retries, otherwise.
  AP implicitly does the GLK-GCR Service setup for all SYNRA
    The retransmission policy may be modified if the AP decides to move between Block ACKs and Unsolicited Retries
    [Re]Association response include the GLK-GCR Response element
      may also include a BA Agreement element if the GLK-GCR retransmission policy is Block ACK
    The GCR Delivery Method is non-GCR-SP (See Cl. 10.24.16.3.1)
    Notifications can be groupcast to all affected GLK STAs using current GLK-GCR retransmission policy
      Useful when GLK-GCR retransmission policy changes

## Slide 5: AP Functions
If one or more GLK STAs go into PS mode, the AP will not buffer GLK-GCR frames destined to those GLK STAs
  But send the corresponding frames as unicasts to the GLK STA.
AP needs to advertize (via the GLK Capabilities element) if GLK-GCR is active or otherwise
  Helps a STA to decide if it should associate with the AP or look for a different AP.
  GLK-GCR bits in the GLK Capabilities element
Notes: GCR-SP transmits GCR group addressed frames at intervals, where the interval between transmissions might be smaller than the beacon interval. Compared to non-GCR-SP, GCR-SP might provide lower delay and jitter.

## Slide 6: GLK STA functions
Set internal state based on the contents of the GLK-GCR Response element in [Re]Association Response frames and in that include a GLK-GCR Response element
  Handle corresponding GLK-GCR frames received appropriately
    Drop duplicates, respond to BARs, etc

## Slide 7: Overview of the frames/elements
GLK Capabilities Element
GLK-GCR Response element
Retransmission Policy Change Notification frame

## Slide 8: GLK Capabilities Element
GLK-Capabilities |  |  | GLK Capability field |  |  |  | 
 | Element ID | Length | DNSB | DNSU | DNSM | GLK-GCR | Reserved
Octets bits | 1 | 1 | 1 |  |  |  | 
 |  |  | b0:1 | b1:1 | b2:1 | b3,4:2 | b,5,6,7:2
b3 | b4 | 
0 | 0 | GLK-GCR not supported/implemented/activated
0 | 1 | GLK-GCR not operational (reserved in STA)
1 | 0 | Operating in GLK-GCR unsolicited retransmission mode (reserved in STA)
1 | 1 | Operating in GLK-GCR Block ACK mode (reserved in STA)

## Slide 9: GLK-GCR element
GLK-GCR Response |  |  |  | optional |  | 
 | Element ID | Length | GLK-GCR Retransmission Policy | Reserved | Reorder Buffer Size | Block Ack Timeout Value
Octets bits | 1 | 1 | 2 |  |  | 2
 |  |  | 2 | 4 | 10 | 
b0 | b1 | Description
0 | 0 | Reserved
0 | 1 | GLK-GCR not operational (implies groupcast using directed multicast)
1 | 0 | Operating in GLK-GCR unsolicited retransmission mode (reserved in STA)
1 | 1 | Operating in GLK-GCR Block ACK mode (reserved in STA)

## Slide 10: GLK Groupcast Mode Change Notification frame (GLK Action Frame)
 | Category | Public Action | GLK-GCR element
octets | 1 | 1 | 4 or 8

## Slide 11: Questions from the discussion
GLK-GCR may not be good for some applications
  Like video where unsolicited retransmissions will be wasteful of the bandwidth and Block ACK based retransmissions may be too late. So we need a mode for STAs to choose not to do GLK-GCR
  Might need a hybrid model where legacy multicast is used with GLK STAs that choose not to do GLK-GCR; SYNRA may not be useful with these GLK STAs
What if a device desires GCR for some applications and non-GCR for others?
  Use different Groupcast Addresses
What if a GLK device desires GLK-GCR for some applications and non-GLK-GCR for others?
  Do not use GLK-GCR
What happens when a GLK STA that does not support GLK-GCR joins the BSS?
  The AP terminates GLK-GCR by sending a Retransmission Policy Change Notification where the GLK-GCR Retransmission Policy is set to GLK-GCR Not Operational

## Slide 12: How is the BlockAckRequest and the corresponding Block Ack tied to GLK-GCR?
Replace the GCR bit in the BlockAckReq and BlockAck Control fields with a 2-bit field to allow for signaling GCR or GLK-GCR
GLK-GCR BlockAckReq/BlockAck apply to all SYNRA (not a specific SYNRA)
Introduce new GLK-GCR Modes for BlockAckReq (Cl. 8.3.1.8.1 and 8.3.1.9.7) and BlockAck (Cl. 8.3.1.9.1 and 8.3.1.9.7)
Modify Cl. 9.24.6 accordingly

## Slide 13: BlockAckReq and BlockAck for GLK-GCR
 | B0 | B1 | B2 | B3 B4 | B5-B11 | B12-B15
 | BA Ack Policy | Multi-TID | Compressed Bitmap | GCR Mode | Reserved | TID_INFO
Bits | 1 | 1 | 1 | 2 | 7 | 4
GCR Mode (B3 B4) | Description
00 | Reserved (or non-GCR modes)
01 | The BA is a GLK-GCR Block Ack
10 | The BA is a GCR Block Ack
11 | Reserved
Multi-TID subfield value | Compressed Bitmap subfield value | GCR Mode subfield value (b3, b4) | BlockAckReq/BlockAck frame variant
0 | 0 | 00 | Basic BlockAck
0 | 1 | 00 | Compressed BlockAck
1 | 0 | 00 | Extended Compressed BlockAck
1 | 1 | 00 | Multi-TID BlockAck
0 | 0 | 01, 10 or 11 | Reserved
0 | 1 | 00 or 11 | Reserved
0 | 1 | 10 | GCR BlockAck
0 | 1 | 01 | GLK-GCR BlockAck
1 | 0 | 00, 01, 10 or 11 | Reserved
1 | 1 | 00, 01, 10 or 11 | Reserved
Wow a legacy implementation treat this combination as Compressed BlockAckReq/BlockAck?
No. Since the Block ACK Request would only be sent to a STA with which the GLK-GCR service has been setup.

## Slide 14: GLK-GCR with BA Operation
GLK-GCR service setup on association
AP assigns unique sequence numbers to all packets sent via GLK-GCR irrespective of the SYNRA used in the RA field of the corresponding frame
{
  After transmitting a set of frames (less than or equal to the Reorder Buffer Size field in the GLK-GCR element), the AP
  {
      sends a GLK-GCR BlockAckReq frame to each of the associated GLK STAs (in some cases a select subset of GLK STAs depending on APs policy)
      On receipt of the BlockAckReq, the corresponding GLK STA responds with a bitmap identifying the frames successfully received (but may or may not be passed up the stack based on SYNRA filtering)
  }
  The AP then performs the required retransmissions based on the response from the GLK STAs to the BlockAckReq
}