## Slide 1: Potential of Modified Signal Detection Thresholds
Date: 2015-03-09
Authors:

## Slide 2: Abstract
Several studies have investigated the impact of increased signal detection thresholds
Performance gains vary a lot between evaluations
Importance of correct modeling of preamble detection shown in 11-15/0050r0, [1]
This contribution investigates effects of changing signal and energy detection thresholds and estimates the potential gains of such changes

## Slide 3: Investigated Parameters
CCAT is signal detect threshold
EDT is energy detection threshold
Energy detection will be used if
  The SINR of the preamble is too low to decode (< 3 dB)
  The receiver is busy with transmission or reception at the time the preamble is sent and starts sensing in the middle of the frame
3 cases
  Legacy: CCAT = -82dBm, EDT = -62dBm
  Green: CCAT = -62dBm, EDT = -62dBm
  Red: CCAT = -52dBm, EDT = -52dBm

## Slide 4: Simulation assumptions
TGax Scenario 2: Enterprise
50% UL 50% DL traffic
Equal buffer (file transfer with varied intensity), file size 1MB
  Ref: 11-14/0866r1, [2]
“Served traffic per AP” is total volume received in UL & DL per AP
CWmin = 15, CWmax = 1023
Realistic link adaptation algorithm (Minstrel)

## Slide 5: DL performance
Next slides present results from a highly loaded traffic point at ~120 Mbps/AP

## Slide 6: Utilization
At the selected load point the mean access point utilization is around 25%
The channel utilization as perceived from one AP is however ~70% for the legacy system.
With increased sensing thresholds the channel is not perceived as busy, reducing the time spent in back-off state.
Chart: AP and Channel utilization [%]
| Legacy | CCAT = -62 dBm | CCAT = -52 dBm
AP utilization | 27 | 25 | 24
Channel utilization | 72 | 52 | 25

## Slide 7: DL Transmission attempts
Number of back-offs reduced substantially, from 72% in legacy system to 25% in most aggressive case
Fraction of failed packets does not increase very much
-82 dBm
-62 dBm
-52 dBm
Out of transmissions
Out of attempts

## Slide 8: UL Transmission attempts
Number of back-offs reduced substantially, from 65% in legacy system to 27% in most aggressive case
Fraction of failed transmissions quite high in all scenarios, but does not increase much with increased thresholds
-82 dBm
-62 dBm
-52 dBm
Out of transmissions
Out of attempts

## Slide 9: Signal vs. Energy Detect DL
Signal detect back-offs significantly reduced when increasing CCAT, when increasing ED also energy detection back-offs are reduced
At -52dBm the main back-off reason is for transmissions in same BSS
-82 dBm
-62 dBm
-52 dBm
Out of back-offs
Out of attempts

## Slide 10: Signal vs. Energy Detect UL
At -52dBm 94% of back-offs are for transmissions in same BSS, equally split over DL and UL
-82 dBm
-62 dBm
-52 dBm
Out of back-offs
Out of attempts

## Slide 11: Failure causes
An analysis was made on what caused a packet failure, the following categories were used:
  Coll DL: Collision with a DL frame in the same BSS due to same random backoff value
  Coll UL: Collision with an UL frame in the same BSS due to same random backoff value
  BSS DL: Frame was partly concurrent with a DL frame in the same BSS
  BSS UL: Frame was partly concurrent with an UL frame in the same BSS, hidden node
  BSS: Frame was partly concurrent with more than one frame in the same BSS
  OBSS DL: Frame was interfered by a DL frame from another BSS
  OBSS UL: Frame was interfered by an UL frame from another BSS
  Multiple OBSS: Frame was interfered by several frames from another/other BSS/s

## Slide 12: Cause of Failures DL
Collisions reduced with increased CCAT and EDT
  Fewer nodes becoming aligned in time due to back-off for the same transmissions
Mainly OBSS interference from multiple interferers behind failures
-82 dBm
-62 dBm
-52 dBm
Out of failures
Out of failures
Multiple OBSS TX
ACK not a problem

## Slide 13: Cause of Failures UL
Hidden node problem increases with increased CCAT, but fraction still <10%
Hidden node
Out of failures
Out of failures
Multiple OBSS TX
-82 dBm
-62 dBm
-52 dBm

## Slide 14: Potential of Modified Signal Detection Thresholds
Removing all waiting time due to CS back-off, what is the potential gain?
Same SINR and MCS assumed
Chart: 
| Gain potential
CCAT = -82dBm | 28
CCAT = -62dBm | 9.4
CCAT = -52dBm | 3.5

## Slide 15: Summary/Conclusion
By modifying the CCAT and EDT the number of back-offs is reduced substantially, from 70% in legacy system to 25% in most aggressive case (CCAT = EDT = -52dBm)
The potential of reducing sensing thresholds from legacy levels is about 28%. At -52dBm CCAT and EDT there is only 3.5% potential left

## Slide 16: References
[1] “Modeling components impacting throughput gain from CCAT adjustment”, 11-15/0050r0
[2] “Traffic modeling and system capacity performance measure”, 11-14/0866r1