## Slide 1: Power Save Mode Calibration Results
Date: 2015-03-09
Authors:

## Slide 2: Abstract
The contributions [1]-[3] described one or more of the 3 existing power save mechanisms in 802.11-2012 [4] as baseline for energy efficiency evaluation in simulation scenario [5] and evaluation methodology documents [6] for TGax
  Power save mode (PSM)
  Power save polling (PSP)
  Unscheduled automatic power save delivery (U-APSD)
For this activity, a MAC calibration test for power save is defined in [5] for companies to calibrate their MAC system simulators
  Some companies have presented results for PSM [8] and U-APSD [7-9].
This contribution presents calibration test results for PSM

## Slide 3: Calibration Test Setup
Scenario
  Simulation Run Time = 9000 seconds
  802.11n PHY, 20 MHz bandwidth, 5 GHz band
  PER = 0
  No A-MPDU aggregation
Power Save Test Parameters
  MSDU length: 1500 bytes with CWmin=15 downlink every 200 ms
  RTS/CTS [ OFF ]
  AIFS=DIFS=34us
  MCS = [ 0 ]
  DTIM = [ 3 ]
  PSM timeout = [ 100 ] ms
AP
STA
Output
  Percentage of time spent in each power state over simulation run
  Average power consumed for each power state over simulation run

## Slide 4: Summary of Parameters for PSM
Pre-TBTT
Mechanism | Parameter | Definition/Values | Suggested Set of Simulation Values **
Power save mode (PSM) | Beacon Interval (BI) | 100 TU | 100 TU
 | DTIM | Integer in unit of BI | { 1, 3 }
 | PSM timeout | Length of time before STA goes to sleep | { 50, 100, 200 } ms
 | Pre-Target Beacon Transmission Time (TBTT) | Length of time before a STA wakes before Beacon | { 0 } ms
 | Beacon timeout | Length of time after TBTT | { 5 } ms
AP
STA
Beacon
A Power Save STA fails to receive Beacon after Beacon timeout, and switches back to Sleep state
Beacon timeout
TBTT
A Power Save STA switches from Sleep to Listen state in anticipate for Beacon

## Slide 5: Example of PSM Operation [3]
AP buffers this frame since this STA is in power save mode
AP
STA
ACK
Beacon
A-MPDU
STA starts CCA for Data frame with PM=0
DATA
AP starts CCA
BA
STA return to Doze, and AP resumes buffering traffic for this STA
STA exits power save mode and is Awake for DTIM Beacon, i.e. DtimCount=0; STA skips other Beacons that are not DTIM
PM=0
PM=0
A-MPDU
BA
AP is aware STA is out of PM mode, and no longer buffers traffic for this STA
MPDU
ACK
ACK
PM=1
PM=1
PSM Timeout
STA starts CCA
DtimCount=0

## Slide 6
Simulation Results for PSM
Percentage of Time Spent in Each Power State over Simulation Run
Power Save Mode (PSM) |  |  | STA (% of Total Simulation Time) |  |  |  | AP (% of Total Simulation Time) |  |  | 
Enabled? | DTIM Period (BI) | PSM Timeout (ms) | Listen | RX | TX | Sleep | Listen | RX | TX | Sleep
No | - | - | 98.0645 | 1.9055 | 0.0300 | 0 | 98.0645 | 0.0300 | 1.9055 | 0
Yes | 1 | 50 | 25.0644 | 1.9655 | 0.1060 | 72.8641 | 97.9285 | 0.1060 | 1.9655 | 0
Yes | 3 | 50 | 18.2680 | 1.3221 | 0.0795 | 80.3305 | 97.9760 | 0.0795 | 1.9445 | 0
Yes | 1 | 100 | 50.1297 | 1.9538 | 0.1025 | 47.8140 | 97.9313 | 0.1024 | 1.9663 | 0
Yes | 3 | 100 | 40.2283 | 1.6287 | 0.0790 | 58.0640 | 97.9754 | 0.0790 | 1.9456 | 0
Yes | 1 | 200 | 96.6702 | 1.9063 | 0.0311 | 1.3924 | 98.0626 | 0.0311 | 1.9063 | 0
Yes | 3 | 200 | 95.9646 | 1.8952 | 0.0311 | 2.1091 | 98.0626 | 0.0311 | 1.9063 | 0

## Slide 7
Power Save Mode (PSM) |  |  | STA (Average Power, mW) |  |  |  |  | AP (Average Power, mW) |  |  |  | 
Enabled? | DTIM Period (BI) | PSM Timeout (ms) | Listen | RX | TX | Sleep | Total Average Power | Listen | RX | TX | Sleep | Total Average Power
No | - | - | 53.9355 | 2.0961 | 0.0924 | 0 | 56.1239 | 53.9355 | 0.0330 | 5.8690 | 0 | 59.8374
Yes | 1 | 50 | 13.7854 | 2.1621 | 0.3265 | 0.0024 | 16.2764 | 53.8607 | 0.1166 | 6.0538 | 0 | 60.0310
Yes | 3 | 50 | 10.0474 | 1.4543 | 0.2448 | 0.0027 | 11.7491 | 53.8868 | 0.0874 | 5.9892 | 0 | 59.9634
Yes | 1 | 100 | 27.5713 | 2.1492 | 0.3156 | 0.0016 | 30.0377 | 53.8622 | 0.1127 | 6.0562 | 0 | 60.0311
Yes | 3 | 100 | 22.1255 | 1.7916 | 0.2435 | 0.0019 | 24.1625 | 53.8865 | 0.0869 | 5.9925 | 0 | 59.9658
Yes | 1 | 200 | 53.1686 | 2.0970 | 0.0957 | 0.0000 | 55.3613 | 53.9344 | 0.0342 | 5.8715 | 0 | 59.8401
Yes | 3 | 200 | 52.7805 | 2.0847 | 0.0957 | 0.0001 | 54.9610 | 53.9344 | 0.0342 | 5.8715 | 0 | 59.8401
Based average current consumption values @ 1.1V in [5], i.e. TX = 280 mA, RX = 100 mA, Listen = 50 mA, Sleep = 0.003 mA;
Simulation Results for PSM
Average Power Consumed for Each Power State over Simulation Run

## Slide 8: Discussion
A Power Save (PS) STA depends on the TIM IE in Beacon to know if there are any bufferable units (BUs) at the AP, and decide whether to exit Power Save mode or Doze state
  It is likely a STA may fail to receive this Beacon due to clock drift after a long sleep, or congested wireless medium
To model Beacon reception, we introduce two new parameters to each power save mechanism
  “Pre-Target Beacon Transmission Time (TBTT)” is defined as the time a PS STA wakes prior to TBTT, i.e. Sleep Listen
  “Beacon timeout” is defined as the time a PS STA declares that it has missed a Beacon after waiting for a fix period of time after TBTT and return back to Sleep, i.e. Listen  Sleep

## Slide 9: Conclusion
This contribution presents and discusses calibration test results for PSM
Additional, introduce two parameters to model Beacon reception associated to each power save mechanism
  pre-TBTT
  Beacon timeout

## Slide 10: Straw Poll
Do you agree to define pre-TBTT and Beacon timeout parameters associated with each power save mechanism to the simulation scenario document (11-14/980r6)?
  Yes
  No
  Abstain

## Slide 11: References
E. Wong et al, “Energy efficiency evaluation methodology,” IEEE 11-14-827r3 July 2014
E. Wong et al, “Energy efficiency evaluation methodology follow up”, IEEE 11-14-1162r1, Sept 2014
E. Wong et al, “Parameters for power save mechanisms,” IEEE 11-14-1161r3, Sept 2014
IEEE 802.11-2012
S. Merlin et al, “TGax Simulation Scenarios,” IEEE 11-14-980r6, Jan 2015
R. Porat et al, “11ax Evaluation Methodology,” IEEE 11-14-571r7, Jan 2015
J. Kneckt et al, “Power save calibration results,” IEEE 11-14-1495r0, Nov 2014
J. Kneckt et al, “Power save calibration,” IEEE 11-15-0103r0, Jan 2015
Y. Li et al, “U-APSD power saving-calibration-results,” IEEE 11-15-0072r0, Jan 2015