## Slide 1: MAC calibration results for Test 4
Date: 2015-03-09
Authors:
Name | Affiliation | Address | Email
Ke Yao | ZTE |  | yao.ke5@zte.com.cn
Ruimei Li | ZTE |  | li.ruimei@zte.com.cn
Zhiqiang Han | ZTE |  | han.zhiqiang1@zte.com.cn
Bo Sun | ZTE |  | sun.bo1@zte.com.cn
Kaiying Lv | ZTE |  | lv.kaiying@zte.com.cn
Yonggang Fang | ZTE |  | yfang@ztetx.com
Jiadong Du | CATR |  | dujiadong@catr.cn

## Slide 2: Introduction
This proposal provides ZTE’ MAC calibration results for Test 4 of Box 3.
According to [1][2][3], channel bandwidths and traffic models for each BSS are set as follows
  channel bandwidth:
    BSS1: 40MHz
    BSS2: 20MHz (the secondary channel of BSS1)
  traffic model:
    BSS1: full buffer
    BSS2: Poisson distribution with lamda=100

## Slide 3: PHY layer settings
PHY | 
BW | All BSSs at 5 GHz [20/40 MHz]
Channel Model | TGac D NLOS per link
Shadow fading | i.i.d. log-normal shadowing (5 dB standard deviation) per link
Data preamble | [5 GHz, 11ac], duration is considered.
Control Preamble | [5 GHz, 11a], duration is considered.
Number of AP TX/RX antenna | 1/1
Number of STA TX/RX antenna | 1/1
AP antenna gain | 0dbi
STA antenna gain | -2dbi
Noise Figure | 7dB
CCA threshold | -82dBm
ED threshold | -72dBm/secondary channel
Link Adaption | MCS=0
Channel estimation | Ideal
Channel correlation | Same as that defined in the channel model

## Slide 4: MAC layer settings
MAC | 
Access protocol | [EDCA, AC_BE with default parameters] [CWmin = 15, CWmax = 1023, AIFSn=3]
Queue length | A single queue for each traffic link is set inside AP/STA sized of 2000 packets
MPDU size | 2000 Bytes (1964 Data + 8 UDP header + 20 IP header + 8 LLC header)
Aggregation | Non
Max number of retries | 10
Beacon | Disable
RTS/CTS | OFF/ON
Traffic direction | DL

## Slide 5: Traffic Model
 | Transport Protocol | Rate (Mbps) | MSDU Size (Byte) | Distribution | AC
BSS 1 | UDP | 1.5712*10^8bps | 2000 | Full Buffer | BE
BSS 2 | UDP | 1.57*10^6bps | 2000 | Poisson | BE

## Slide 6: Test 4: Deferral Test 1
STA 1
AP 2
AP 1
STA 2
(AP1 and STA2 are essentially co-located)
Simulation Settings:
  Distance: AP1STA1 1m; AP2STA2 1m
  RTS/CTS: off/on
  Simulation: 10 drops, each drop duration is 10s

## Slide 7: Results comparison [4]
Chart: RTS/CTS: OFF
| BSS 1 | BSS 2
ZTE | 9.21 | 1.56
MTK | 8.11 | 1.52
Chart: RTS/CTS:ON
| BSS 1 | BSS 2
ZTE | 8.19 | 1.57
MTK | 7.76 | 1.3

## Slide 8: Analysis (1)
BSS 1: 9.21 Mbps (OFF), 8.19 Mbps (ON)
When RTS/CTS is OFF:
  Ideal thpt. for BSS 1 is 9.429 Mbps (rough estimate)
    The ideal application thpt. of 40 MHz channel is10.77 Mbps, and that of 20 MHz channel is 5.7967 Mbps.
    Within 1 second, the time of BSS 1 taking 40 MHz channel is roughly 0.72895 s, and the time of only primary 20 MHz channel is 0.27105 s.
    Therefore, the ideal application throughput of BSS 1 is:
    10.77 Mbps*0.72895+5.80*0.27105=9.429 Mbps.
  Simulation Result of 9.21 Mbps is close to the estimation.
  When RTS/CTS is ON:
  Ideal thpt. for BSS1 is 8.661 Mbps (rough estimate).
  Simulation Result of 8.19 Mbps is close to the estimation.

## Slide 9: Analysis (2)
BSS2: 1.565Mbps (OFF), 1.57Mbps (ON)
  Ideal thpt. for BSS 1 is 1.6 Mbps (rough estimate)
    Poisson traffic with lamda = 100 means that there are averagely 100 packets generated per second. With MSDU size is 2000 bytes the long term average data rate is 2000*8/(1/100)=1.6 Mbps.
  Simulation Results is close to the estimation.

## Slide 10: References
  [1]. Doc. IEEE 802.11-14/0571r5 11ax evaluation methodology
  [2]. Doc. IEEE 802.11-14/0621r4 / Doc. IEEE 802.11-14/0980r4 ax Simulation scenarios
  [3]. Doc. IEEE 802.11-14/0895r1 Calibration of MAC simulator with OBSS Network Scenario
  [4]. Doc. IEEE 802.11-15/0104r1 11ax sls mac test 4 results