## Slide 1: Simulation Results for Box5
Date: 2015-03-09
Authors:
Name | Affiliation | Address | Email
Ke Yao | ZTE |  | yao.ke5@zte.com.cn
Zhiqiang Han | ZTE |  | han.zhiqiang1@zte.com.cn
Ruimei Li | ZTE |  | li.ruimei@zte.com.cn
Bo Sun | ZTE |  | sun.bo1@zte.com.cn
Kaiying Lv | ZTE |  | lv.kaiying@zte.com.cn
Yonggang Fang | ZTE |  | yfang@ztetx.com
Jiadong Du | CATR |  | dujiadong@catr.cn

## Slide 2: Abstract
  The submission provides updated simulation results for Box-5 calibration.
  Applying the assumptions about preamble detection and other issues like receiving procedure in [2].
  Some further details in our simulation are listed in the following slides.
  We also compare our results with some other companies.

## Slide 3: Simulation Methods
Traffic Initialization
  To avoid collision storm at the beginning of the simulation, the start time of each traffic is randomized. It means that the start time of every traffic link is equal to a constant time plus a random time, and the random time is a (0, 1s) uniformly distributed random variable.
Throughput
  Without the effect of association and ARP procedure
  50 drops, each drop lasts for 5s.

## Slide 4: Box5 Calibration Scenario
11ac SS6 – OBSS Enterprise [1]
AP C | (-40,-20)
STA6 | (-5.5+xc,4.5+yc)
STA12 | (7+xc,7+yc)
STA18 | (10+xc,0.5+yc)
STA24 | (3+xc,2.5+yc)
STA30 | (9.5+xc,3.5+yc)
AP A | (0,0)
STA1 | (5,-9.5)
STA2 | (3.5,7.5)
STA4 | (-4.5,0.5)
STA5 | (-1.5,6)
STA7 | (-9,-5)
STA8 | (-8.5,8.5)
STA10 | (-3,0.5)
STA11 | (-0.5,8)
STA13 | (-4,-4)
STA14 | (7.5,-1)
STA16 | (8,-6)
STA17 | (0,-7.5)
STA19 | (-2.5,-4.5)
STA20 | (0.5,-2)
STA22 | (0,-4.5)
STA23 | (-1.5,7)
STA25 | (3.5,-5)
STA26 | (9,9.5)
STA28 | (-8,-5.5)
STA29 | (1.5,3.5)
Fixed Location and Association
AP A | (0,0)
AP B | (40,20)
AP C | (-40,-20)
AP B | (40,20)
STA3 | (7.5+xb, ‑9.5+yb)
STA9 | (7+xb, -7.5+yb)
STA15 | (3+xb, -0.5+yb)
STA21 | (-6.5+xb, -3+yb)
STA27 | (‑6+xb, 2.5+yb)

## Slide 5: 11ac SS6 Traffic Flow Model
DL/UL traffic assigned for each STA
STA | DL | UL | STA | DL | UL
STA1 | y | y | STA23 | n | y
STA2 | y | y | STA25 | y | y
STA4 | y | y | STA26 | y | y
STA5 | y | y | STA28 | y | y
STA7 | y | y | STA29 | y | y
STA8 | y | y | STA3 | y | y
STA10 | y | n | STA9 | y | n
STA11 | y | n | STA15 | y | n
STA13 | y | n | STA21 | n | y
STA14 | y | n | STA27 | y | y
STA16 | y | n | STA6 | y | y
STA17 | y | n | STA12 | y | n
STA19 | y | n | STA18 | y | n
STA20 | y | n | STA24 | n | y
STA22 | n | y | STA30 | y | y
“y” means having DL/UL traffic flow; “no” means not having DL/UL traffic flow

## Slide 6: Box-5 PHY Details
PHY parameters | 
BW | All BSSs at 5GHz [80 MHz, no dynamic bandwidth]
Channel model | TGac D NLOS per link
Shadow fading | iid log-normal shadowing (5 dB standard deviation) per link
Data Preamble Type | [5GHz, 11ac], always decoded correctly after successful reception, duration is considered.
STA TX Power | 15 dBm per antenna
AP TX Power | 20 dBm per antenna
AP number of TX/RX antennas | 1/1
STA number of TX /RX antennas | 1/1
Capture Window | [0 ns 800ns]
preemption window | [0 ns]
AP antenna gain | 0 dBi
STA antenna gain | -2 dBi
Noise Figure | 7dB
CCA threshold ( CCA-SD) | -76dBm (measured across the entire bandwidth after large-scale fading)
ED threshold (CCA-ED) | -56dBm
Link Adaption | Fixed MCS =7 (292.5Mbps)
Channel estimation | ideal
PHY abstraction | RBIR, BCC [1, 5]
Channel correlation | Independent or time-correlated channel per packet

## Slide 7: MAC Parameters
MAC parameters | 
Access protocol | [EDCA, AC_BE with default parameters] [CWmin = 15, CWmax = 1023, AIFSn=3]
Queue length | 2000 packets length multiplied by the STA number inside AP; 2000 packets length inside STA
Traffic type | UDP CBR with rate 10^8bps. The same traffic is attached to each STA or AP.
MPDU size | 1530 Bytes (1472 MSDU + 36 UDP、IP、LLC header + 30 MAC header)
Aggregation | [A-MPDU / max aggregation size / BA window size, No A-MSDU with immediate BA], Max aggregation: 64 MPDUs with 4-byte MPDU delimiter (with 2 bytes padding)
Max number of retries | 10
Beacon | Disabled
RTS/CTS | OFF
Traffic direction | UL Only, DL only, Mixed DL & UL
Throughput metric | CDF or Histogram of per non-AP STA throughput (received bits/overall simulation time)

## Slide 8: DL only of One BSS
1-BSS DL-only results from five companies show similar trend.
Chart: 
| 3 | 9 | 15 | 21 | 27
Huawei | 51.09 | 51.55 | 51.05 | 51.42 | 51.37
LG | 51.05 | 50.97 | 51.11 | 50.7 | 51.1
MRVL | 52 | 52.68 | 52.68 | 52.51 | 52.81
NTT | 49.92 | 50.08 | 49.95 | 50.04 | 50.24
ZTE | 51.98 | 52.03 | 52.16 | 52.21 | 51.86

## Slide 9: UL only of UL BSS
1-BSS UL-only results from five companies show similar trend and aligned within an acceptable range.
Chart: 
| 3 | 9 | 15 | 21 | 27
Huawei | 40.83 | 45.4 | 48.49 | 43.29 | 44.06
LG | 36.83 | 39.86 | 48.95 | 42 | 39.01
MRVL | 37.74 | 41.15 | 51.52 | 46.6 | 44.83
NTT | 42.79 | 44.86 | 48.92 | 40.4 | 42.21
ZTE | 39.75 | 43.14 | 43.38 | 41.11 | 39.18

## Slide 10: Three BSSs Test Result -- DL only
Chart: 
| 1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 22 | 23 | 25 | 26 | 28 | 29 | 3 | 9 | 15 | 21 | 27 | 6 | 12 | 18 | 24 | 30
20 drops | 3.44 | 3.12 | 3.45 | 2.9 | 2.7 | 2.4 | 3.14 | 2.48 | 3.01 | 2.86 | 2.47 | 3.58 | 3.75 | 4.72 | 0 | 0 | 3.19 | 2.36 | 3.36 | 3.85 | 39.5 | 41.28 | 47.01 | 0 | 43.47 | 39.67 | 34.92 | 35.01 | 0 | 34.85
Capture Window=0ns
Throughput (Mbps):
  BSS A: 56.77
  BSS B: 171.26
  BSS C: 144.45

## Slide 11: Three BSSs Test Result -- DL only
Chart: 
| 1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 22 | 23 | 25 | 26 | 28 | 29 | 3 | 9 | 15 | 21 | 27 | 6 | 12 | 18 | 24 | 30
20 drops | 3.1 | 1.97 | 3.3 | 3.41 | 3.02 | 3.07 | 3.54 | 3.88 | 2.35 | 3.42 | 4 | 2.17 | 3.56 | 3.86 | 0 | 0 | 2.38 | 1.65 | 2.72 | 5.02 | 39.29 | 43.18 | 47.16 | 0 | 42.71 | 40.07 | 35.43 | 34.62 | 0 | 35.55
Capture Window=800ns
Throughput (Mbps):
  BSS A: 56.42
  BSS B: 172.34
  BSS C: 145.67

## Slide 12: Three BSSs Test Result -- UL only
Capture Window=0ns
Throughput (Mbps):
  BSS A: 61.75
  BSS B: 90.40
  BSS C: 125.43
Chart: 
| 1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 22 | 23 | 25 | 26 | 28 | 29 | 3 | 9 | 15 | 21 | 27 | 6 | 12 | 18 | 24 | 30
UL Throughput | 1.26 | 2.04 | 13.24 | 3.95 | 1.21 | 0.72 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 10.36 | 2.86 | 4.06 | 0.69 | 1.01 | 20.35 | 4.37 | 0 | 0 | 38.69 | 47.34 | 29.28 | 0 | 0 | 85.25 | 10.9

## Slide 13: Three BSSs Test Result -- UL only
Capture Window=800ns
Throughput (Mbps):
  BSS A: 57.65
  BSS B: 91.11
  BSS C: 123.65
Chart: 
| 1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 22 | 23 | 25 | 26 | 28 | 29 | 3 | 9 | 15 | 21 | 27 | 6 | 12 | 18 | 24 | 30
UL Throughput | 0.56 | 2.79 | 11.91 | 3.18 | 1.23 | 1.13 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 11.6 | 2.3 | 2.58 | 0.53 | 1.26 | 18.6 | 4.7 | 0 | 0 | 39.37 | 47.03 | 26.04 | 0 | 0 | 85.34 | 12.26

## Slide 14: Three BSSs Test Result -- DL&UL
Capture Window=0ns
Throughput (Mbps):
  BSS A: 46.40(DL:16.75, UL:29.65)
  BSS B：127.35 (DL:88.76, UL:38.59)
  BSS C：125.58 (DL:34.78, UL:90.80)
Chart: 
| 1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 22 | 23 | 25 | 26 | 28 | 29 | 3 | 9 | 15 | 21 | 27 | 6 | 12 | 18 | 24 | 30
DL | 0.75 | 0.66 | 1.18 | 0.87 | 0.79 | 0.83 | 1.19 | 0.87 | 0.86 | 0.92 | 0.94 | 1.36 | 0.96 | 1.5 | 0 | 0 | 0.74 | 0.49 | 0.62 | 1.23 | 19.74 | 21.49 | 25.71 | 0 | 21.82 | 11.07 | 7.51 | 8.01 | 0 | 8.18
UL | 0.44 | 0.6 | 5.83 | 1.79 | 0.6 | 0.51 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 5.21 | 1.31 | 1.71 | 0.31 | 0.5 | 10.83 | 2.02 | 0 | 0 | 15.86 | 20.71 | 12.61 | 0 | 0 | 72.61 | 5.58

## Slide 15: Three BSSs Test Result -- DL&UL
Capture Window=800ns
Throughput (Mbps):
  BSS A: 45.45(DL:14.62, UL:30.83)
  BSS B：129.78 (DL:90.65, UL:39.13)
  BSS C：126.83 (DL:37.84, UL:88.99)
Chart: 
| 1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 22 | 23 | 25 | 26 | 28 | 29 | 3 | 9 | 15 | 21 | 27 | 6 | 12 | 18 | 24 | 30
DL | 1.04 | 0.63 | 1.52 | 1.07 | 0.66 | 1 | 0.93 | 0.91 | 0.68 | 0.71 | 0.86 | 0.73 | 0.93 | 0.76 | 0 | 0 | 0.48 | 0.33 | 0.49 | 0.91 | 19.46 | 22.06 | 25.55 | 0 | 23.58 | 12.72 | 7.73 | 8.38 | 0 | 9.01
UL | 0.64 | 0.64 | 6.76 | 1.9 | 0.69 | 0.46 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 5.46 | 0.9 | 1.64 | 0.2 | 0.39 | 11.13 | 1.5 | 0 | 0 | 15.23 | 22.4 | 12.39 | 0 | 0 | 71.34 | 5.26

## Slide 16: Summary
Provide our Box 5 simulation results and compare with some other companies.
1-BSS case results are already aligned.
For 3-OBSS cases, results from different companies have not converged to a stable state, our results are within them.
More efforts are needed for calibration of box 5, especially for multi-OBSS cases.

## Slide 17: References
[1] 11-15-0053-00-00ax-box5-results-of-11ac-ss6.
[2] 11-14-1523-03-00ax-offline-discussion-minutes-of-sls-calibration
[3] 11-15-0051-00-00ax-box5-calibration-results
[4] 11-14-1392-04-00ax-simulation-results-for-box-5-calibration
[5] 11-14-1419-00-00ax-sls-box5-calibration-results-and-discussions
[6] 11-14-1388-01-00ax-consideration-on-per-prediction-for-phy-abstruction
[7] 11-14-1392-01-00ax-simulation-results-for-box-5-calibration