## Slide 1: CCA Regime Evaluation Revisited
March 2015
Name | Affiliations | Address | Phone | email
Amin Jafarian | NEWRACOM |  |  | amin.jafarian@newracom.com
Minho Cheong |  |  |  | 
Reza Hedayat |  |  |  | 
Young Hoon Kwon |  |  |  | 
Daewon Lee |  |  |  | 
Vida Ferdowsi |  |  |  | 
Yongho Seok |  |  |  | 

## Slide 2: Evaluation of CCA protocols
Conventional ways to evaluate CCA protocols
  Consider a few specific scenarios, each with fixed location of STAs/APs
  Compute the average throughput gain/loss due to the proposed CCA per scenario and compare it with the baseline CCA
Potential Issues:
  In each Scenario, the evaluation results can be STA locations dependent
      There might be many more locations that the proposed CCA does not provide any gain
      There might be many locations that the gain is higher
  What is a good definition for gain can be debatable and the result can totally change depends on the definition
      Weighted sum-rate (unfair to the originator)
      Maximum achievable rate (unfair to the originator)

## Slide 3: Proposed Evaluation Criteria
To address the previous issues, we propose the following way to evaluate CCA:
For a specific scenario, consider many joint locations for all the STAs in the network
For each of the locations, compute the event if a simultaneous transmission was possible but the proposed CCA did not allow (under scenario 1 or 2, see below)
Compute the percentage number of joint locations (average cases) that #2 was satisfied. The lower the number is, the higher chance of spatial reuse
Above is done for the current /new CCA protocols and the results indicate which has higher spatial reuse
The simultaneous transmission could have no additional conditions:
  Metric 1: Both transmissions are allowed by at least the lowest MCS.
  Note: this provides an upper bound on the performance of the CCA. But it is not fair for the CCA originator
Or under the condition that the secondary transmission does not hurt the first transmission
  Metric 2: the secondary transmission is allowed with at least the lowest MCS while the first transmission does not change its MCS level
  Note 1: that this is the best performance that one can expect from a CCA protocol and what we believe is the correct definition of medium efficiency and fairness in this scenario.
  Note 2: while we believe it is very difficult to propose a CCA regime to accomplish this, in our examples, by providing some side information to the transmitters, we will put a figure on this gain.

## Slide 4: Comparing two approaches
While conventional approach can provide us with the maximum and minimum gain (e.g. throughput gain) in an specific CCA regime, the new approach will provide a figure of how the CCA regime works in an average deployment. Note that most of the users will not “optimize” the location of their APs and most of the STAs are moving around, so and average gain (average over the joint possible locations of all the STAs) should be a better metric to measure proposed CCA performance.
We propose to Compute the percentage number of joint locations that two simultaneous transmission (by either allowing hurting or not allowing hurting the original transmitter) was possible but not allowed under the proposed CCA.
  This allows us to find a lower and upper bound on the performance of CCA regime instead of focusing on an specific efficiency metric.

## Slide 5: Simple Scenario
We will show a few example of two different CCA regimes under a very simple scenario and assumptions:
  We consider a simple outdoor scenario, no shadowing, no multipath
    Primary BSS: This is the originator BSS, we assume the STA started the NAV is the AP in the primary BSS but the same idea goes through if it is a non-AP STA
    Secondary BSS: This is an OBSS in proximity of the primary BSS
      The transmitter of the secondary BSS is located in the area that is blocked by the existing CCA rules (received power at the transmitter of secondary is greater than the proposed CCA threshold)
      We will calculate the percentage of scenarios (locations) under which there could be a secondary transmission
  Because of symmetry we will fix the location of primary pair and change the secondary pair locations
    We find the percentage of locations that the secondary transmission could exist but it is not allowed as a function of normalized distance of Primary TX and RX (normalized such that the maximum distance for MCS0 being 1).
  We modify the TX powers at each STA and plot the result for each set of TX power.
  For MCS calculations, we used a simple mapping of received SINR to MCS at each receiver. We considered RX sensitivity =-88dbm, and the minimum SINR=4db that maps to MCS0.
  Data Packet Assumptions: Primary Transmitter has a very long packet in the air (more than the duration needed for the secondary packet to be transmitted)

## Slide 6: Step1: Fixed the Location of Primary Pairs at distance r (start with very small r)
Location of Primary Receiver
Location of Primary Transmitter
Primary Receiver RX sensitivity Range
Primary Transmitter Range for
TX power=15dbm
RX sensitivity=-88 dBm

## Slide 7: CCA Coverage
CCA coverage of the ongoing transmission

## Slide 8: Step 2: Through Secondary TX and RX
Location of secondary Transmitter. NOTE: it is within CCA threshold of ongoing transmission
Secondary Transmitter Range for
TX power=15dBm
RX sensitivity=-85 dBm

## Slide 9: Step 3: Compute if two simultaneous transmission is possible
Location of secondary receiver. NOTE: it is within the RX range of secondary transmitter
Secondary Receiver Range for
TX power=15dBm
RX sensitivity=-85 dBm

## Slide 10: Final Steps
Step 4: Repeat step 2 and 3 many times
  At the end find the percentage of cases that two simultaneous transmission was possible
Step 5: Change the normalized distance of primary pair to r+delta
  Redo the computations
Step 6: Plot the percentage of cases with respect to distance r

## Slide 11: CCA Regimes
Four CCA regimes are considered:
CCA threshold -72dbm
  Fixed power: Secondary STAs are not allowed to change their TX power
  Dynamic Power: Secondary STAs are provided with the channel knowledge so that they can compute the optimal transmit power that enables them to communicate without causing much interference to the primary pair if possible at all
    Note that this provides the best possible performance one can expect from dynamic CCA. The goal of this presentation is no to address how this information is provided. It is more along the direction of how much this best information can improve CCA regime
CCA threshold -82dbm
  Fixed Power
  Dynamic Power

## Slide 12: Results I (MAX TX powers= 15, 15, 15, 15 dBm)
Metric 2
Metric1

## Slide 13: Results I (TX powers= 15, 15, 5, 5 dBm)
Metric 2
Metric1

## Slide 14: Conclusion
A new evaluation method for analyzing CCA is proposed
  To capture the potential of spatial reuse which is prevented with the CCA
A simple scenario is considered to show the difference of a few CCA regimes (dynamic and static for aggressive -72dBm and conventional -82dBm)
  A brief comparison of these regimes presented with the new evaluation method
In these scenarios dynamic power optimization (one notion of dynamic CCA) seems to be less effective:
  CCA threshold of -72dBm provides good result, in fact it is less than 3% of locations that the secondary pair could utilize the medium and CCA prevents that
    Less than 10% in the case that STAs could also optimize their power
  This is even more significant where the secondary Transmitter an AP STA.
    Less than 3% opportunity to utilize the medium for secondary under dynamic CCA

## Slide 15: Appendix: What is potential gain of Spatial Reuse? [14/1580r0]
Contribution | PHY/MAC Modeling, SS, … | Results
14/779r2 | Path-loss considered | Improvement for Single apartment: 296%, double apartment 412%, cell structure network 800%
14/82r0, 83r0 | SS1. PHY system simulation, pathloss/shadowing considered, gene-based MCS selection, … | >2X gain in mean throughput and 2X gain in 5% throughput (UL and DL traffic) by increasing threshold to [-70,-60]dBm range
14/1427r2 | SS1-SS3. 50% UL & 50% DL traffic. PHY/MAC modeling | Increasing the CCA threshold provides throughput gains in the order of 20-40% (depending on the load levels) in all simulation scenarios except for S4
14/832r0 | SS1-SS3, Using MAC system simulation. Full buffer. Genie MCS selection. | About 2x-3x mean throughput increase for 11ax, and significant loss for legacy STAs
14/889r3 | SS1-SS3. PHY system simulation, no MAC modeling, gene-based MCS selection, … | 2X or greater feasible in many scenarios. For SS3, 5% throughput drops to zero for very aggressive CCA threshold
14/861r0 | SS1. Integrated PHY/MAC simulator. Separate DL/UL full buffer simulations | Mean throughput gains around 18-52% are observed
14/846r1 | SS1 with reuse 1. Pathloss/shadowing and no fading modeled. Full MAC modeling. Color bit. DL data. Full buffer UDP. | Difficult to optimize CCA for mean and 5% throughput. Optimum CCA=-72dBm for mean throughput, and CCA=-92/-82dBm for 5% throughput
14/1199r0 | SS1 with reuse 3 and 6. Pathloss/shadowing and no fading modeled. Full MAC modeling. Color bit. UL data. Full buffer UDP. | Reuse 3 and 6, no significant gain in optimizing mean throughput (vs -82dBm). 5%-throughput optimized at -72dBm for reuse 3, and at -82dBm for reuse 6.
14/866r1 | SS2. FTP in UL/DL with Poisson arrival with 80% vs 20% arrival ration in DL vs UL. | DSC in UL/DL offers 90% system capacity improvement, and TPC in UL/DL offers 77% system capacity improvement.
14/1171r1 | SS3. PHY/MAC modeling (?). No DL, 10 UL flows. | 36% Throughput gain, per-STA 5%-throughput reduces 94%
14/1426r2 | SS2. 50% traffic in DL and 50% in UL. | Increasing the CCA threshold from -82 to -62 provides 20-25% gain in average and 5th percentile user throughputs
14/372r2 | SS1. PHY/MAC modeling;. DSC and Color bits. | Compared to -82dBm, CCA=-62dBm offers 20-36% gain for mixed/11ax-only cases. Legacy STAs throughput drop by 48%.