## Slide 1: U-APSD Enhancements for HE
Date: 2015-03-06
Authors:

## Slide 2: Abstract
The submission contains a proposal to enhance U-APSD.
The enhancements targets to reduce protocol overheads.

## Slide 3: Power Save Mechanisms
The power save mechanisms for infrastructure mode are power save mode (PSM) transition and U-APSD
These mechanisms were not designed for 802.11ax
  Target is to avoid overhead and improve power efficiency
  Submission 11-14-1454r1 [1] describes some inefficiencies in power save mechanisms
Enhancements for U-APSD service period trigger and termination are proposed in next slides

## Slide 4: Challenges of Service Period Initiation
Currently all UL QoS data frames initiate a service period
  Unnecessary service periods are initiated
    The associated STA needs to be available during the service period
    The associated STA does not have control when it needs to be available for the AP
Some traffic models generate data frames mainly to one direction at a time
  Silent compression in VoIP, video streaming, …

## Slide 5: STA Controlled Service Period Initiation
An associated STA indicates to the AP if a Service Period is initiated
  UL frame contains a trigger bit
STA
AP
Qos Data frame (no trigger)
ACK / BA
STA may go to Doze. STA knows that AP will not transmit data to it.

## Slide 6: Challenges in Service Period Termination
If an AP does not have any frames to transmit to a STA a QoS-Null frame is required to terminate the service period
  The service period termination requires an acknowledged QoS Data frame with EOSP field = 1

## Slide 7: Improved Service Period Termination
The service period can be terminated with an ACK or Block ACK frame from the AP
  This enables immediate service period termination
  A DL QoS-Null frame to terminate a service period is not needed
Trigger/data frame
ACK
STA
AP
SP termination frame
ACK
Trigger/data frame
ACK /BA with SP termination
STA
AP
SP duration
SP duration
DOZE
DOZE

## Slide 8: Motion 1
Add following requirement to the section 6.1 Power Save of the SFD [2]:
A HE STA shall be capable to indicate in a trigger frame whether the frame initiates an U-APSD service period.

## Slide 9: Motion 2
Add following requirement to the section 6.1 Power Save of the SFD [2]:
A U-APSD service period shall be terminated when a HE AP transmits a frame (data, ACK, BA or management) with an indication to terminate the U-APSD service period.

## Slide 10: References
[1] 11-14-1454r1 Power Save Discussion
[2] 11-15-132 Spec Framework