## Slide 1: Microsleep for HE STA
Date: 2015-03-06
Authors:

## Slide 2: Abstract
The submission presents a microsleep mechanism that enables a non-AP STA to operate in Doze state while the channel is not available due to transmissions to other STAs.
Submission 11-14-1454r1 [1] discusses some challenges in power save mechanisms including microsleep.

## Slide 3: Legacy microsleep
Microsleep is a mechanism for a STA to be in Doze during other STAs transmissions
  STA knows that it cannot transmit or receive during the transmission
Microsleep drastically reduces power consumption

## Slide 4: Microsleep and HE
Simultaneous transmissions in HE make microsleep challenging
  A HE STA needs to be prepared to receive a transmission during an ongoing transmission

## Slide 5: HE microsleep solution
HE STA can microsleep when it knows that it is not able to receive from HE AP
  The HE STA indicates the STAs whose transmissions block reception from the HE AP
HE AP can microsleep when it knows that it cannot receive from any STA
  The HE AP indicates the STAs whose transmissions block reception from the HE STAs

## Slide 6: Motion
Add following requirements to the section 6.1 Power Save of the SFD [2]:
  The HE STA shall be capable to indicate the STAs whose transmissions block reception from the HE AP.
  The HE AP shall be capable to indicate the STAs whose transmissions block reception from the HE STAs.

## Slide 7: References
[1] 11-14-1454r1 Power Save Discussion
[2] 11-15-132 Spec Framework