## Slide 1: Throughput Comparison of Some Multi-user Schemes in 802.11ax
Date: 2015-03-13
Authors:

## Slide 2
Abstract
This contribution provides throughput calculations for some previously proposed MU OFDMA schemes [3, 4] with assumed preamble format, FFT size, MAC header size, and numerology from other previous contributions [1, 5, 6]. These calculations provide a performance comparison of MU-MIMO, OFDMA, and single user transmissions for both uplink and downlink transmissions with varying packet size, SNR and control frame overhead.

## Slide 3: Table of Contents
Introduction
Scenarios Considered and Channel Access Schemes
Throughput Calculations and Assumptions
Results
Summary

## Slide 4: Introduction
802.11 TGax has included MU transmissions in the 11ax Specification Framework Document [7].
TGax has discussed two types of MU transmissions OFDMA and MU-MIMO.
This contribution provides a throughput comparison between OFDMA and MU-MIMO for both downlink and uplink MU-transmission.

## Slide 5: Scenarios Being Considered
DL Scenarios:
  SU transmission
  DL MU-MIMO with simultaneous ACK
  DL OFDMA with simultaneous ACK
UL Scenarios:
  SU transmission
  UL MU-MIMO with simultaneous ACK
  UL OFDMA with simultaneous ACK

## Slide 6: SU and DL-MU Transmissions
DL-MU User Transmission (MIMO/OFDMA)
  AP acquires medium using CSMA/CA.
  AP transmits data to multiple users and receives simultaneous ACK
UL/DL Single User Transmission
    STA/AP acquires medium using CSMA/CA.
    STA/AP sends data and receives ACK
time
UL SU Data
Transmission
ACK
time
DL SU Data
Transmission
ACK
time
DL MU Data
Transmission
Simultaneous
Block ACK

## Slide 7: UL MU Transmission (MIMO/OFDMA)
Scheme 1: Full Control Frame Exchange
Use sequential RTS/CTS [3] or sequential inquiry/response [4] (FrameA/FrameB) exchanges between AP/STAs. AP sends Trigger/Poll frame (Frame C).
STAs send data and receive simultaneous block ACK
Scheme 2: Short Control Frame Exchange
One STA sends RTS (Frame B) and the AP polls the STAs (Frame C) [4]
STAs send data and receive simultaneous block ACK
time
time
Frame A
Frame B
Frame C
UL MU Data
Transmission
Simultaneous
Block ACK
Frame A
Frame B
...
N Frame A
/
Frame B exchanges
N = Number of Users

## Slide 8: Throughput Calculation
DL TxOP Duration
  MU = Data + SIFS + Simultaneous BA
  SU = Data + SIFS + ACK
UL TxOP Duration
  MU (scheme 1) = FrameA*N + FrameB*N + FrameC+ Data + SIFS*(2N+2) + BA
  MU (scheme 2) = FrameB+ FrameC+ DATA + SIFS*3+ BA
  SU TxOP Duration = Data + SIFS + ACK
  N = Number of Users
Throughput=Data Packet Size/(TXOP + DIFS + BO)*(1-PER)

## Slide 9: Assumptions
20 MHz channel with 256 FFT
Preamble format is from [1]
Nt = number of Transmit antennas
Parameter | Value
Bandwidth | 20MHz
FFT size | 256 [1]
# of data tones | 234 : 80 MHz 11ac numerology [5]
# of pilot tones | 8 : 80 MHz 11ac numerology [5]
GI | 3.2us [1]
DFT period for Data | 12.8 [1]
MAC header size | 30 Bytes [6]
# of antennas at AP side | 8
# of antennas at STA side | 1
MAC Frame (A/B/C) Size | Case 1: 25 Bytes, Case 2: 0 Bytes
MCS | Genie AMC [2]
802.11 parameter duration | Back-off: 3 slots (27 us), DIFS: 34 us
L-STF | L-LTF | L-SIG | HE-SIG-A | HE-LTF
8us | 8us | 4us | 12us | Nt x 16us
Preamble duration 48us
Overhead of UL control frames | Duration
Scheme 1, Case 1 | 880 us
Scheme 1, Case 2 | 448 us
Scheme 2, Case 1 | 208us
Scheme 2, Case 2 | 112us
Slide 9

## Slide 10
Observations
Packet size:
  Large packet: MU-MIMO is the most efficient at high SNR ranges
  Small packet: OFDMA is the most efficient over entire SNR range
SNR: At low SNRs, OFDMA always outperforms MU-MIMO
Analysis Results for DL

## Slide 11: Analysis results for UL, Scheme 1
Observations
For Scheme 1 (full control frame exchange), the performance gain over SU transmission is highly dependent on the control frame size.
Packet size:
  Large packet: MU-MIMO (case 2) is the most efficient at high SNR ranges
  Small packet: OFDMA (case 2) is the most efficient over entire SNR range

## Slide 12: Analysis results for UL, Scheme 2
Observations
For Scheme 2 (short control frame exchange), the performance gain over SU transmission is not as dependent on the control frame size as Scheme 1
Packet size:
  Large packet: MU-MIMO is most efficient at high SNR ranges
  Small packet: OFDMA is most efficient over entire SNR operation range

## Slide 13: Conclusion
The control overhead determines the gain of MU over SU transmissions
  Overhead is a function of the number and size of frames
    The channel access scheme determines the number.
    The design of the control information determines the size.
Performance of the MU schemes varies with packet size and operating SNR
  For large packets: MU-MIMO is the most efficient at high SNR ranges
  For small packet: OFDMA is the most efficient over entire SNR range
  OFDMA is more efficient than MU-MIMO at low SNRs for all packet sizes

## Slide 14
References
11-15/0099r4, Broadcom, Payload symbol size for 11ax
11-14/1186r2, InterDigital, Comparisons of Simultaneous Downlink Transmissions
11-14/1431r1, Newracom, Issues on UL-OFDMA
11-15/0064r0, Toshiba, Consideration on UL-MU overheads
IEEE P802.11ac™/D1.0: Part 11, Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) specifications. Amendment 5: Enhancements for Very High Throughput for Operation in Bands below 6 GHz
11-14/980r6, Qualcomm, Simulation Scenarios
11-15/132r2, Intel, Specification Framework

## Slide 15: Backup Slides

## Slide 16: Comparison Methodology
Link level PER simulation results
  DL-MU-MIMO: ZF transmit beamforming per subcarrier
  DL-OFDMA/SU: Single user transmit beamforming per subcarrier
  UL-MU-MIMO: MMSE receiver per subcarrier
  UL-OFDMA/SU: MRC per subcarrier
Comparison methodology
  For each SNR point, consider the maximum MCS which satisfies the PER constraint: PER<=1%
  Determine the TXOP duration by taking into account the maximum MCS, as well as signaling overhead:
    BA, BAR, SIFS, DIFS, ACK, backoff, etc.
Throughput= Data Packet Size/(TXOP duration+DIFS+BO) * (1-PER)

## Slide 17: Comparison Methodologies Cont’d
We assume
  Single stream transmission per user
  Fixed number of transmit antennas (eight).
  Fixed/variable number of users supported
    DL/UL OFDMA : Fixed at 4 users
    DL/UL MU-MIMO : Varied (up to 4) based on the maximum number of users/streams supported by the channel SNR
  Average random backoff of 3 slots
  CSI feedback overhead not included

## Slide 18: Multi-user Transmission
Multi-User MIMO
  Spatial domain multiple user separation (ZF, MMSE, non-linear etc.)
  DL MU-MIMO first introduced in IEEE 802.11ac.
  UL-MU-MIMO discussed but not adopted.
  Requires multiple transmit antennas
  DL MU-MIMO requires high precision Channel State Information at the Transmitter (CSIT)
OFDMA
  Frequency domain multiple user separation
  DL/UL have been discussed as a possible technology in several contributions
  Relaxed requirements for multiple transmit antennas
  CSIT requirements are reduced (may be used for scheduling gain)

## Slide 19: UL OFDMA Schemes, Taken from [3]
Multiple RTS/CTS exchange
  AP initiates RTS/CTS procedure for each STA sequentially.
Simultaneous CTS transmission with identical waveform
  .
AP1
STA1
STA2
RTS
CTS
RTS
CTS
Trigger
UL DATA
UL DATA
ACK*
ACK
TXOP duration
AP1
STA1
STA2
RTS
CTS
Trigger
UL DATA
UL DATA
ACK
ACK
TXOP duration
CTS

## Slide 20: UL OFDMA Schemes, Taken from [4]
Assume two approaches
AP
STA 1
STA 2
STA N_m
…
Poll
N_m: number of STAs multiplexed (4)
Inquiry
Resp.
Poll
…
≒RTS
≒CTS
Note: above conventional frames were used as substitutes for throughput calculation (may be too convenient)
ref. doc.11-14/0598
Inquiry
Resp.
Inquiry
Resp.
≒QoS CF-Poll
AP asks STAs one by one if they have Tx demands
method 1
method 2
TxReq
to N_m
STAs
…
≒RTS
≒CTS
Both exchanges in legacy rate (24 Mbps)