## Slide 1: A Framework for MIMO Operation over mmWave Links
Authors:
Name | Affiliation | Address | Phone | Email
Alireza Tarighat | Broadcom |  |  | atarighat@broadcom.com
Payam Torab | Broadcom |  |  | ptorab@broadcom.com
Brima Ibrahim | Broadcom |  |  | brima@broadcom.com
Vipin Aggarwal | Broadcom |  |  | vaggarwa@broadcom.com
Vinko Erceg | Broadcom |  |  | verceg@broadcom.com

## Slide 2: Contents
mmWave MIMO for NG60
Possible MIMO scenarios
  SVD multiplexing
  Multi-array beamforming
  Spatial aggregation
  Multi-array diversity
Impact of phase noise on SVD multiplexing
Conclusions

## Slide 3: Applicability of MIMO to mmWave
A 2x2 mmWave system deploys 2 TX arrays and 2 RX arrays.
  Each array may have N elements, but only two data feeds are available.
Each array has a programmable phase shifter that can be leveraged to change the MIMO channel seen by the 2x2 system.
  A major difference with sub-5GHz systems where omni elements are used.
  Additional knob available through changing array patterns.
RF TRX
RF TRX
RF TRX
RF TRX
2x2 MIMO
2x2 MIMO

## Slide 4: Scenario 1: SVD Multiplexing (SM)
Form a 2x2 MIMO System
Apply SVD with/without waterfilling
SVD Spatial De-Multiplexing
RF TRX
RF TRX
2-stream Decoder
SVD Spatial Multiplexing
RF TRX
RF TRX
2-stream Encoder

## Slide 5: Scenario 1: SVD Multiplexing (SM)
Two example usage cases
  High cross-interference between the streams (LOS MIMO & AWGN MIMO scenarios)
These two scenarios can be very common in outdoor deployments.
Device
Device
Device
Device
LOS
Blocker
Reflector
Reflector

## Slide 6: Scenario 1: SVD Multiplexing (SM)
SISO Capacity
1
x1
y1
TX Power: P

## Slide 7: Scenario 1: SVD Multiplexing (SM)
Line-of-Sight MIMO Capacity
x1
x2
y1
y2
Without waterfilling →
With waterfilling →
Where , and are the eigenvalues of
Phase delta (function of distance) →

## Slide 8: MIMO Capacity vs Phase Delta

## Slide 9: Scenario 1: SVD Multiplexing (SM)
Phase delta=180deg (maximizes capacity)
K=0dB

## Slide 10: Scenario 1: SVD Multiplexing (SM)
Phase delta=0deg (minimizes capacity)
K=0dB

## Slide 11: Scenario 1: SVD Multiplexing (SM)
TX arrays spacing=15cm
RX arrays spacing=20cm
K=0dB
Short range (low # of elements)

## Slide 12: Scenario 1: SVD Multiplexing (SM)
TX arrays spacing=15cm
RX arrays spacing=20cm
K=0dB
Long range (high # of elements)

## Slide 13: Scenario 2: Multi-Array Beamforming (MAB)
Form a larger single array by phase-aligning the two arrays
Transport a single stream at higher SNR
  9dB higher SNR compared to SISO case
Multi-Array Beamforming
RF TRX
RF TRX
1-stream Decoder
Multi-Array Beamforming
RF TRX
RF TRX
1-stream Encoder

## Slide 14: Scenario 2: Multi-Array Beamforming (MAB)
Two example usage cases
9dB SNR gain compared to single array case (6dB from TX and 3dB from RX)
At low SNR, scheme 2 outperforms scheme 1 without waterfilling
Device
Device
Device
Device
LOS
Blocker
Reflector

## Slide 15: SVD Multiplexing vs MAB
Multi-array beamforming (MAB) provides 9dB SNR gain compared to a single array case (6dB from TX and 3dB from RX)
At high SNR, SVD-SM outperforms MAB in terms of capacity.
At low SNR, MAB outperforms “SVD-SP w/o waterfilling” (with substantial delta)
At low SNR and under certain conditions, MAB outperforms “SVD-SP w waterfilling” (but with very marginal delta)
Multi-Array Beamforming (MAB) is simple to support from standard perspective (11ad nearly sufficient to support it)

## Slide 16: SVD Multiplexing vs MAB
SVD-SM can reach MAB performance at low SNR only with the help of waterfilling

## Slide 17: Scenario 3: Spatial Aggregation (SA)
SVD can be eliminated if sufficiently separated beams can be identified.
Simplified TX and RX implementation
May be defined as a mandatory mode (while making SVD-SM as optional)
RF TRX
RF TRX
2-stream Encoder
Optional Interference-Cancellation
RF TRX
RF TRX
2-stream Decoder

## Slide 18: Scenario 3: Spatial Aggregation (SA)
Example usage case
SA is a subset of SVD-SM
Use of interference cancellation in RX side is implementation and vendor choice.
Device
Device
Blocker
Reflector
Reflector

## Slide 19: Scenario 4: Multi-Array Diversity (MAD)
A sub-optimal configuration to MAB when MAB is not applicable.
  SNR is low for significant gain out of SVD-SM
  Link reliability/redundancy is a key metric
  Cross-interference between the multiple beams is relatively high
3dB diversity/energy combining gain compared to a single array case.
RF TRX
RF TRX
1-stream Encoder
Spatial Diversity Combining
RF TRX
RF TRX
1-stream Decoder

## Slide 20: Scenario 4: Multi-Array Diversity (MAD)
Example usage case
  Simple reliability improvement
  Energy combining gain
Device
Device
Blocker
Reflector
Reflector

## Slide 21: Summary of MIMO Scenarios
Mode | Number of data streams (Constellation-Level) | True MIMO Coding | Improved Merit of Figure | Some applicable usages
SVD Multiplexing (SM) -Closed Loop | Two | Yes | Throughput | Backhaul capacity, adjacent arrays, high SNR, polarization multiplexing
Multi-Array Beamforming (MAB) | Single | No | SNR | Backhaul range, adjacent arrays, low SNR
Spatial Aggregation (SA) -Open Loop | Two | No | Throughput | Indoor/Outdoor, polarization multiplexing when good separation available
Multi-Array Diversity (MAD) | Single | No | SNR | Indoor, distant arrays

## Slide 22: Phase Noise Impact on SVD Multiplexing
Phase noise seen by the multiple streams may only be partially correlated
  Cases that two different RFIC dies are deployed
An SVD-based multiplexing will experience cross-stream interference due to uncorrelated phase noise
  This effect is not seen in existing MIMO systems (such as 11ac)
Simulation scenario:
  Low-frequency “correlated phase noise” and high-frequency “uncorrelated phase noise”
  Integrated phase noise (uncorrelated portion) of 5 deg

## Slide 23: Phase Noise Impact on SVD Multiplexing

## Slide 24: Summary
All four “multi-radio” scenarios can be implemented using a common PHY framework.
Possible standard framework:
  Ability to generate 2 to 4 independent streams (no cross coding)
    Enables two modes of operation: transport data streams over the same frequency channel (spatial aggregation) or over different frequency channels (carrier aggregation)
  Ability to apply some form of “SVD coding” to generate 2 to 4 coded data streams
  This “waveform generation” framework enables following usages: SVD multiplexing (LOS/AWGN MIMO), polarization multiplexing, multi-array beamforming, spatial aggregation, carrier aggregation, multi-array diversity.
 | Same channel | Different channels
No TX cross-coding | Spatial aggregation | Carrier aggregation
TX cross-coding | SVD multiplexing | N/A