## Slide 1: 8K UHD Wireless Transfer Usage Model for NG 60
Date: 2015-03-06
Authors:
Name | Affiliation | Address | Email
Sang Gook Kim | LG Electronics | North America R&D Lab. SanDiego | sanggook.kim@lge.com
JangWoong Park |  | Seocho R&D Lab. Seoul, Korea | jangwong.park@lge.com
Do Kyun Kim |  |  | keneth.kim@lge.com
HanGyu Cho |  |  | hg.cho@lge.com

## Slide 2: Abstract
This contribution briefly provides evolution of high-resolution display and service, reviews wired interface solutions, and suggests 8K UHD wireless transfer usage model for NG60.

## Slide 3: High-resolution Display and Service Evolution
2012
2016
High-resolution Display
Broadcasting
Service
BBC, NHK
4K UHD (’12 London Olympic)
Korea
8K UHD (’18 PyeongChang Olympic)
KBS, SBS
4K UHD (’14 Brazil Worldcup)
IP streaming
Service
Amazon, Netflix, LG U+
4K UHD VoD Service (‘14)
2014
Qualcomm & Saffron Digital
4K UHD streaming in Snapdragon Tablet (CES 2015)
8K UHD Display and Services are nearly in market
LG
8K UHD (IFA 2014, CES 2015)
LG
4K UHD commercial (‘12)
2018

## Slide 4: Wired Solution for High-Resolution Display
VESA
MHL Consortium
HDMI Forum
HDMI 2.0
Link rate : up to 18Gbps
Max. Resolution : 4K@60p
DisplayPort 1.3
Link rate : up to 32.4Gbps
Max. Resolution : 8K@60p
superMHL
Link rate : unknown
Max. Resolution : 8K@120pCES 2015 (Realtime Demo b.w. TV and HDD)
http://www.hdmi.org/press/press_release.aspx?prid=133, http://www.vesa.org/uncategorized/vesa-releases-displayport-1-3-standard/
http://www.mhlconsortium.org/technology.aspx#superMHL
2013
2014
2015
HDMI 2.1
To support 8K
Wired interface solutions are ready to support 8K UHD

## Slide 5: NG 60 as a wireless solution for 8K UHD
Replacement of wired interface, wireless transfer from fixed/mobile devices for 8K UHD
TV or Display
(thin as <5mm)
Set-top box
(TV controller)
Blu-ray player
Smart phone/Tablet
Replacement of wired interface
Wireless Transfer from fixed device
Wireless Transfer from mobile device
NG 60

## Slide 6: How much Data Rate is required for 8K UHD resolution?
4K@60p
*bpp: bits per pixel
**: Chroma sampling
24 bpp*
4K@60p
30 bpp
4:2:0 **
4:4:4
8K@60p
24 bpp
8K@60p
24 bpp
4:2:0
4:4:4
8K@120p
24 bpp
4:4:4
8K@120p
30 bpp
4:4:4
7.13Gbps
17.82Gbps
28.51Gbps
142.55Gbps
57.02Gbps
114.05Gbps
Min. Required Data Rate for 8K

## Slide 7: How to achieve the data rate required for 8K UHD in NG60?
Data rate of 28.51 Gbps is required for 8K UHD.
Given that MAC efficiency is 70%, the minimum PHY rate required for 8K UHD is 40.73 Gbps which is about 6 times larger than 6.7Gbps of 11ad.
Technical requirements to support 8K UHD wireless transfer are
- Channel bonding of at least 2CH
- More than 2 spatial stream MIMO (if 2 CH is bonded, at least 3 spatial stream required)
- Higher order modulation (128 QAM, 256 QAM) is highly beneficial
- MAC efficiency enhancement is highly beneficial
 |  | Channel Bonding |  |  | 
 |  | 1 CH | 2CH | 3CH | 4CH
MIMO | 1 stream | 1X | 2X | 3X | 4X
 | 2 stream | 2X | 4X | 6X* | 8X
 | 3 stream | 3X | 6X | 9X | 12X
 | 4 stream | 4X | 8X | 12X | 16X
: Uncompressed 8K UHD feasible
*6X: 6 times increase of data rate
** Compression can be adopted to lighten the required rate, but, here is targeting the uncompressed case which might be considered in the product from the perspective of technology, cost, and etc.

## Slide 8: Usage Model: 8K UHD Wireless Transfer at Smart Home
Pre-Conditions:
NG60 is interfaced between a source device (e.g. set-top box, blu-ray player, tablet, smart phone) and a sink device (e.g. smart TV, thin display) to stream 8K UHD contents at home.
Environment:
Devices are operating in close proximity at home. Typical distance between devices are < 5m.
When it comes to the link between a set-top box and a thin display (or smart TV), the set-top box can be inside a table which may provide some SNR loss.
Application:
At least 40 Gbps PHY rate is required for a link to stream uncompressed 8K UHD streaming (60 frames per second, 24 bits per pixel, 4:2:2 Chroma sampling at minimum).
Traffic Conditions
Only a single link may exist at a time.
There is typically no interference from other mm-wave links at home.
Traffic is mostly unidirectional.
Use Case
Split TV: TV is on the wall as a thin display and set-top box works as a controller, wirelessly interfaced by NG60 to replace wired interfaces.
Smart display (Mirroring): Uncompressed 8K UHD streaming is through smart TV. 8K UHD video can be real-time transferred from smartphone/tablet to smart TV. When user enters home, the video which the user is watching in his/her smart phone is seamlessly played in the smart TV.
TV or Display
Set-top box
(TV controller)
Blu-ray player
Smart phone/Tablet
Replacement
of wired interface
Wireless Transfer
from fixed device
Wireless Transfer
from mobile device
8K UHD
Service

## Slide 9: Conclusions
We reviewed
8K UHD is nearly in market.
Wired interface solutions are ready to commercialize 8K UHD.
We provided technical requirements for 8K UHD
At least 6 times data rate enhancement required
Channel bonding, MIMO, and some PHY/MAC enhancements necessary
We believe that NG60 is the best candidate wireless standard for 8K UHD and proposed an usage model.

## Slide 10: References
[1] http://www.hdmi.org/press/press_release.aspx?prid=133
[2] http://www.vesa.org/uncategorized/vesa-releases-displayport-1-3-standard/
[3] http://www.mhlconsortium.org/technology.aspx#superMHL

## Slide 11: Back-up: Video Resolution
SD
(720x576)
HD
(1280x720)
Full HD
(1920x1080)
Quad HD
(3840x2160)
4K
(4096x2160)
8K
(7680x4320)