## Slide 1: Bandwidth granularity on UL-OFDMA data allocation
Date: 2015-03-09
Authors:

## Slide 2: Introduction
UL-OFDMA is included in Spec Framework Document for 11ax [1],[2]
  Key enabling technique to meet the requirement of throughput enhancement
  Simultaneous transmission from multiple STAs to AP
  It is necessary to decide how to support UL data transmitted by multiple STAs
Bandwidth granularity of multiple UL data allocation
  Considering wideband, larger FFT size
20MHz based or sub-channel based

## Slide 3: UL-OFDMA procedure
Initiation (AP)
  UL-OFDMA procedure start indication
  Synchronization of UL-OFDMA procedure
  Channel availability indication of AP
  Duplicated for available channel from AP’s perspective
Scheduling (AP, STAs)
  STA
    Medium contention (Resource request)
    Channel availability indication of STAs
    UL-data length and AC indication
  AP
    Resource (Channel) allocation
  Explicit or implicit

## Slide 4: How do we develop UL-OFDMA procedure?
The very first step of designing UL-OFDMA
Procedural detail may vary depending on the target environment/situation/traffic/STA
Among these ingredients, we more focus on how many STAs can be allowed in a single UL-OFDMA session
  The number tx-STAs can be determined by bandwidth granularity of UL-data allocation

## Slide 5: Multiple STAs’ UL bandwidth occupation in UL-OFDMA
In conventional 802.11, minimum bandwidth occupation is 20HMz
  Only one tx-STA is allowed
  Control mechanism/signaling/frame structure have been designed based on 20MHz channel
DL-OFDMA of 11ax is considering to support finer granularity of bandwidth occupation [3], [4], [5], [6]
Finer bandwidth occupation could also be considered for UL-OFDMA
  Multiple non-AP STAs to 1 AP
Signaling/control mechanism/frame structure might vary depending on the channel occupation structure

## Slide 6: 20MHz based UL-OFDMA
Only 1 STA per 20MHz channel
  The winner of contention at each channel will participate UL-OFDMA
    Similar to conventional 802.11 medium contention
  Less complexity
  Relatively short scheduling duration per UL-OFDMA session
Assigned STA may exploit the control information in L/HE preamble exclusively
  Easier to design and implement

## Slide 7: 20MHz based UL-OFDMA –drawbacks (1)
Contention isolation gain decreases
  The number of UL-OFDMA STAs is the same as available channel
  No contention isolation gain for single 20MHz channel
The smaller data size, the less spectral efficiency
  Tdata/(Tdata +Toverhead)
  UL-OFDMA may introduce increased overhead (e.g., initiation, scheduling)
  The proportion of UL-OFDMA overhead will increase as the data size decreases
  Traffic measurement on packet size reveals that packet size is <66B with >75% chance for UL [7]

## Slide 8: 20MHz based UL-OFDMA –drawbacks (2)
Inflexible and inefficient resource allocation
  AP cannot transmit ACK while it receives UL data through another channel
  Every UL data must be timely aligned (e.g., zero padding, data repetition)
  The greater difference of data size among UL-OFDMA STAs, the less spectral efficiency

## Slide 9: Sub-channel based UL-OFDMA
Multiple UL STAs on a single channel
More contention isolation gain
  The ratio of contention and collision increases drastically as the network gets denser[8]
  The number of contention period could be reduced by 1/M (M: max. number of STAs per 20MHz channel)
  Contention reduction could be a key feature to enhance Tput as the network gets denser [9]
More spectral efficiency
  The airtime of data will increase as the occupied bandwidth gets narrower
  The ratio of control overhead to data will decrease

## Slide 10: Sub-channel based UL-OFDMA
More flexibility in resource allocation
  Finer granularity of channel allocation
  Depending on the data size of each STA, different size of sub-channels can be assigned
  Less zero padding or data repetition is required for time alignment of data period
Sub-channel based UL-OFDMA seems more preferable in order to meet the tput requirement of 11ax PAR
There are some issues and concerns on implementing sub-channel based UL-OFDMA

## Slide 11: Granularity of bandwidth occupation
It seems possible to allow ½, ¼, 1/8 of current channel bandwidth(10/5/2.5 MHz)
5GH ISM regulation of ETSI [10]
  4.3.2 Limits The Nominal Channel Bandwidth shall be at least 5 MHz at all times. The Occupied Channel Bandwidth shall be between 80 % and 100 % of the declared Nominal Channel Bandwidth. In case of smart antenna systems (devices with multiple transmit chains) each of the transmit chains shall meet this requirement. During an established communication, the device is allowed to operate temporarily with an Occupied Channel Bandwidth below 80 % of its Nominal Channel Bandwidth with a minimum of 4 MHz.
  Should 5MHz be the minimum bandwidth occupation?

## Slide 12: L-preamble transmission
L-preamble should be sent on 20MHz channel with 64 FFT size
  Used for delivering common control information of single transmitter
1. A chosen STA transmits L-preamble as a representative of the PPDU
  Might influence the decoding performance of STAs without L-preamble
2. Every STA sends identical L-preamble
  Different delay spread might degrade the decoding performance
  Common control information should be shared among UL STAs in advance

## Slide 13: HE preamble structure for sub-channel based UL-OFDMA
Should HE-SIG A also contain common control information for every STA on 20MHz channel?
  TX-specific information should be contained in latter field of HE preamble (including training sequence, control information) ①
  With proper protection mechanism from legacy STAs, L preamble and HE-SIG A might be dropped ②
    Corresponding information must be negotiated before data transmission
HE-SIG A might be designed with the minimum size of channel occupation ③
  TX-specific information might be included for every STA
  HE-SIG A for STA with multiple sub-channel might be duplicated on every assigned sub-channel
①
②
③

## Slide 14: Conclusion
UL-OFDMA is likely to become one of the most important feature of 11ax in terms of throughput enhancement
It is necessary to decide bandwidth occupation pattern for UL-OFDMA in advance to design procedural detail
We have discussed the way of deployment of multiple STA’s UL data
  20MHz based / sub-channel based
In terms of Tput enhancement, sub-channel based UL-OFDMA seems more preferable
  Adjustment for sub-channel based operation should be followed

## Slide 15: References
[1][14/1453/r2] Spec Framework Proposal
[2][14/1447/r1] Proposed Spec Framework Document for 11ax considering potential tech features
[3] [14/1452/r0] Frequency selective scheduling in OFDMA
[4] [15/0082/r1] Considerations on 11ax OFDMA Frequency Granularity
[5] [15/0305/r0] Effective Subcarrier Assignment for DL-OFDMA
[6] [15/0092/r1] DL-OFDMA Procedure in IEEE 802.11ax
[7] [14/1232/r1] On Multi-STA Aggregation Mechanisms in 11axOn Multi-STA Aggregation Mechanisms in 11ax
[8] Sakurai, Taka, and Hai L. Vu. "MAC access delay of IEEE 802.11 DCF."Wireless Communications, IEEE Transactions on 6.5 (2007): 1702-1710.
[9] [14/1442/r1] Considerations on DL OFDMA control mechanism
[10] ETSI EN 301 893 V1.8.0

## Slide 16: Strawpoll
UL-OFDMA shall support UL data allocation below 20MHz for an HE STA
Y/N/A