## Slide 1: Clarification of MIMO Box2 calibration
Date: 2015-03-06
Authors:

## Slide 2: MIMO Box 2 Calibration
4 Scenarios
  3 test cases per scenario
    Test 1 (Interference free): CDF for per-tone SINR and effective SINR
    Test 2 (Interference only on DL): CDF for per-tone SINR and effective SINR
    Test 3 (CCA, Interference on DL/UL): CDF for per-tone SINR and effective SINR on DL, CDF for per-tone SINR and effective SINR on UL
Channel model (Default)
  Scenario 1/2/3: 11n Channel model D
  Scenario 4: ITU UMi
MIMO configuration
  2x2 antenna configuration

## Slide 3: Per-Tone Post Processing SINR
For MIMO configuration,
  STA j in AP i
  k-th layer per-tone post processing SINR with linear receiver
: Co-stream interference
: Interference from other STAs/APs
: linear receive filter
: precoding matrix
: precoding matrix for k-th layer
: covariance

## Slide 4: Precoding Matrix & Receiver Filter?
However, current EMD [1] does not describe how to decide precoding matrix & receiver filter clearly.
  MIMO calibration result could be differentiated according to precoding matrix & assumptions on receiver
  There are few receive filter options for calibration purpose
  There are few precoding options for calibration purpose:
    Genie selection (i.e. full rank, right sided SVD matrix based on channel of the intended link only)
    No precoding matrix (full rank, identity matrix)
    Some fixed matrix

## Slide 5: MMSE Receiver Assumption
Proposed that MMSE receiver is used for calibration purpose.
  Proposed Baseline:
    Option 1:
    Option 2:
    Option 3: (suggested assumption for calibration)

## Slide 6: LSP correlation for link from STA(AP) to STA(AP) in Scenario 4
In ITU channel model, LSP (Large Scale Parameter) is correlated based on geometrical distance.
  And, in general, exponential filter is used to reduce calculation complexity, in which determined geometrical random values are filtered and their location is not related to number of links.
  However, current ITU channel model does not clearly show the correlation for link from AP to AP or from STA to STA.
  ‘AP to AP’ seems uncorrelated circumstances since distance between AP to AP is quite big.
  ‘STA to STA’ seems quite complex since the number of STAs is too much.
    How to handle this?

## Slide 7: Conclusion
Receiver filter assumption is not clear in MIMO Box 2 calibration
  We propose to use the most basic assumption, MMSE receive filter with only co-stream interference covariance estimation, for calibration purposes.
Precoding matrix selection rule is not clear in MIMO Box 2 calibration
  Precoding matrix selection rule should be described in EMD
  For simplicity reasons, we prefer to have no precoding matrix (i.e. full rank identity matrix) for calibration.
LSP correlation
  We need verification of the ‘AP to STA’ LSP correlation and concrete description on ‘AP to AP’ links and ‘STA to STA’ links.
  To simplify the calibration, we propose the following
    ‘AP to STA’: LSP is correlated using distance based correlation between ‘BS and UE’ in ITU UMi/UMa model
    ‘AP to AP’: LSP is uncorrelated
    ‘STA to STA’: LSP is uncorrelated
  However, simplified assumptions may not reflect reality well. We would like feedback from TGax members on this issue.

## Slide 8: Straw Poll #1
What should be the receiver assumption for MIMO Box 2 “calibration” purposes?
  MMSE receiver with ideal interference rejection (Option 1 in slide)
  MMSE receiver with only co-spatial-stream interference rejection (Option 3 in slide)
  Need further discussion

## Slide 9: Straw Poll #2
What should be the precoding matrix assumption for MIMO Box 2 “calibration” purposes?
  No precoding (i.e. full rank transmission with identity matrix as precoding matrix)
  Genie precoding (i.e. full rank transmission with right sided SVD matrix based on channel matrix of the intended signal link)
  Something else (e.g. some fixed precoding rank 1 vector)
  Need further discussions

## Slide 10: Straw poll #3
What is the current understanding of the LSP correlation conditions between ‘AP to STA’ for MIMO Box 2?
  Distance based correlation (based on ITU M.2135 correlation between ‘Base Station and User Terminal’
  Uncorrelated
  Undefined in the EMD and therefore interpretation left up to each individual contributor

## Slide 11: Straw Poll #4
What should be the LSP correlation conditions for MIMO Box 2? For options with correlation, the assumption is that correlation shall be based on the distance-based-correlation defined for ‘BS and UT’ in ITU M.2135
  ‘AP to AP’ uncorrelated & ‘STA to STA’ uncorrelated
  ‘AP to AP’ correlated & ‘STA to STA’ correlated
  ‘AP to AP’ uncorrelated & ‘STA to STA’ correlated
  ‘AP to AP’ correlated & ‘STA to STA’ uncorrelated
  Need further discussions

## Slide 12: References
[1] https://mentor.ieee.org/802.11/dcn/15/11-14-0571-07-00ax-evaluation-methodology.docx