## Slide 1: MAC calibration test 4 simulation results
Date: 2015-03-08
Authors:

## Slide 2: Abstract
This submission provides simulation results for MAC calibration test case 4 [1]

## Slide 3: Test 4: Deferral Test for 20 and 40MHz BSSs [1]
BSS1 and BSS2 are co-located
BSS1 operates on 40MHz mode
  Full buffer traffic
BSS2 operates on 20MHz mode, primary channel is the same as BSS1 secondary channel
  Poisson distributed traffic, theoretical avg. 1.6Mbps
Parameters as in 0980r6 ”Simulation Scenarios” [1]
  MSDU length: [2000Bytes]
  RTS/CTS for BSS2: [ON/OFF]
  MCS: [0]
STA 1
AP 2
AP1
STA 2
(AP1 and STA2 are essentially co-located)
AP1 -> STA1
AP2 -> STA2
BSS1 Prim. Ch.
BSS2 Prim. Ch.
AP1 -> STA1
Time
ACK
ACK
ACK

## Slide 4: The percentage of time the 40MHz BSS running in 40 and 20 MHz mode
TX
TX
TX
TX
Primary
Secondary
T1
T2
T3
T4
Percentage_40Mhz = 100 x (T2+T4)/(T1+T2+T3+T4)
Percentage_20Mhz = 100 x (T1+T3)/(T1+T2+T3+T4)
Example: AP1 transmits to downlink:

## Slide 5: Simulation results for Test 4:
 |  | RTS CTS [ON/OFF] | MAC Tput [Mbps] | Time in 40MHz [%] | Time in 20MHz [%]
Simulation 1 | AP1 | OFF | 8.9 | 46.7 | 53.3
 | AP2 | OFF | 1.6 | 0.0 | 100.0
Simulation 2 | AP1 | OFF | 8.9 | 46.6 | 53.4
 | AP2 | ON | 1.6 | 0.0 | 100.0

## Slide 6: References
[1] IEEE 802.11-14/0980r6 – Simulation Scenarios

## Slide 7: Appendix: TX times in seconds
 |  | RTS CTS [ON/OFF] | Mode [20MHz/40MHz] | TX time [s]
Simulation 1 | AP1 | OFF | 20MHz | 50.6
 |  |  | 40MHz | 44.4
 | AP2 | OFF | 20MHz | 26.2
 |  |  | 40MHz | 0.00
Simulation 2 | AP1 | OFF | 20MHz | 50.7
 |  |  | 40MHz | 44.3
 | AP2 | ON | 20MHz | 26.0
 |  |  | 40MHz | 0.00
LI=LISTEN, RX=RECEIVING,TX=TRANSMITTING
SIMULATION TIME = 100s

## Slide 8: Appendix: power states percentages
 |  | RTS CTS [ON/OFF] | LI [%] of simulation time | RX [%] of simulation time | TX [%] of simulation time
Simulation 1 | AP1 | OFF | 3.4 | 1.8 | 94.9
 | STA1 |  | 3.4 | 94.9 | 1.8
 | AP2 | OFF | 72.6 | 1.3 | 26.2
 | STA2 |  | 73.2 | 26.1 | 0.6
Simulation 2 | AP1 | OFF | 3.4 | 1.8 | 94.9
 | STA1 |  | 3.4 | 94.9 | 1.8
 | AP2 | ON | 72.3 | 1.7 | 26.0
 | STA2 |  | 72.4 | 26.6 | 1.0
LI=LISTEN, RX=RECEIVING,TX=TRANSMITTING
SIMULATION TIME = 100s