## Slide 1: MAC Calibration Results
Date: 2015-03-8
Authors:

## Slide 2: Abstract
This contribution summarizes our simulation results for test case 1-3 according to 802.11ax Simulation Scenarios document (11-14-0984-06)
The results are compared with previous contributions and match well with previous simulation results

## Slide 3: Test 1a: Application Throughput Comparison (Mbps)
Contribution #1 | MCS 0 |  |  |  | MCS 8 |  |  | 
 | 500 | 1000 | 1500 | 2000 | 500 | 1000 | 1500 | 2000
11-14/0600r0 | 4.76 | 5.53 | 5.82 | 5.98 | 23.92 | 37.25 | 45.55 | 50.81
11-14/1147r0 | 4.79 | 5.54 | 5.84 | 6.00 | 22.00 | 35.00 | 43.20 | 48.40
11-14/1175r1 | 4.81 | 5.55 | 5.84 | 5.99 | 22.4 | 35.2 | 43.25 | 48.9
11-14/1191r0 | 4.79 | 5.55 | 5.84 | 6.00 | 21.98 | 34.91 | 43.24 | 48.67
11-14/1217r0 | 4.76 | 5.52 | 5.83 | 5.97 | 21.19 | 34.22 | 41.93 | 47.74
11-14/1230r2 | 4.76 | 5.53 | 5.82 | 5.98 | 21.71 | 34.65 | 42.71 | 48.15
11-14/1342r1 | 4.79 | 5.55 | 5.84 | 5.99 | 21.99 | 34.94 | 43.27 | 48.68
11-14/1449r0 | 4.85 | 5.55 | 5.84 | 5.99 | - | - | - | -
11-15/0022r1 | 4.79 | 5.55 | 5.84 | 6.00 | 21.94 | 34.87 | 43.19 | 48.66
This contribution | 4.80 | 5.55 | 5.84 | 5.99 | 21.96 | 34.7 | 43.4 | 48.5

## Slide 4: Test 1b: Application Throughput Comparison (Mbps)
Contribution #5.84 | MCS 0 |  |  |  | MCS 8 |  |  | 
 | 500 | 1000 | 1500 | 2000 | 500 | 1000 | 1500 | 2000
11-14/0600r0 | 4.40 | 5.29 | 5.64 | 5.84 | 18.64 | 30.75 | 38.94 | 44.51
11-14/1147r0 | 4.42 | 5.30 | 5.67 | 5.85 | 16.00 | 27.10 | 34.97 | 40.40
11-14/1175r1 | 4.45 | 5.31 | 5.66 | 5.86 | 16.20 | 27.30 | 35.00 | 40.80
11-14/1191r0 | 4.42 | 5.31 | 5.66 | 5.85 | 15.94 | 27.07 | 34.97 | 40.61
11-14/1217r0 | 4.40 | 5.28 | 5.64 | 5.83 | 15.52 | 26.66 | 34.12 | 39.96
11-14/1230r2 | 4.40 | 5.29 | 5.64 | 5.84 | 15.79 | 26.90 | 34.62 | 40.24
11-14/1342r1 | 4.42 | 5.31 | 5.66 | 5.85 | 15.94 | 26.97 | 34.99 | 40.63
11-14/1449r0 | 4.43 | 5.27 | 5.62 | 5.82 | - | - | - | -
11-15/0022r1 | 4.43 | 5.31 | 5.66 | 5.85 | 15.95 | 27.09 | 35.00 | 40.57
This contribution | 4.45 | 5.31 | 5.66 | 5.84 | 15.94 | 27.1 | 34.90 | 41.43

## Slide 5: Test 2a: Application Throughput Comparison (Mbps)
Contribution # | RTS/CTS Off |  |  |  | RTS/CTS On |  |  | 
 | 500 | 1000 | 1500 | 2000 | 500 | 1000 | 1500 | 2000
11-14/0600r0 | 4.57 | 5.26 | 5.53 | 5.67 | 4.45 | 5.32 | 5.67 | 5.86
11-14/1147r0 | 4.58 | 5.25 | 5.45 | 5.66 | 4.49 | 5.35 | 5.70 | 5.88
11-14/1175r1 | 4.62 | 5.28 | 5.54 | 5.66 | 4.50 | 5.34 | 5.68 | 5.88
11-14/1191r0 | 4.56 | 5.25 | 5.51 | 5.66 | 4.46 | 5.33 | 5.68 | 5.87
11-14/1217r0 | 4.58 | 5.29 | 5.56 | 5.71 | 4.48 | 5.32 | 5.67 | 5.85
11-14/1230r2 | 4.71 | 5.48 | 5.78 | 5.94 | 4.35 | 5.24 | 5.62 | 5.81
11-14/1342r1 | 4.59 | 5.28 | 5.55 | 5.68 | 4.47 | 5.31 | 5.65 | 5.87
11-14/1449r0 | 4.80 | 5.49 | 5.77 | 5.93 | 4.39 | 5.22 | 5.57 | 5.77
11-15/0022r1 | 4.64 | 5.29 | 5.55 | 5.70 | 4.47 | 5.36 | 5.71 | 5.87
This contribution | 4.64 | 5.28 | 5.48 | 5.66 | 4.51 | 5.34 | 5.68 | 5.86

## Slide 6: Test 2b: Application Throughput Comparison (Mbps)
Contribution # | MCS 0 |  | MCS 8 | 
 | No Frame Aggregation | Frame Aggregation | No Frame Aggregation | Frame Aggregation
11-14/0600r0 | - | 0.98 | - | -
11-14/1147r0 | - | 1.06 | - | -
11-14/1175r1 | 1.70 | 1.02 | 26.80 | 35.00
11-14/1191r0 | 1.62 | 1.01 | 26.54 | 34.75
11-14/1217r0 | - | 1.20 | - | 35.66
11-14/1230r2 | - | 0.04 | - | -
11-14/1342r1 | 1.62 | 0.95 | 28.85 | 33.96
11-14/1449r0 | - | 1.03 | - | -
11-15/0022r1 | - | 1.38 | - | 23.61
This contribution | 1.59 | 1.08 | 26.30 | 33.67

## Slide 7: Test 3: Application Throughput Comparison (Mbps)
Contribution # | MCS 0 |  | MCS 8 | 
 | No Frame Aggregation | Frame Aggregation | No Frame Aggregation | Frame Aggregation
11-14/0600r0 | - | 5.55 | - | -
11-14/1147r0 | - | 5.40 | - | -
11-14/1175r1 | 5.14 | 5.58 | 22.40 | 34.20
11-14/1191r0 | 5.15 | 5.58 | 22.04 | 34.05
11-14/1217r0 | - | 5.59 | - | 31.35
11-14/1230r2 | - | 5.64 | - | -
11-14/1342r1 | 5.19 | 5.61 | 21.64 | 33.82
11-14/1449r0 | - | 5.78 | - | -
11-15/0022r1 | - | 5.80 | - | 22.92
This contribution | 5.10 | 5.59 | 21.05 | 33.86

## Slide 8: Conclusion
  MAC calibration simulation results for Tests 1a, 1b, 2a, 2b, and 3 are provided which match well with previous contribution results

## Slide 9: References
[1] IEEE 802.11-14/0980r5, Simulation Scenarios, Simone Merlin et. al., November 2014.
[2] IEEE 802.11-14/0571r6, Evaluation Methodology, Ron Porat et. al., November 2014.
[3] IEEE 802.11-14/0600r0, MAC Simulator Calibration, Gwen Barriac et. al., May 2014.
[4] IEEE 802.11-14/1147r0, MAC Simulator Calibration Results, Shoko Shinohara, et. al. September 2014.
[5] IEEE 802.11-14/1175r1, MAC Calibration Results, Suhwook Kim, et. al., September 2014.
[6] IEEE 802.11-14/1191r0, MAC Calibration Huawei Results, Yanchun Li, et. al., September 2014.
[7] IEEE 802.11-14/1192r3, Comparing MAC Calibration Results, Yanchun Li, et. al., October 2014.
[8] IEEE 802.11-14/1217r0, MAC Calibration Results for Tests 1 and 2, Esa Tuomaala, et.al., September 2014.
[9] IEEE 802.11-14/1230r2, MAC Calibration Result, Chinghwa Yu, et. al., September 2014.
[10] IEEE 802.11-14/1342r1, MAC Calibration Results, Igor Kim, et. al., November 2014.
[11] IEEE 802.11-14/1449r0, MAC Calibration Results, Vida Ferdowsi, et.al., November 2014.
[12] ] IEEE 802.11-54/0022r1m MAC Calibration Results, Kome Oteri et. al., November 2015