## Slide 1: Further Considerations on Legacy Fairness with Enhanced CCA
Date: 2015-03-10
Authors:

## Slide 2: Abstract
In [1], we investigated legacy fairness issues of enhanced CCA.
Legacy STA’s throughput can be starved from HE STA’s increased CCA threshold and continuous channel occupation.
In this contribution, we evaluate two fairness methods:
  Legacy Frame Protection [2] where HE STA does not apply increased CCA threshold on legacy frames;
  PPDU Size Reduction where HE STA limits its PPDU sizes (or TXOP duration [3]) when they obtain a channel with increased CCA threshold.
From simulation studies, we show that the above methods effectively mitigate legacy starvations up to moderate CCA threshold levels.
Also, we report a new contention unfairness that may become severe when there are multiple HE STAs around Leg STAs.

## Slide 3: Recap: Legacy Fairness Issues [1]
HE
Leg
HE
HE
Leg
Data
Data
Data
defer
backoff
backoff
HE
Leg
Data
Data
defer
backoff
HE
Leg
Data
Data
backoff
HE
1. CCA threshold unfairness
2. Airtime unfairness
HE STA applies increased CCA threshold on Legacy frames
HE STA can continuously access the channel thus unfair to Legacy STA
 (Solution) Legacy Frame Protection
Two HE STAs apply increased CCA threshold on mutual HE frames
HE STAs can continuously occupy the channel thus unfair to Legacy STA
 (Solution) PPDU Size Reduction
CCA (e.g. -62dBm) range of HE STA
CCA (e.g. -82dBm) range of Legacy STA
defer
backoff

## Slide 4: Fairness Provisioning Methods
Legacy Frame Protection
HE STA applies increased CCA threshold when OBSS HE frame is observed
HES STA applies the legacy CCA threshold when non-HE frame is observed
PPDU(TXOP) Size Reduction
For PPDU transmission, HE STA limits its PPDU size to the OBSS HE PPDU (e.g. limiting the # of MPDUs in A-MPDU)
Data
Data
backoff
backoff
HE
Leg
Data
Data
backoff
HE
Data
defer
defer
remaining
backoff
backoff
backoff
If RSSI>=“CCA-SD”,
If preamble passes,
If MYDATA, receive the packet.
If OBSS HE PPDU, apply “CCA-SD-HE”
If MYBSS HE PPDU, apply “CCA-SD”
If non-HE PPDU, apply “CCA-SD”
If preamble fails, apply “CCA-ED”
Data
Data
back
off
HE
Leg
Data
HE
Data
Data
Data
Data
TXOP
TXOP
For TXOP-based transmission, HE STA limits its TXOP duration to the OBSS HE STA’s TXOP duration [3][7]

## Slide 5: Simulation Settings
Topography/Channel Model [4][5]
  1 floor, 1x2 apartments per floor, each apt. is 10m x 10m x 3m
  1 AP, 4 STAs per apt. (1 HE STA, 3 Legacy STAs)
  AP/STA at random (x,y) locations, all with z=1.5
  5GHz, all BSS has the same 80MHz channel (Reuse 1)
  Pathloss model with Wall/Floor penetration loss, 5dB std log-normal shadowing, no multipath fading
Traffic
  DL+UL full buffer
  Packet size: 1500 Byte, Max # of MPDUs in A-MPDU=8
  MCS: Fixed MCS 0
CCA threshold
  CCA-SD: -82dBm
  CCA-SD-HE: -82, -72, -62, -52 dBm
HE
Leg
HE
HE
Leg
HE
Leg
Leg
Leg
Leg

## Slide 6: Throughput & Fairness
Without fairness method
  large unfairness between HE STA vs. Leg STA (starvation of Leg STA) as CCA threshold increases.
LFP (Legacy Frame Protection) only
  prevent legacy starvation up to moderate CCA threshold (-72dBm).
LFP+PSR (PPDU Size Reduction)
  prevent legacy starvation up to high CCA threshold (-62dBm).

## Slide 7: Contention unfairness
Contention unfairness
  HE STA can decrement its Contention Window value sensing “idle channel” with increased CCA threshold.
  Leg STA cannot decrement its Contention Window value sensing “busy channel” with legacy CCA threshold.
  It becomes severe when Leg STA is with many HE STAs in a BSS.
HE
2
Leg
X
HE
HE
Leg
HE
HE
3
HE
HE1
HE
Data
HE
1
Leg
X
Data
Data
backoff
HE
backoff
Data
HE
2
remaining backoff
HE
3
backoff
backoff
backoff
defer
defer
remaining backoff
defer
defer
backoff
defer
defer
3HE-1Leg Case
Example

## Slide 8: Summary
Legacy fairness is an important requirement when 11ax designs spatial reuse technologies.
In this contribution, we demonstrated that previously discussed two fairness methods can preserve legacy fairness.
We also identified the Contention unfairness issue that needs further discussions in 11ax.

## Slide 9: References
  [1] 11-15/0085r1, Legacy Fairness Issues of Enhanced CCA
  [2] 11-14/0629r0, Further discussions on Enhanced CCA
  [3] 11-14/0637r0, Spatial Reuse and Coexistence with Legacy Devices
[4] 11-14/0980r6, Simulation Scenarios
[5] 11-14/0571r7, Evaluation Methodology
[6] Jain, R.; Chiu, D.M.; Hawe, W. (1984). "A Quantitative Measure of Fairness and Discrimination for Resource Allocation in Shared Computer Systems". DEC Research Report TR-301.
[7] IEEE 802.11ah D4.0, 9.50.4 TXOP-based sectorization operation