## Slide 1: Considerations on UL MU resource scheduling
Authors:
Name | Affiliations | Address | Phone | Email
Leonardo Lanante | Kyushu Institute of Technology | 〒820-8502 Kawazu 680-4, Iizuka City, Fukuoka Japan | +81-948-29-7692 | leonardo@cse.kyutech.ac.jp
Tran Thi Thao Nguyen | Kyushu Institute of Technology | 〒820-8502 Kawazu 680-4, Iizuka City, Fukuoka Japan | +81-948-29-7692 | nguyen@dsp.cse.kyutech.ac.jp
Tatsumi Uwai | Radrix co.ltd | 〒820-8502 Incubation Facilities, Kawazu 680-4, Iizuka City, Fukuoka Japan | +81-948-29-7937 | uwai@radrix.com
Yuhei Nagao | Radrix co.ltd | 〒820-8502 Incubation Facilities, Kawazu 680-4, Iizuka City, Fukuoka Japan | +81-948-29-7937 | nagao@radrix.com
Hiroshi Ochi | Kyushu Institute of Technology | 〒820-8502 Kawazu 680-4, Iizuka City, Fukuoka Japan | +81-948-29-7692 | ochi@cse.kyutech.ac.jp
Date: 2015-03-09

## Slide 2: Abstract
UL MU transmission such as OFDMA is currently being considered in 11ax [1].
Parameters such as bandwidth, number of subcarriers per resource block, and number of parallel STAs have not been decided.
We are presenting some simulations that would help decide some of these parameters.
In addition, we show that OFDMA performance suffer when only a few number of active STAs are present. We present a solution to the said problem.

## Slide 3: OFDMA resource block scheduling
In SU case, the whole subcarrier set is used by only 1 STA
In MU case, a group of subcarriers which we call resource block (RB) are allotted to multiple STAs depending on specific criteria.
SU STA
STA 1
STA 2
STA 3
STA 5
STA 4
RB 1
RB 2
RB 3
RB 4
Single user
Multi-user

## Slide 4: OFDMA resource block scheduling
In the figure below, there are 5 active STAs competing for N=4 RBs. We then allot an RB depending on the STA with strongest channel on that RB.
RB 1
RB 2
RB 3
RB 4
BER performance will approach AWGN channel
As the number of active STAs increase with respect to the number of RB, AWGN BER performance can be obtained.
STA 1
STA 2
STA 3
STA 4
STA 5

## Slide 5: Simulation 1- OFDMA Performance with number of active STAs
Parameters
  FFT size = 256
  OFDM symbol duration (16us)
  GI=3.2us
  MCS = 0 (SU PHY rate=7.0 Mbps)
  Channel B
  Bandwidth = 20MHz
  Number of Data Subcarriers = 224
  Number of Pilot Subcarriers = 16
  Scheduling algorithm – Maximum average power

## Slide 6: Results
#Active STAs= 4 x N
N (number of RBs) = 20MHz/RB Bandwidth
4 STAs
8 STAs
16 STAs
32 STAs
64 STAs
With 4N active STAs, there is a high chance of a STA exists with high power on a particular RB.
With RB bandwidth of 2.5MHz, the performance start to approach non fading BER performance.

## Slide 7: Results
2 STAs
4 STAs
8 STAs
16 STAs
32 STAs
N (number of RBs) = 20MHz/RB Bandwidth
#Active STAs= 2 x N
With 2N active STAs, there are less number of STAs per RB resulting in lower average performance compared to the 4N active STAs case.

## Slide 8: Results
#Active STAs= 1 x N
1 STA
2 STAs
4,8,16 STAs
N (number of RBs) = 20MHz/RB Bandwidth
With only N active STAs, the multi-user diversity is not enough to offset the loss of frequency diversity by transmitting in a sub 20MHz bandwidth. Each user effectively experience a flat fading channel.

## Slide 9: Issue when there are few STAs
If there are only a few active STAs (e.g. #Active STAs=< N), OFDMA may be detrimental because the multiuser diversity is not enough to offset the loss of frequency diversity.
Possible solutions
  Use single user OFDM
  Allocate a common strong RB to STA1 and STA 2. (Note: Interference cancellation in the receiver is needed)
STA 1
STA 2
half of the RBs are bad
subcarriers
allocated to STA 1 or 2
allocated to STA 2 or 1
Due to low number of STAs, any allocation configuration will result in bad performance in either STA

## Slide 10: Resource Block Sharing
Conventional OFDMA
OFDMA with RB Sharing
STA 1
STA 2
RB 1
RB 2
RB1 | RB2
STA1 | STA 2
STA 2 | STA 1
Possible Scheduling
RB1 | RB2
STA1 | STA 2
STA 2 | STA 1
STA 1, STA 2 | 
 | STA 1, STA 2
STA 1, STA 2 | STA 1, STA 2
Possible Scheduling
STA 1
STA 2
RB 2
RB 1

## Slide 11: Simulation 2
Parameters
  FFT size = 256
  OFDM symbol duration (16us)
  GI=3.2us
  MCS
    MCS 1 for 1 user SU (Total = 14 Mbps)
    MCS 1 for 2 user conventional OFDMA with RB BW=10MHz (Total =14 Mbps)
    MCS 0 for 2 user proposed with RB BW=20MHz (Total = 14 Mbps)
  Channel B
  Bandwidth = 20MHz
  Number of Data Subcarriers = 224
  Number of Pilot Subcarriers = 16

## Slide 12: Results
RB sharing with interference canceller result in good performance compared to Conv. OFDMA

## Slide 13: Conclusion
We showed some simulations showing the effect of the number of active STAs in UL MU performance.
With low number of STAs, the effect of low frequency diversity experience by the STA affect average BER performance.
We show that being able to use an RB already allotted to one user, the loss in frequency diversity can be reduced.

## Slide 14: Straw Poll
Do you agree that TGax should support a resource block sharing as defined in slide 10?
Y
N
A

## Slide 15: Reference
[1] 11-15-0132-02-00ax-spec-framework.doc