## Slide 1: Channel Sensing in UL-OFDMA
Date: 2015-03-09
Authors:
Name | Affiliations | Address | Phone | email
Reza Hedayat Young Hoon Kwon Yongho Seok Vida Ferdowsi | Newracom | 9008 Research Drive, Irvine, CA 92618 |  | reza.hedayat at newracom.com younghoon.kwon at newracom.com yongho.seok at newracom.com vida.ferdowsi at newracom.com
Reza Hedayat, NEWRACOM

## Slide 2: Summary
TGax SFD considers UL MU transmissions such as UL OFDMA and UL MU MIMO, which is expected to offer good medium utilization
Compared to existing SU and DL MU MIMO, UL OFDMA is unique due to multiple STAs participating in forming a single PPDU
This contribution focuses on channel sensing in presence of UL OFDMA frames

## Slide 3: SU vs UL MU Transmission
CSMA/CA is an important aspect in 802.11 operation, where all clients sense the medium and verify if the medium is busy/idle based on which they decide to access to access the medium
In SU transmission and DL MU transmission, since the frame is sent by a single node, it is straightforward how the neighboring nodes interpret the state of the medium
However, multiple clients participate in forming UL OFDMA PPDUs, hence the assessment of the status of the medium becomes tricky
The goal is that unintended neighboring STAs have accurate channel sensing regarding the ongoing PPDU on the entire BW

## Slide 4: Channel sensing in presence of UL OFDMA frames
802.11 offers several channel sensing mechanisms such as carrier sensing (CS), energy detect (ED), and virtual carrier sensing
However despite above mechanisms, operation of UL OFDMA might get affected by unintended BSS clients, or OBSS clients that start assessing the medium in the middle of an UL OFDMA PPDU
Depending on the sub-band assignment of an UL OFDMA PPDU, there could be ambiguity in channel sensing in the neighborhood of each of the clients participating in the UL OFDMA frame
The problem mostly comes from the fact that 802.11 clients assess availability of the medium based on 20MHz portions, while UL OFDMA assignments could be narrower and varying across the BSS coverage

## Slide 5: Channel sensing in presence of UL OFDMA frames
Channel sensing of single-transmitter transmission (SU and DL MU)
  All the nodes in the coverage area of the transmitter would have proper assessment of the medium status, using ED and CS mechanisms, even if they start assessing the medium in the middle of the frame
Channel sensing of UL OFDMA transmission
  A STA that participates in forming an UL OFDMA PPDU transmits no energy on some sub-bands, hence its coverage area varies across the bandwidth.
  For instance, it is possible that within part of the coverage area of an UL OFDMA STA the primary channel is sensed as idle during transmission of an UL OFDMA PPDU

## Slide 6: Partially-Hidden Nodes
STA1’s Sub-band
20 MHz
STA2’s Sub-band
20 MHz
STA1’s Sub-band
20 MHz
STA2’s Sub-band
20 MHz
STA1’s Sub-band
20 MHz
STA2’s Sub-band
20 MHz
Channel sensing in presence of UL OFDMA causes partially-hidden nodes
  For instance, in the case of a 40MHz UL OFDMA PPDU with two STAs (each assigned one 20MHz sub-channel) only the cross-coverage of the STAs sense the medium properly, and some of the neighborhood of each STA cannot sense that there is an ongoing frame on the whole 40MHz
  This is due to the fact that ED and CS mechanisms cannot detect presence of an UL-OFDMA PPDU on parts of 40MHz for the whole duration of the PPDU
AP
STA2
STA1

## Slide 7: Partially-Hidden Nodes
AP
STA1
STA2
STA3
STA4
AP
STA1
STA2
STA3
Partially-hidden nodes are not the same as hidden nodes:
  Hidden nodes are outside of the coverage of a frame that a STA sends
  Partially-hidden nodes are out of the coverage of part of the bandwidth of an UL OFDMA frame
  As a reference, for any frame where transmitter is a single node there is no partially-hidden node
  Using example of previous slide, below figures show the areas that partially-hidden nodes exist with 3 or 4 UL OFDMA nodes
Next slide shows some analysis of the probability of partially-hidden nodes when an UL OFDMA PPDU is formed by N=2, 3, 4 or 5 STAs

## Slide 8: Probability of Presence of Partially-Hidden Nodes
Percentage of partially-hidden nodes
Analysis assumptions:
  Transmit power =15dBm
  IEEE propagation loss model with exponent 2 up to 5m breakpoint, and exponent 3.5 thereafter is modeled
  Mean value for shadowing fading of lognormal (0dB,5dB) is used
Note: each plot shows the percentage of nodes within the cross-coverage of all UL OFDMA STAs vs the union of the coverage of all the STAs
Below analysis shows that for larger number of STAs participating in an UL OFDMA PPDU the chance that unintended clients appear as partially-hidden is large and increases with number of STAs in an UP OFDMA PPDU

## Slide 9: Conclusion
CSMA/CA is an important aspect of 802.11 operation that needs to be observed in presence of UL OFDMA frames
UL MU transmissions require additional considerations so that unintended nodes sense presence of UL MU PPDUs across the whole bandwidth of the frame and throughout the frame duration

## Slide 10: Straw Poll
Do you agree to add the following to 11ax SFD:
  “4.x.x TGax shall provide mechanisms that enable physical channel sensing (ED and CS) across the bandwidth and throughout the duration of an UL OFDMA frame.”