## Slide 1: Discussion on OFDMA Scheduling for 802.11ax
Date: 2015-03
Authors:

## Slide 2: Introduction
OFDMA multiuser transmission has been agreed as one of the most important features in 802.11ax.
We have agreed to use the 4x symbol length within symbols in 11ax [1].
  256-FFT for 20MHz
  512-FFT for 40MHz
  1024-FFT for 80MHz
For data payload, we consider following options for OFDMA resource allocation in 20/40/80MHz [2].
  nx26 tones
  mx242 tones
We start from BW<=20MHz and compare the allocation with following options from system performance point of view.
  Option1: w/o limitation on the resource allocation
    nx26 with n=1, 2, 3, 4, 5, 6, 7, 8 per STA for OFDMA
    mx242 with m=1 per STA for OFDM
  Option2: w/ limitation on the resource allocation [2]
    nx26 with n=1,2, 3 or 4 per STA for OFDMA
    mx242 with m=1 per STA for OFDM

## Slide 3: Scheduling in SLS (1/2)
OFDMA scheduling options in SLS
  Option 1: w/o limitation on nx26 with n=1…8 per STA for OFDMA and n=9 to approximate 1x242 for OFDM
    Flexible allocation to allow resources for large packets
     Short/compact transmission can reduce QoS delay
  Option 2: w/ limitation on nx26 with n=1, 2, 3 or 4 per STA for OFDMA and n=9 to approximate 1x242 for OFDM [2]
    Limited resources for large packets
    Long transmission time may increase QoS delay
#1
t
f
#2
#3
#4
#1
#3
t
f
#2
#1
#3
#4
frame
frame
frame
frame
Huawei Technologies Co. LTD.

## Slide 4: Scheduling in SLS (2/2)
Common assumption for Opt1 and Opt2
  Proportional fairness (PF) scheduling on each RU for user fairness
    PF(STAu, RUi) = EstimatedRate(STAu, SINR_RUi)/AverageRate(STAu)
  Channel-dependent scheduling to achieve frequency selective gain
    Only choose{RUi} to the STA with highest PF
  Contiguous frequency-domain allocation per STA
  Maximize time-domain allocation to improve the padding efficiency
    MinNumRU{Si[EstimatedRate(STAu, SINR_RUi)*NumSymbolsPerFrame]}
  Prioritize the allocation for the STA with remained data in previous frame
Huawei Technologies Co. LTD.

## Slide 5: Simulation Assumptions
Assumptions
  Bandwidth: 20MHz
  Scenario: SS2 enterprise; 32 APs, 2048STAs [3]
  Tx power: 20dBm@AP; 15dBm@STA
  Tx/Rx antenna: 2x2
  OFDMA with Nss=1-2 SU-MIMO
  Antenna gain: AP: 0dBi ;STA: -2dBi
  Channel CSI feedback: Ideal
  Simulation time/drop: 5s per drop/5 drops
  Max scheduled STA number in one frame: 20
  RTS/CTS for each cascading frame
  Traffic ratio for DL:UL is 1:1
  Frame length for data payload is 0.544ms with 40 symbols of 12.8us+0.8us GI [1]
  PHY preamble overhead is 10% [2]
BSS 9-12
BSS13-16
BSS 5-8
BSS 1-4
20 m
20 m
BSS 25-28
BSS 29-32
BSS 21-24
BSS 17-20
1
2
4
3
Huawei Technologies Co. LTD.

## Slide 6: Mixed Traffic and QoS requirement
In SS2, we use the following mixed types of traffic [4].
We have delay requirement for each type of traffic respectively [5].
Traffic name | Percent of STAs in Test Population (%) | Mean traffic size | Delay requirement
Buffered Video Streaming | 5% | min{application traffic of 13.9kbytes, AMPDU with 1.5kbytes*k} | 20ms
Video Conferencing | 10% |  | 
Virtual desktop infrastructure (VDI) | 100% | For UL: 50.6bytes | 
 |  | For DL: 41bytes of 70.57% and 1478.3 bytes of 32.43% | 
Voice (VoIP) | 15% | 36bytes if active 10bytes if silent | 10ms
Huawei Technologies Co. LTD.

## Slide 7: Throughput and Goodput Definition
System Throughput:
  S(Successful transmitted Packet bits)
  Observation_time
System Goodput:
  S(Successful transmitted Packet bits satisfying delay requirement)
  Observation_time
Huawei Technologies Co. LTD.

## Slide 8: Throughput and Goodput (Case1)
BW=20MHz | Opt1: w/o limitation on nx26 | Opt2: w/ limitation on nx26 | 
 | n=1,2,3,4,5,6,7,8,9 | n=1,2,3,9 | n=1,2,4,9
System throughput (Mbps) | 371.45 (0%) | 382.88 (+3.1%) | 368.54 (-0.8%)
System Goodput (Mbps) | 200.35 (0%) | 201.75 (+0.7%) | 195.73 (-2.3%)
Observation:
-For small packets with max size of 1.5kbytes, limitation on OFDMA scheduling has marginal impact on both system throughput and Goodput.
Case 1: MPDU with 1.5kbytes for Video
Huawei Technologies Co. LTD.

## Slide 9: RU Num per STA (Case1)
Ratio of RB # per user | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
Opt1: n=1,2,3,4,5,6,7,8,9 | 99.65% | 0.35% | 0% | 0% | 0% | 0% | 0% | 0% | 0%
Opt2: n=1,2,3,9 | 99.60% | 0.4% | 0% | 0% | 0% | 0% | 0% | 0% | 0%
Opt2: n=1,2,4,9 | 99.68% | 0.32% | 0% | 0% | 0% | 0% | 0% | 0% | 0%
Case 1: MPDU with 1.5kbytes for Video
Huawei Technologies Co. LTD.

## Slide 10: Throughput and Goodput (Case2)
BW=20MHz | Opt1: w/o limitation on nx26 | Opt2: w/ limitation on nx26 | 
 | n=1,2,3,4,5,6,7,8,9 | n=1,2,3,9 | n=1,2,4,9
System throughput (Mbps) | 298.14 (0%) | 294.82 (-1.1%) | 301.99 (+1.3%)
System Goodput (Mbps) | 233.26 (0%) | 145.87 (-37.46%) | 153.33 (-34.27%)
Observation:
-For large packets with max size of 6x1.5kbytes, limitation on OFDMA scheduling has marginal impact on system throughput but significant loss on Goodput.
Case 2: AMPDU with 6x1.5kbytes for Video
Huawei Technologies Co. LTD.

## Slide 11: RU Num per STA (Case2)
Ratio of RB # per user | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
Opt1: n=1,2,3,4,5,6,7,8,9 | 72.57% | 9.41% | 5.75% | 3.69% | 2.62% | 5.94% | 0.005% | 0% | 0%
Opt2: n=1,2,3,9 | 67.56% | 13.60% | 18.84% | 0% | 0% | 0% | 0% | 0% | 0%
Opt2: n=1,2,4,9 | 71.48% | 19.87% | 0% | 8.65% | 0% | 0% | 0% | 0% | 0%
Case 2: AMPDU with 1.5kbytes*6 for Video
Huawei Technologies Co. LTD.

## Slide 12: Throughput and Goodput (Case3)
BW=20MHz | Opt1: w/o limitation on nx26 | Opt2: w/ limitation on nx26 | 
 | n=1,2,3,4,5,6,7,8,9 | n=1,2,3,9 | n=1,2,4,9
System throughput (Mbps) | 301.04 (0%) | 283.28 (-5.9%) | 279.14 (-7.3%)
System Goodput (Mbps) | 151.14 (0%) | 96.73 (-36.0%) | 95.85 (-36.6%)
Observation:
-For large packets with max size of 9x1.5kbytes, limitation on OFDMA scheduling results in slight degradation on system throughput and significant loss on Goodput.
Case 3: AMPDU with 9x1.5kbytes for Video
Huawei Technologies Co. LTD.

## Slide 13: RU Num per STA (Case3)
Ratio of RB # per user | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
Opt1: n=1,2,3,4,5,6,7,8,9 | 69.17% | 10.95% | 7.63% | 4.94% | 3.17% | 1.99% | 1.26% | 0.67% | 0.23%
Opt2: n=1,2,3,9 | 66.36% | 12.18% | 21.46% | 0% | 0% | 0% | 0% | 0% | 0.03%
Opt2: n=1,2,4,9 | 70.71% | 18.54% | 0% | 10.75% | 0% | 0% | 0% | 0% | 0.01%
Case 3: AMPDU with 1.5kbytes*9 for Video
Huawei Technologies Co. LTD.

## Slide 14: Conclusion
  For 802.11ax, we preliminarily evaluated system-level throughput and goodput with various OFDMA resource allocation options within 20MHz.
  The results indicated that
    For traffic with small size, limitations of nxRU have marginal impact on system throughput as well as goodput.
    For traffic with large size, limitations of nxRU may have slight impact on system throughput but result in significant degradation on system goodput.
  Further discussion and evaluation is needed for OFDMA in 802.11ax.
Huawei Technologies Co. LTD.

## Slide 15: References
[1] 11-15-0099-04-11ax-Payload-symbol-size-for-11ax
[2] 11-15-0101-01-11ax-Preamble structure for 11ax system
[3] 11-15-0330-00-00ax-OFDMA numerology and structure
[4] 11-14-0874-00-00ax-unified-traffic-model-on-enterprise-scenario
[5] 11-13-0657-06-0 hew-sg-usage-models-and-requirements-liaison-with-again
Huawei Technologies Co. LTD.