## Slide 1: HE-STF Proposal
Date: 2015-03-09
Authors:
Name | Affiliation | Address | Phone | Email
Yakun Sun | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | yakunsun@marvell.com
 |  |  |  | hongyuan@marvell.com
Hongyuan Zhang |  |  |  | 
Lei Wang |  |  |  | Leileiw@marvell.com
Liwen Chu |  |  |  | liwenchu@marvell.com
Jinjing Jiang |  |  |  | jinjing@marvell.com
Yan Zhang |  |  |  | yzhang@marvell.com
Rui Cao |  |  |  | ruicao@marvell.com
Jie Huang |  |  |  | jiehuang@marvell.com
Sudhir Srinivasa |  |  |  | sudhirs@marvell.com
Saga Tamhane |  |  |  | sagar@marvell.com
Mao Yu |  |  |  | my@marvel..com
Edward Au |  |  |  | edwardau@marvell.com
Hui-Ling Lou |  |  |  | hlou@marvell.com

## Slide 2: Authors (continued)
Name | Affiliation | Address | Phone | Email
Ron Porat | Broadcom |  |  | rporat@broadcom.com
Matthew Fischer |  |  |  | mfischer@broadcom.com
Sriram Venkateswaran |  |  |  | 
Tu Nguyen |  |  |  | 
Vinko Erceg |  |  |  | 
Robert Stacey | Intel | 2111 NE 25th Ave, Hillsboro OR 97124, USA | +1-503-724-893 | robert.stacey@intel.com
Eldad Perahia |  |  |  | eldad.perahia@intel.com
Shahrnaz Azizi |  |  |  | shahrnaz.azizi@intel.com
Po-Kai Huang |  |  |  | po-kai.huang@intel.com
Qinghua Li |  |  |  | quinghua.li@intel.com
Xiaogang Chen |  |  |  | xiaogang.c.chen@intel.com
Chitto Ghosh |  |  |  | chittabrata.ghosh@intel.com
Rongzhen Yang |  |  |  | rongzhen.yang@intel.com
Laurent cariou |  |  |  | laurent.cariou@intel.com

## Slide 3: Authors (continued)
Name | Affiliation | Address | Phone | Email
Wookbong Lee | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | wookbong.lee@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Giwon Park |  |  |  | giwon.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Thomas Derham | Orange |  |  | thomas.derham@orange.com
Brian Hart | Cisco Systems | 170 W Tasman Dr, San Jose, CA 95134 |  | brianh@cisco.com
Pooya Monajemi |  |  |  | pmonajem@cisco.com
Joonsuk Kim | Apple |  |  | joonsuk@apple.com
Aon Mujtaba |  |  |  | mujtaba@apple.com
Guoqing Li |  |  |  | guoqing_li@apple.com
Eric Wong |  |  |  | ericwong@apple.com
Chris Hartman |  |  |  | chartman@apple.com

## Slide 4: Authors (continued)
Name | Affiliation | Address | Phone | Email
Fei Tong | Samsung | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434633 | f.tong@samsung.com
Hyunjeong Kang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-31-279-9028 | hyunjeong.kang@samsung.com
Kaushik Josiam |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7437 | k.josiam@samsung.com
Mark Rison |  | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434600 | m.rison@samsung.com
Rakesh Taori |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7470 | rakesh.taori@samsung.com
Sanghyun Chang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-10-8864-1751 | s29.chang@samsung.com
Yasushi Takatori | NTT | 1-1 Hikari-no-oka, Yokosuka, Kanagawa 239-0847 Japan |  | takatori.yasushi@lab.ntt.co.jp
Yasuhiko Inoue |  |  |  | inoue.yasuhiko@lab.ntt.co.jp
Yusuke Asai |  |  |  | asai.yusuke@lab.ntt.co.jp
Koichi Ishihara |  |  |  | ishihara.koichi@lab.ntt.co.jp
Akira Kishida |  |  |  | kishida.akira@lab.ntt.co.jp
Akira Yamada | NTT DOCOMO | 3-6, Hikarinooka, Yokosuka-shi, Kanagawa, 239-8536, Japan |  | yamadaakira@nttdocomo.com
Fujio Watanabe |  | 3240 Hillview Ave, Palo Alto, CA 94304 |  | watanabe@docomoinnovations.com
Haralabos Papadopoulos |  |  |  | hpapadopoulos@docomoinnovations.com

## Slide 5: Authors (continued)
Name | Affiliation | Address | Phone | Email
Phillip Barber | Huawei | The Lone Star State, TX |  | pbarber@broadbandmobiletech.com
Peter Loc |  |  |  | peterloc@iwirelesstech.com
Le Liu |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18601656691 | liule@huawei.com
Jun Luo |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | jun.l@huawei.com
Yi Luo |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18665891036 | Roy.luoyi@huawei.com
Yingpei Lin |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | linyingpei@huawei.com
Jiyong Pang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | pangjiyong@huawei.com
Zhigang Rong |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | zhigang.rong@huawei.com
Rob Sun |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Rob.Sun@huawei.com
David X. Yang |  | F1-17, Huawei Base, Bantian, Shenzhen |  | david.yangxun@huawei.com
Yunsong Yang |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | yangyunsong@huawei.com
Zhou Lan |  | F1-17, Huawei Base, Bantian, SHenzhen | +86-18565826350 | Lanzhou1@huawei.com
Junghoon Suh |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Junghoon.Suh@huawei.com
Jiayin Zhang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai | +86-18601656691 | zhangjiayin@huawei.com

## Slide 6: Authors (continued)
Name | Affiliation | Address | Phone | Email
Albert Van Zelst | Qualcomm | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | allert@qti.qualcomm.com
Alfred Asterjadhi |  | 5775 Morehouse Dr. San Diego, CA, USA |  | aasterja@qti.qualcomm.com
Bin Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | btian@qti.qualcomm.com
Carlos Aldana |  | 1700 Technology Drive San Jose, CA 95110, USA |  | caldana@qca.qualcomm.com
George Cherian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gcherian@qti.qualcomm.com
Gwendolyn Barriac |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gbarriac@qti.qualcomm.com
Hemanth Sampath |  | 5775 Morehouse Dr. San Diego, CA, USA |  | hsampath@qti.qualcomm.com
Menzo Wentink |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | mwentink@qti.qualcomm.com
Richard Van Nee |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | rvannee@qti.qualcomm.com
Rolf De Vegt |  | 1700 Technology Drive San Jose, CA 95110, USA |  | rolfv@qca.qualcomm.com
Sameer Vermani |  | 5775 Morehouse Dr. San Diego, CA, USA |  | svverman@qti.qualcomm.com
Simone Merlin |  | 5775 Morehouse Dr. San Diego, CA, USA |  | smerlin@qti.qualcomm.com
Tevfik Yucek |  | 1700 Technology Drive San Jose, CA 95110, USA |  | tyucek@qca.qualcomm.com
VK Jones |  | 1700 Technology Drive San Jose, CA 95110, USA |  | vkjones@qca.qualcomm.com
Youhan Kim |  | 1700 Technology Drive San Jose, CA 95110, USA |  | youhank@qca.qualcomm.com

## Slide 7: Authors (continued)
Name | Affiliation | Address | Phone | Email
James Yee | Mediatek | No. 1 Dusing 1st Road, Hsinchu, Taiwan | +886-3-567-0766 | james.yee@mediatek.com
Alan Jauh |  |  |  | alan.jauh@mediatek.com
Chingwa Hu |  |  |  | chinghwa.yu@mediatek.com
Frank Hsu |  |  |  | frank.hsu@mediatek.com
Thomas Pare | Mediatek USA | 2860 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | thomas.pare@mediatek.com
ChaoChun Wang |  |  |  | chaochun.wang@mediatek.com
James Wang |  |  |  | james.wang@mediatek.com
Jianhan Liu |  |  |  | Jianhan.Liu@mediatek.com
Tianyu Wu |  |  |  | tianyu.wu@mediatek.com
Russell Huang |  |  |  | russell.huang@mediatek.com
Bo Sun | ZTE | #9 Wuxing duan, Xifeng Rd, Xi’an, China |  | Sub.bo1@zte.com.cn
Kaiying Lv |  |  |  | lv.kaiying@zte.com.cn
Yonggang Fang |  |  |  | yfang@ztetx.com
Ke Yao |  |  |  | Yao.ke5@zte.com.cn
Weimin Xing |  |  |  | Xing.weimin@zte.com.cn

## Slide 8: Overview
11ax will adopt new PHY technologies:
  4x OFDM data symbol duration of 11ac has been agreed for 11ax.
    “Data symbols in an HE PPDU shall use a DFT period of 12.8 µs and subcarrier spacing of 78.125 kHz.” [1]
  Other ongoing discussions on OFDMA, UL-MU-MIMO, etc.
HE-STF design needs to address the new 11ax PHY.
  Provide reliable power measurement for new 11ax PHY and also high efficiency (low overhead).
  Also important to maintain periodical HE-STF signals to leverage existing 11ac receiver designs and reduce implementation costs.
In this contribution:
  Present different options for HE-STF
  Extensively simulated and analyzed different options, and
  Propose an HE-STF design.

## Slide 9
HE-STF Design Considerations

## Slide 10: Receiver AGC Assumptions
DL/UL-SU, DLMU:
  Operating the same way as 11ac, need to re-start AGC during HE-STF, especially when TxBF/DLMU is supported.
DL-OFDMA:
  A STA still operates in full-BW (20/40/80/160MHz ) front-end, even when its own tone allocation is smaller than 20MHz;
  Therefore AGC should be running in time domain for the full-BW signal to avoid clipping.
ULMU, UL-OFDMA:
  For example, AP triggers multiple STAs to transmit simultaneously in UL [2].
  AP receives signals from different STAs, and will operates the same way as 11ac and 11ax SU.
  Due to power control, signals from different STAs are expected with similar Rx power, beamforming effect might be smaller.
For all receivers,
  Set AGC with some headroom for PAPR
  Need to re-calculate DC offset compensation after AGC over HE-STF is done.

## Slide 11: HE-STF Periodicity
Option 1 (short): keep the legacy periodicity of 0.8us  16-tone sampling
Option 2 (mid): balance option 1&3, 8-tone sampling  1.6us periodicity
Option 3 (long): keep the legacy 4-tone sampling  period = 3.2us

## Slide 12: Number of HE-STF Periods
AGC design needs 5 periods for processing.
  AGC design includes multiple states of processing, such as coarse and fine gain steps, time for gain settling and DC offset estimation after gain settling.
  At least 5 periods are needed.
Keeping HE-STF of 5 periods as in 11ac allows chip vendors to reuse 11ac AGC design and receiver state machines.
For simplicity, use the same number of periods for both UL and DL PPDUs.

## Slide 13: HE-STF Tone Indices
HE-STF tones are desired to
  sample the full bandwidth universally (no holes or uncovered edge) for OFDMA.
  be placed to generate periodic HE-STF signals in time domain.
Hence, HE-STF tone indices will be

## Slide 14: Offset of HE-STF Tones
If HE-STF tones positions are not exactly multiple of NSTF_sample, the time domain signals are not periodical.
  Suppose the HE-STF position is shifted from Eq(1) by m tones, the corresponding time signal has a linear phase related to periodic HE-STF signals in Eq(1).
  The linear phase is not periodic, hence leads to aperiodic HE-STF time signals, as long as m is not equal to zero.
  Note that the amplitude of HE-STF is still periodic, but neither of real/imaginary part is.

## Slide 15: Example of Different Offset
Periodic for m=0
Aperiodic for m=2
Aperiodic for m=4
Aperiodic for m=8

## Slide 16: Performance of Aperiodic HE-STF Signals
Aperiodic HE-STF signals (offset = 8) degrade power measurement.
Using different period leads to different bias for aperiodic HE-STF; while periodic HE-STF performance is almost insensitive to the measuring window.
Aperiodic HE-STF signal leads to unnecessary DC offset.
  DC offset is measured by averaging time domain signal in an 0.8us window (either an exact period – ideal timing or an arbitrary 0.8us window – imperfect timing) and normalized by signal power per tone.
  In absence of DC offset, DC estimate based on aperiodic HE-STF signals is inaccurate and artificially introduces DC offset.
Periodic HE-STF (offset=0) is preferred for better performance.

## Slide 17: Example of HE-STF for 0.8us Periodicity
20MHz
  Assume guard/DC tone as [6 3 5]*
40MHz
  Assume guard/DC tone as [12 5 11]*
80MHz
  Assume guard/DC tone as [12 7 11]*
* For illustration only.

## Slide 18
Performance of HE-STF Periodicities

## Slide 19: Performance of Different Periodicity
Data:
  4x symbol duration + 0.8us CP
  HE-STF:
    Option 1: 0.8us periodicity for 4us symbol
    Option 2: 1.6us periodicity for 8us symbol
    Option 3: 3.2us periodicity for 16us symbol
    HE-STF tones assigned according to Equation (1) on slide 4.
  HE-LTF:
    Uncompressed
    Compressed (P-matrix based, Ng4) or uncompressed LTF, 0.8us CP [2]
  Legacy preambles are prepended.
  Power is collected only over 1 Rx antenna and over the 2nd HE-STF period.

## Slide 20: DL/UL-SU, DLMU: (1) 20MHz, D-NLOS, 1x1
SNR = 0dB
SNR = 30dB
Performance close to 11ac
Even for shortest HE-STF (0.8us), power bump within -1.5~1dB for both low and high SNR

## Slide 21: (2) Outdoor Channels – UMi-NLOS
Power bump still within -2 ~1.5dB and no worse than 11ac performance
SNR = 0dB
SNR = 30dB

## Slide 22: (3) Wider BW, 4Tx No TxBF
Power bump for 80MHz and 4Tx within a similar range as 20MHz 1Tx.
SNR = 30dB, Nss=1

## Slide 23: (4) TxBF
SNR = 30dB, Nss=2
SNR = 30dB, Nss=1
Power bump gap between 0.8us HE-STF and longer (1.6-3.2us) HE-STF is very small for TxBF in both indoor and outdoor channels.

## Slide 24: DL-OFDMA: (1) Narrowband Allocation
For each PPDU, schedule 56 best (contiguous) tones for STA1 in term of average SNR, and the rest tones for STA2
TxBF to each STA on the scheduled tones
STA1 measures HE-STF power over in time domain
The 2-user OFDMA transmission is very close to a general multi-user DL-OFDMA transmission to each individual receiver. (All unscheduled tones are randomly beamformed.)
Power bump gap between different periodicities is less than 0.5-1dB.

## Slide 25: (2) Different Sizes of Allocations
SNR = 30dB, Nss=2
Small range of power bump for OFDMA resource allocations (no allocation  narrow allocation  wide resource allocation  SU)
STA1 is allocated 14 tones on the edge and only beamformed over those tones.
STA1 is allocated half of all tones and only beamformed over those tones.
STA1 is not scheduled (each tone is beamformed to STA2, STA1 is an unintended receiver).

## Slide 26: (3) Insufficient Coverage
  DL-OFDMA + TxBF with STA1/STA2
STA1 transmit over 26 contiguous tones symmetrically across DC.
STA2 transmit over the rest tones.
TxBF to each STA on the allocated tones.
Artificially put 3 DC tones (so all HE-STF are beamformed to STA2)
STA1 always uses the center 26 tones  no beamformed HE-STF for STA1  worst scenario in DL-OFDMA.
Power bump performance is only 0.5dB between different HE-STFs.

## Slide 27: (4) Partial BW
Assume data tones are [-118:-2 2:118]. Split 20MHz into 9 blocks of 26-tone each.
Only a single allocation of 26/52/104 (except the center 26x1), the rest tones are unused.
  Corresponds to 11% to 44% BW usage  corner cases in DL-OFDMA.
0.8us HE-STF works well for DL-OFDMA even for partial BW usage.
  Typically has less than 1dB loss than 1.6us HE-STF.
  A little longer tail at 26x1 for UMi-NLOS less than 3%. For such a case, a low MCS may more likely be used, therefore the noise will be the dominant factor rather than AGC/ADC clipping.

## Slide 28: UL-OFDMA: (1) Narrowband Resource Allocations
  UL-OFDMA with 9 STAs
20MHz, UMi-NLOS
1 Tx, 1 Rx
Assume data tones are [-118:-2 2:118].
Split the data tones into 9 blocks of 26-tone each.
Each STA occupies 1 block, and transmits HE-STF tones within its allocated bandwidth.
The received power is roughly equal by each STA transmitting equal power and normalizing its channel.
0.8us HE-STF shows 0.8dB loss at 10% and 1.2dB loss at 1% comparing 1.6us HE-STF.

## Slide 29: (2) Variable Bandwidth Allocation
  UL-OFDMA with up to 9 STAs
20MHz, UMi-NLOS
1 Tx, 1 Rx
Assume data tones are [-118:-2 2:118], and split into 9 26-tone blocks.
Each user can be scheduled with n blocks, n=1…4
Each UL transmission with a variable bandwidth allocations.
  Each STA occupies a random valid number of blocks.
  All tones are allocated.
  Number of STAs in each UL transmission varies.
Gap between 0.8us and 1.6us HE-STF becomes smaller over variable bandwidth allocations.

## Slide 30: (3) Single Narrowband Allocation
  UL-OFDMA with a single STA1
STA1 randomly transmit over 26 contiguous tones; No STA2.
STA1 transmits HE-STF tones within its allocated bandwidth.
  Power bump of 0.8us LTF for the worst scenario (single narrowband) UL-OFDMA has a longer tail.

## Slide 31: (4) Impact on Timing and Power Offset
Users in UL-OFDMA inevitably have different timing offsets.
  From synchronization error and round-trip delay.
UL power control will not lead to equal received power from all users.
  Due to imperfect/intentional power control.
HE-STF of 1.6us periodicity is much more robust to the timing and power offset in UL-OFDMA than HE-STF of 0.8us periodicity.
  UL-OFDMA with 9 STAs
20MHz, UMi-NLOS
1 Tx, 1 Rx
Split the data tones into 9 blocks of 26-tone each, and each STA occupies 1 block.
Random power offset of each user in [-5, 5]dB.
Random timing offset of each user in [0, 0.8us] relative to user 1.

## Slide 32: Discussions on UL-MU Transmissions
Power measurement is more challenging in UL-MU (OFDMA/MU-MIMO) PPDUs.
  Users in UL-MU transmissions have different timing, resulting in effective longer channel delay spread.
    HE-STF of longer duration to protect from ISI from larger time offset spread among different STAs and better cover frequency selectivity.
  Imperfect or intentional UL power control leads to unequal received power from each user.
    0.8us period (16-tone sampling) STF results in 1 STF tone in certain user’s UL signals and less reliable power measurements than 1.6us period STF.
1.6us HE-STF improve the performance of 0.8us HE-STF for UL-OFDMA
  More reliable in NB allocation (remove long tail from 0.8us HE-STF), and more robust to timing/power offset.

## Slide 33: Discussions on HE-STF Periodicity in Different HE PPDU
All DL PPDUs and UL-SU PPDUs: prefer 0.8us HE-STF
  performs fine with the highest efficiency.
UL-MU PPDUs: prefer 1.6us HE-STF
  Improve performance and reliability
    More robust to timing/power offset and NB allocation
  Little sacrifice on efficiency
    No much overhead using longer HE-STF (additional 4us) in trigger-based frame with potentially less SIG symbols.
    No need to signal HE-STF periodicity.
Propose to use 0.8us HE-STF for a non-trigger-based PPDU (DL, and UL-SU), and 1.6us HE-STF for a trigger-based PPDU (UL-MUMIMO/OFDMA).

## Slide 34: Compressed LTF
No TxBF, UMi-NLOS,
SNR=30dB, Nss=1
DL-OFDMA 56 tones, D-NLOS,
SNR=30dB, Nss=2
Compressed LTF has been proposed in [3], with a different symbol duration as 4x data symbols.
Assume 4x compression (1x LTF symbol duration).
Power ratio between compressed LTF and 0.8us/1.6us HE-STF is close that of 4x data symbols.

## Slide 35: PER Performance Based on 0.8us HE-STF
2-STA DL-OFDMA setup (STA1 with 56 contiguous tones, STA2 with the rest tones).
PER for STA1 only (of 8000 bits)
AGC set by power measurement over the 2nd period of HE-STF, 10bit ADC
0.8us HE-STF leads to almost no performance degradation comparing to no AGC/ADC
MCS9
MCS9
MCS7
MCS4

## Slide 36: Summary
By extensive simulations we compared three (long, median, and short) HE-STF designs in different channels and signal types.
Short HE-STF of 0.8us periodicity performs close to 11ac STF, as well as 1.6us/3.2us periodicity in DL, and provides lowest overhead.
Median HE-STF of 1.6us periodicity provides additional performance improvement and reliability in UL-MU PPDUs.
It is also proposed to keep 5 periods of HE-STF signals to leverage the 11ac design (AGC, receiver state machine, etc).
The best solution is to use
  5 periods of 0.8us HE-STF for non-trigger based PPDUs (DL PPDUs, UL-SU PPDUs)
  5 periods of 1.6us HE-STF for trigger-based PPDUs (UL-MUMIMO/UL-OFDMA PPDUs)

## Slide 37: SP #1
Do you support the HE-STF of a non-trigger-based PPDU has a periodicity of 0.8 µs with 5 periods?
  A non-trigger-based PPDU is not sent in response to a trigger frame
Yes
No
Abs

## Slide 38: SP #2
Do you support the HE-STF of a trigger-based PPDU has a periodicity of 1.6 µs with 5 periods?
  A trigger-based PPDU is an UL PPDU sent in response to a trigger frame
Yes
No
Abs

## Slide 39: SP #3
Do you support the HE-STF tone positions are defined in Equation 1 where NSTF_sample = 16 for a non-trigger-based PPDU and NSTF_sample = 8 for a trigger-based PPDU?
Yes
No
Abs

## Slide 40: Reference
[1] 11-15-0132-02-00ax-spec-framework
[2] 11-15-0365-00-00ax-ul-mu-procedure
[3] 11-15-0349-00-00ax-HE-LTF-proposal