## Slide 1: MAC Calibration Test 4
Date: 2015-Mar-05
Authors:

## Slide 2: Multichannel MAC Calibration (Test 4)
The goal of test4 is to check whether STAs (AP1 and STA1 which is served by AP1) respect EDCA channel access rule and can properly choose the transmission bandwidth for each of its packets (RTS, CTS, Data, ACK).

## Slide 3: MAC calibration test 4
AP1 sends traffic to STA1 on a 40MHz channel with a full buffer continuously.
AP2 sends traffic to STA2 on a 20MHz channel starting at t1, which is located at the secondary channel of BSS1.
  The traffic is based on the Poisson distribution
STA 1
AP 2
AP1
STA 2
(AP1 and STA2 are essentially co-located)

## Slide 4: MAC Parameters
EDCA and basic MAC parameters
Parameter | Value
RTS/CTS | OFF, ON
MCS | 0
MSDU length (bytes) | 2000
MPDU limit | 2
CWmin | 15
CWmax | 1023
AIFSN | 2
AIFS (us) | 34
Max number of retries | 10
PIFS (us) | 25

## Slide 5: Assumption on A-MPDU
The A-MPDU setting is MPDU limit =2. (according to “All other setting is the same as test case 2a.” [1])
MAC transmitter fetches PPDUs from buffer after the successful transmission of last data packet (ACK received) or CTS received.

## Slide 6: Assumption on A-MPDU (Conti.)
Since AP2 has non-full-buffer traffic, there may be either 1 or 2 MPDUs in each PPDU.

## Slide 7: Backoff behavior with RTS/CTS exchanges
CTS timeout happens after aSIFSTime + aSlotTime + aRxPHYStartDelay.
Try random backoff after CTS timeout.
  The next RTS start time is aSIFSTime + aSlotTime + aRxPHYStartDelay +AIFS+aSlotTime*random slot number

## Slide 8: The duration of PPDU
The duration of PPDU varies with the transmit channel bandwidth and the number of MPDUs within it.
PPDU duration with different AMPDU numbers and 20/40MHz BW (unit: us) |  |  |  | 
 |  |  | BW=20MHz | BW=40MHz
RTS |  |  | 52 | 52
CTS |  |  | 44 | 44
Data | CBR | (AMPDU_num=1)* |  | 1248
 |  | AMPDU_num=2 | 5056 | 2456
 | Poisson | AMPDU_num=1 | 2548 | 
 |  | AMPDU_num=2 | 5056 | 
ACK |  |  | 68 | 68
*The A-MPDU size is always 2 for full buffer CBR STA.

## Slide 9: Simulation Results
AP2’s MAC Tput approaches its non-full-buffer traffic rate.
 |  |  |  | Precentage of Tx Time |  | 
 |  | BW mode | MAC Tput (Mbps) | 20MHz | 40MHz | APP Tput (Mbps)
RTS off | BSS1: AP1->STA1 | 20/40MHz Adaptive | 8.99 | 48.32% | 51.68% | 8.83
 | BSS2: AP2->STA2 | 20MHz Fixed | 1.59 | 100.00% | 0.00% | 1.56
RTS on | BSS1: AP1->STA1 | 20/40MHz Adaptive | 8.69 | 51.71% | 48.29% | 8.53
 | BSS2: AP2->STA2 | 20MHz Fixed | 1.59 | 100.00% | 0.00% | 1.56

## Slide 10: Conclusions
In the scenario of test 4, AP1 in RTS-disable case achieves slightly higher throughput than in RTS-enable case.
Further assumptions on RTS/CTS transmission and the required outputs shall be provided in SSD[1] to help every participant get the calibration results aligned.
Next step, to check the performance of multi-channel in system simulation scenarios (Residential, Enterprise, etc.)

## Slide 11: References
[1] 11-14-0980-06-00ax-simulation-scenarios.docx

## Slide 12: Appendix
 |  |  |  | Num of 20MHz Data PPDU |  | Num of 40MHz Data PPDU |  | Tx Time (s) |  | Precentage of Tx Time* |  |  | 
 |  | BW mode | MAC Tput (Mbps) | Tx | Num of Rx | Num of Tx | Num of Rx | 20MHz | 40MHz | 20MHz | 40MHz |  | APP Tput (Mbps)
RTS off | BSS1: AP1->STA1 | 20/40MHz Adaptive | 8.99 | 1838 | 1837 | 3996 | 3833 | 9.4178 | 10.0736 | 48.32% | 51.68% |  | 8.83
 | BSS2: AP2->STA2 | 20MHz Fixed | 1.59 | 1999 | 1835 | NA | NA | 5.6797 |  | 100.00% | 0.00% |  | 1.56
 | Packet loss |  | 0.00 |  | 164 |  | 163 |  |  |  |  |  | 0.00
 | PER |  |  |  |  |  | 2.794% |  |  |  |  |  | 
RTS on | BSS1: AP1->STA1 | 20/40MHz Adaptive | 8.69 | 1988 | 1987 | 3566 | 3566 | 10.0138 | 9.3503 | 51.71% | 48.29% |  | 8.53
 | BSS2: AP2->STA2 | 20MHz Fixed | 1.59 | 1890 | 1889 |  |  | 5.4264 |  | 100.00% | 0.00% |  | 1.56
*Tx Time includes RTS, CTS, DATA and ACK time