## Slide 1: NGP Use Case Template
Date: 2015-03-09
Authors:

## Slide 2: Abstract
This document is a proposed template to describe use cases, and some location requirements per use case, for Next Generation Positioning
In this initial version, only one sample use case is included. Additional use cases are expected to be added in future versions of this document
Location requirements are included with each use case to drive focus for the study group
The goal is to come up with a superset of everything potentially needed and then narrow down the field from there on

## Slide 3: Terminology
  User – The end entity (human) who would use this technology
  Use case – A use case is task oriented. It describes the specific step by step actions performed by a user or device. One use case example is a user starting and stopping a video stream.
  Environment – The type of place in which a network is deployed, such as home, outdoor, hot spot, enterprise, metropolitan area, etc.
    Frequency bands of interest (FBoI): The 802.11 operating frequency bands relevant to this use case. Eg. for a shopping mall’s enterprise wireless it will be 2.4GHz and 5GHz
    AP density: Density of AP deployment, e.g. APs deployed every 4000 sq.ft.
    AP height: Height, above the floor, at which the APs are deployed, e.g. for shopping mall APs deployed approximately 15-25 ft above the floor
Key Location Requirement-
    Expected Horizontal Accuracy: XY accuracy expected for the use case to succeed, <1m@90% is a requirement is that the computed location be within 1m horizontally of the actual location 90% of the time
    Expected Vertical Accuracy: Z accuracy expected for the use case to succeed, “same floor@99%” is a requirement is that the computed location be on the same floor as the actual location 99% of the time. “0.5m@90%” is a requirement is that the computed location be within 0.5m vertically of the actual location 90% of the time
    Expected Latency: Expected time taken to complete a single atomic location process. The location process begins with initiating a location request, then computing location, and ends with returning the computed location. E.g. 10 ms latency would indicate that it takes 10 ms after the request is transmitted to gather measurements, compute a location, and transfer any parameters such that the requester has a location within 10 ms.
    Expected Refresh Rate: This defines how frequently is the computation expected when client moving. E.g. a refresh rate of 10 locations per second would indicate that location needs to be refreshed 10 times in a second
    Expected number of simultaneous users

## Slide 4: 1. Micro location in store
User: Person with a smartphone which has the store app installed
Environment: A store has APs for 802.11 coverage. The store may have APs at the store entrance. The expected AP density is about 1 AP per 4000 sq. ft. with APs supporting HT, VHT and NGP
Use case:
  The user enters the store with their phone
  As soon as user enters, the phone notifies the user about the store promotions
  The user can query details about a product on the app
  The app and smartphone can then help the user navigate to the particular shelf containing the product
  The user stands in queue and as they reaches the checkout counter, their loyalty number is brought up on the system
Expected:
  Horizontal accuracy: <0.5 m@90%, vertical accuracy: same floor@99%
  Latency: <500ms
  Refresh Rate: > 1 location/sec

## Slide 5: References
11-07-2988-04-0000-liaison-from-wi-fi-alliance-to-802-11-regarding-wfa-vht-study-group-consolidation-of-usage-models.ppt
11-14-1464-02-0wng-ng-positioning-overview-and-chalanges.pptx