## Slide 1: Corrections to TGah Channel Model
Date: 2015-03-12
Authors:

## Slide 2: Context
Document IEEE 802.11-11/0968r3 [1] provides TGah outdoor and indoor channel models
  Based on 3GPP/3GPP2 spatial channel model (SCM) and TGn (MIMO) channel models.
Particularly, TGah indoor path loss model is modelled by directly scaling down the frequency operation of the TGn model [2]
Recently, a few academic research papers have been published which use TGah Channel Model as a reference

## Slide 3: The error
According to TGn [2], path loss is given by:
TGah indoor path loss model [1] uses eqs. (1) and (2):
LFS(d) d ≤ dBP
L(d) =
LFS(dBP) + 35 log10(d / dBP) d > dBP
LFS is the free space loss eq. (slope of 2)
LFS(d) d ≤ dBP
L(d) =
LFS(d) + 35 log10(d / dBP) d > dBP

## Slide 4: The error
LFS(d) d ≤ dBP
L(d) =
LFS(dBP) + 35 log10(d / dBP) d > dBP
LFS is the free space loss eq. (slope of 2)
TYPO: Applies losses from dBP twice!
According to TGn [2], path loss is given by:
TGah indoor path loss model [1] uses eqs. (1) and (2):
LFS(d) d ≤ dBP
L(d) =
LFS(d) + 35 log10(d / dBP) d > dBP

## Slide 5: The error
~40dB difference at 500m (dBP = 5m)
~25dB difference at 500m (dBP = 30m)

## Slide 6: Proposed changes to TGah Channel Model
Replace LFS(d) with LFS(dBP) in eq. (2)
Replace LFS(d) with LFS(dBP) in eq. (3)
Update date and revision number

## Slide 7: References
“TGah Channel Model – Proposed Text”, IEEE 802.11-11/0968r3
“TGn Channel Models”, IEEE 802.11-03/940r4